## Slide 1: OpenFabrics Interfaces: Past, present, and future
Sean Hefty
[ April 5th, 2016 ]
OFIWG Co-Chair

## Slide 2
Optimized SW path to HW
  Minimize cache and memory footprint
  Reduce instruction count
  Minimize memory accesses
Scalable
Implementation Agnostic
OFIWG: develop … interfaces aligned with … application needs
Software interfaces aligned with application requirements
  Careful analysis of requirement
Expand open source community
  Inclusive development effort
  App and HW developers
Good impedance match with multiple fabric hardware
  InfiniBand*, iWarp, RoCE, Ethernet, UDP offload, Intel®, Cray*, IBM*, others
Open Source
Application-Centric
libfabric
* Other names and brands may be claimed as the property of others

## Slide 3: OFI application Requirements
Give us a high-level interface!
Give us a low-level interface!
MPI developers
OFI strives to meet both requirements

## Slide 4: OFI Software Development strategies
One Size Does Not Fit All
Fabric Services
Application
OFI
Provider
Application
OFI
Provider
Provider optimizes for OFI features
Common optimization for all apps/providers
App uses OFI features
Application
OFI
Provider
App optimizes based on supported features
Provider supports low-level features only

## Slide 5: OFI Development status
Fabric Services
Application
libfabric
Provider
Provider optimizes for OFI features
Common optimization for all apps/providers
Provider supports low-level features only
Many apps
Few apps
Provider’s choice
App optimizes based on supported features
App uses OFI features
OFI-provider gap

## Slide 6: OFI libfabric community
libfabric
Because of the OFI-provider gap, not all apps work with all providers
Intel® MPI Library
MPICH Netmod/CH4
Open MPI
MTL/BTL
Open MPI
SHMEM
Sandia SHMEM
GASNet
Clang UPC
rsockets
ES-API
libfabric Enabled Middleware
Control Services
Communication Services
Completion Services
Data Transfer Services
Discovery
fi_info
Connection Management
Address Vectors
Event Queues
Event Counters
Message Queue
Tag Matching
RMA
Atomics
Sockets
TCP, UDP
Verbs
Cisco usNIC
Intel
OPA, PSM
Cray
GNI
Mellanox MXM
IBM Blue Gene
A3Cube RONNIE
*
*
*
*
*
®
experimental
supported
*
* Other names and brands may be claimed as the property of others

## Slide 7: libfabric scalability
By Courtesy Argonne* National Laboratory, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=24653857
Developed to evaluate the Aurora software stack at scale and assist applications in the transition from Mira to Aurora
Native provider implementation that directly uses the Blue Gene/Q hardware and network interfaces for communication
* Other names and brands may be claimed as the property of others

## Slide 8: libfabric scalability
IBM MPICH / PAMI
  IBM XL C compiler for BG, v12.1
  Optimized for single-threaded latency
  …/comm/xl.legacy.ndebug/bin/mpicc
  v1r2m2
MPICH / CH4 / libfabric
  gcc 4.4.7
  global locks, inline, direct, etc.
  Provider not optimized for performance
PAMI
MPICH
PAMID
hardware
BG/Q Provider
libfabric
MPICH
CH4 OFI
Completely subjective software stack comparison
vs
32 nodes on ALCF Vesta machine
PAMI and libfabric performance

## Slide 9: libfabric scalability
Chart: Bytes
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576
IBM | 2.07 | 2.13 | 2.16 | 2.17 | 2.12 | 2.13 | 2.24 | 2.29 | 3.8 | 4 | 3.7 | 4.06 | 4.93 | 6.49 | 10.45 | 15.19 | 24.35 | 42.84 | 79.61 | 153.43 | 300.81 | 595.89
OFI | 1.78 | 1.85 | 1.84 | 1.84 | 1.84 | 2.2 | 2.15 | 2.1 | 2.45 | 2.74 | 3.05 | 4.52 | 4.88 | 5.78 | 8.12 | 13.21 | 22.23 | 40.29 | 76.38 | 148.58 | 292.95 | 581.72
OSU* MPI Performance Tests v5.0
Chart: Bytes
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576
IBM | 0.93 | 1.84 | 3.63 | 7.42 | 15.03 | 28.68 | 56.9 | 66.61 | 130.87 | 226.96 | 454.02 | 878.11 | 1213.38 | 1601.68 | 1684.39 | 1729.9 | 1753.66 | 1765.58 | 1771.68 | 1774.72 | 1776.25
OFI | 0.91 | 1.82 | 3.63 | 7.26 | 14.59 | 29.31 | 58.72 | 117.57 | 227.71 | 456.12 | 904.56 | 1521.1 | 1687.89 | 1754.71 | 1785.57 | 1800.6 | 1808.04 | 1811.82 | 1813.7 | 1814.66 | 1815.13
Chart: Bytes
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576 | 2097152
IBM | 14928727.15 | 14711620.17 | 14379388.82 | 14848487.81 | 15086677.03 | 14405244 | 14070204.32 | 7458017.48 | 7342526.54 | 7116750.69 | 7115592.68 | 6820139.4 | 4729703.62 | 3120339.28 | 1643291.12 | 844106.55 | 427968.57 | 215486.29 | 108123.42 | 54157.62 | 27102.72 | 13557.37
OFI | 14552397.44 | 14604385.76 | 14555448.96 | 14546175.09 | 14602616.83 | 14637453.32 | 14701177.2 | 14728905.64 | 14315305.06 | 14325869.47 | 14119531.36 | 11915487.61 | 6593560.94 | 3426737.07 | 1743412.41 | 879082.7 | 441398.77 | 221165.16 | 110698.81 | 55378.58 | 27696.66 | 13849.99
MPI scale out testing:
cpi – 1M ranks,
ISx benchmark – 0.5M ranks
Tests document performance of components on a particular test, in specific systems. Differences in hardware, software, or configuration will affect actual performance. Consult other sources of information to evaluate performance as you consider your purchase. For more complete information about performance and benchmark results, visit http://www.intel.com/performance.
* Other names and brands may be claimed as the property of others
Notes: Mira system at Argonne- 32 nodes on ALCF Vesta machine
BlueGene/Q, Power BQC 16C 1.60GHz, Linux
IBM MPICH / PAMI
  IBM XL C compiler for BG, v12.1
  Optimized for single-threaded latency
  …/comm/xl.legacy.ndebug/bin/mpicc
  v1r2m2
MPICH / CH4 / libfabric
  gcc 4.4.7
  global locks, inline, direct, etc.
  Provider not optimized for performance

## Slide 10: Addressing the ofi-provider gap
Libfabric Framework
libfabric API
Components
templates, lists, rbtree, hash table, free pool, ring buffer, stack, …
Base Class Implementations
fabric, domain, EQ, wait sets, AV, CQ, … SHM primitives
Provider Services
Logging
Environment variables
Utility Provider
Core Provider
Interface ‘extensions’ – for consistency
Assist in provider development
Enhance core provider

## Slide 11: Utility provider
 |  | Core Provider |  |  |  | Utility Provider |  | 
 |  | DGRAM | MSG | RDM |  | DGRAM | MSG | RDM
Interfaces | Msg |  |  |  |  |  |  | 
 | Tagged |  |  |  |  |  |  | 
 | RMA |  |  |  |  |  |  | 
 | Atomic |  |  |  |  |  |  | 
Capabilities | Scalable EP |  |  |  |  |  |  | 
 | Shared RX |  |  |  |  |  |  | 
 | Shared TX |  |  |  |  |  |  | 
 | Multicast |  |  |  |  |  |  | 
 | FI_MULTI_RECV |  |  |  |  |  |  | 
 | FI_REMOTE_CQ_DATA |  |  |  |  |  |  | 
 | FI_INJECT |  |  |  |  |  |  | 
 | FI_RMA_EVENT |  |  |  |  |  |  | 
 | FI_SOURCE |  |  |  |  |  |  | 
 | FI_DIRECTED_RECV |  |  |  |  |  |  | 
Attributes | FI_MR_BASIC |  |  |  |  |  |  | 
 | FI_MR_SCALABLE |  |  |  |  |  |  | 
Modes | FI_CONTEXT |  |  |  |  |  |  | 
 | FI_LOCAL_MR |  |  |  |  |  |  | 
 | FI_MSG_PREFIX |  |  |  |  |  |  | 
 | FI_ASYNC_IOV |  |  |  |  |  |  | 
 | FI_RX_CQ_DATA |  |  |  |  |  |  | 
Minimal functionality
Optional functionality
Requested application modes
Optional application modes
Layered over simpler core endpoints
Caps
Attrs
Modes
Interface
Core Provider
Utility Provider
Performance is a primary objective
E.g. RDM over DGRAM

## Slide 12: moving forward
Beyond HPC
Enterprise, Cloud, Storage (NVM)
Stronger engagement with these communities
Beyond Linux*
Sockets – TCP/UDP
NetworkDirect
Analyze requests to expand OFI community
* Other names and brands may be claimed as the property of others

## Slide 13: target schedule
Driven by implementation feedback
Improve error handling, flow control
Better support for non-traditional fabrics
Optimize completion handling
Address deferred features
2016
Q2
Q3
Q4
2017
Q2
Q3
Q4
RDM over DGRAM Util
RDM over MSG Util
Shared Memory
New Core Providers
ABI 1.1
Utility provider is ongoing
Traditional and non-traditional RDMA providers

## Slide 14: Summary
OFIWG development model working well
Interest in OFI and libfabric is high
Growing community
Significant effort being made to simplify the lives of developers
  Applications and providers
OFI is so good

## Slide 15: Legal Disclaimer & Optimization Notice
No license (express or implied, by estoppel or otherwise) to any intellectual property rights is granted by this document. Intel disclaims all express and implied warranties, including without limitation, the implied warranties of merchantability, fitness for a particular purpose, and non-infringement, as well as any warranty arising from course of performance, course of dealing, or usage in trade. This document contains information on products, services and/or processes in development. All information provided here is subject to change without notice. Contact your Intel representative to obtain the latest forecast, schedule, specifications and roadmaps. The products and services described may contain defects or errors known as errata which may cause deviations from published specifications. Current characterized errata are available on request.
Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products.
Copyright © 2016, Intel Corporation. All rights reserved. Intel, Pentium, Xeon, Xeon Phi, Core, VTune, Cilk, and the Intel logo are trademarks of Intel Corporation in the U.S. and other countries.
*Other names and brands may be claimed as the property of others
Optimization Notice
Intel’s compilers may or may not optimize to the same degree for non-Intel microprocessors for optimizations that are not unique to Intel microprocessors. These optimizations include SSE2, SSE3, and SSSE3 instruction sets and other optimizations. Intel does not guarantee the availability, functionality, or effectiveness of any optimization on microprocessors not manufactured by Intel. Microprocessor-dependent optimizations in this product are intended for use with Intel microprocessors. Certain optimizations not specific to Intel microarchitecture are reserved for Intel microprocessors. Please refer to the applicable product User and Reference Guides for more information regarding the specific instruction sets covered by this notice. Notice revision #20110804

## Slide 16: THANK YOU
Sean Hefty
OFIWG Co-Chair