## Slide 1: Open Fabrics Interfaces Architecture Introduction
Sean Hefty
Intel Corporation

## Slide 2: Current State of Affairs
OFED SW was not designed around HPC
Hardware and fabric features are changing
  Divergence is driving competing APIs
Interfaces are being extended, and new APIs introduced
  Long delay in adoption
Size of clusters and single node core counts greatly increasing
More applications are wanting to take advantage of high-performance fabrics
OFED software
Widely adopted low-level RDMA API
Ships with upstream Linux
but…

## Slide 3: Solution
Design software interfaces that are aligned with application requirements
Evolve OpenFabrics
Target needs of HPC
Support multiple interface semantics
Fabric and vendor agnostic
Supportable in upstream Linux

## Slide 4: Enabling through OpenFabrics
Leveraging existing open source community
Broad ecosystem
  Application developers and vendors
  Active community engagement
Drive high-performance software APIs
  Take advantage of available hardware features
  Support multiple product generations
Open Fabrics Interfaces Working Group

## Slide 5: OFIWG Charter
Develop an extensible, open source framework and interfaces aligned with ULP and application needs for high-performance fabric services
Software leading hardware
  Enable future hardware features
  Minimal impact to applications
Minimize impedance match between ULPs and network APIs
Craft optimal APIs
  Detailed analysis on MPI, SHMEM, and other PGAS languages
  Focus on other applications – storage, databases, …

## Slide 6: Call for Participation
OFI WG is open participation
  Contact the ofiwg mail list for meeting details
  ofiwg@lists.openfabrics.org
Source code available through github
  github.com/ofiwg
Presentations / meeting minutes available from OFA download directory
Help OFI WG understand workload requirements and drive software design

## Slide 7: Enable..
Optimized software path to hardware
  Independent of hardware interface, version, features
Scalability
High performance
App-centric
Extensible
Reduced cache and memory footprint
  Scalable address resolution and storage
  Tight data structures
Analyze application needs
  Implement them in a coherent, concise, high-performance manner
More agile development
  Time-boxed, iterative development
  Application focused APIs
  Adaptable

## Slide 8: Verbs Semantic Mismatch
Allocate WR
Allocate SGE
Format SGE – 3 writes
Format WR – 6 writes
Loop 1
Checks – 9 branches Loop 2
Check
Loop 3
Checks – 3 branches
Checks – 3 branches
Direct call – 3 writes
Checks – 2 branches
50-60 lines of C-code
25-30 lines of C-code
generic send call
optimized send call
Reduce setup cost - Tighter data
Eliminate loops and branches - Remaining branches predictable
Selective optimization paths to HW - Manual function expansion
Current RDMA APIs
Evolved Fabric Interfaces

## Slide 9: Application-Centric Interfaces
Collect application requirements
Identify common, fast path usage models
  Too many use cases to optimize them all
Build primitives around fabric services
  Not device specific interface
Reducing instruction count requires a better application impedance match

## Slide 10: OFA Software Evolution
libfabric
FI Provider
IB Verbs
Verbs Provider
Verbs
Fabric Interfaces
Transition from disjoint APIs
to a cohesive set of fabric interfaces
RDMA CM
CM
uVerbs Command

## Slide 11: Fabric Interfaces Framework
Take growth into consideration
Reduce effort to incorporate new application features
  Addition of new interfaces, structures, or fields
  Modification of existing functions
Allow time to design new interfaces correctly
  Support prototyping interfaces prior to integration
Focus on longer-lived interfaces – software leading hardware

## Slide 12: Fabric Interfaces
Fabric Interfaces
Message Queue
Control
Interface
RMA
Atomics
Addressing Services
Tag Matching
Triggered Operations
CM Services
Fabric Provider Implementation
Message Queue
CM Services
RMA
Tag Matching
Control Interface
Framework defines multiple interfaces
Vendors provide optimized implementations
Addressing Services
Atomics
Triggered Operations

## Slide 13: Fabric Interfaces
Defines philosophy for interfaces and extensions
  Focus interfaces on the semantics and services offered by the hardware and not the hardware implementation
Exports a minimal API
  Control interface
Defines fabric interfaces
  API sets for specific functionality
Defines core object model
  Object-oriented design, but C-interfaces

## Slide 14: Fabric Interfaces Architecture
Interfaces
Endpoint
Active
Passive
Events
Queues
Counters
Address Vector
Maps
Tables
Domain
Shared Resources
Memory Descriptors
Fabric
Topology Data
(Virtual) NIC
Based on object-oriented programming concepts
Derived objects define interfaces
  New interfaces exposed
  Define behavior of inherited interfaces
  Optimize implementation

## Slide 15: Control Interfaces
fi_getinfo
Application specifies desired functionality
Identify resources and addressing
fi_fabric
Open a set of fabric interfaces and resources
fi_register
Dynamic providers publish control interfaces
Discover fabric providers and services
FI Framework
fi_getinfo
fi_fabric
fi_register

## Slide 16: Application Semantics
Progress
  Application or hardware driven
  Data versus control interfaces
Ordering
  Message ordering
  Data delivery order
Multi-threading and locking model
  Compile and run-time options
Get / set using control interfaces

## Slide 17: Fabric Object Model
Fabric
Fabric Interfaces
NIC
Physical Fabric
NIC
NIC
Resource Domain
Resource Domain
Event Queue
Event Counter
Active Endpoint
Address Vectors
Event Queue
Event Counter
Active Endpoint
Address Vectors
Passive Endpoint
Event Queue
Boundary of resource sharing
Provider abstracts multiple NICs
Software objects usable across multiple HW providers

## Slide 18: Endpoint Interfaces
Type
Protocol
CM
Message Transfers
RMA
Tagged
Atomics
Triggered
Properties
Interfaces
Endpoint
Communication interfaces
Software path to hardware optimized based on endpoint properties
Capabilities
Message Transfers
RMA
Tagged
Atomics
Triggered
Aliasing supports multiple software paths to hardware

## Slide 19: Application Configured Interfaces
lg. msg
RMA
NIC
Message Queue Ops
RMA Ops
Endpoint
Communication type
Data transfer flags
Capabilities
sm. msg
inline send
send
write
read
Provider directs app to best API sets
App specifies comm model

## Slide 20: Event Queues
Format
Wait Object
Context only
Data
Tagged
Generic
None
fd
mwait
Properties
Interface Details
Event Queues
Asynchronous event reporting
User specified wait object
Compact optimized data structures
Optimize interface around reporting successful operations
Domain
Event counters support lightweight event reporting

## Slide 21: Event Queues
read CQ
optimized CQ
Generic completion
Op context
Send: +4-6 writes, +2 branches
Recv: +10-13 writes, +4 branches
+1 write, +0 branches
App selects completion structure
Generic verbs completion example
Application optimized completion

## Slide 22: Address Vectors
Store addresses/host names
- Insert range of addresses with single call
Start Range | End Range | Base LID | SL
host10 | host1000 | 50 | 1
host1001 | host4999 | 2000 | 2
Share between processes
Enable provider optimization techniques
- Greatly reduce storage requirements
Reference entries by handle or index
- Handle may be encoded fabric address
Reference vector for group communication
Example only
Fabric specific addressing requirements

## Slide 23: Summary
These concepts are necessary, not revolutionary
  Communication addressing, optimized data transfers, app-centric interfaces, future looking
Want a solution where the pieces fit tightly together

## Slide 24: Repeated Call for Participation
Co-chair (sean.hefty@intel.com)
  Meets Tuesdays from 9-10 PST / 12-1 EST
Links
  Mailing list subscription
    http://lists.openfabrics.org/mailman/listinfo/ofiwg
  Document downloads
    https://www.openfabrics.org/downloads/OFIWG/
  libfabric source tree
    www.github.com/ofiwg/libfabric
  labfabric sample programs
    www.github.com/ofiwg/fabtests

## Slide 25: Backup

## Slide 26: Verbs API Mismatch
struct ibv_sge {
uint64_t addr;
uint32_t length;
uint32_t lkey;
};
struct ibv_send_wr {
uint64_t wr_id;
struct ibv_send_wr *next;
struct ibv_sge *sg_list;
int num_sge;
enum ibv_wr_opcode opcode;
int send_flags;
uint32_t imm_data;
...
};
Application request
<buffer, length, context>
3 x 8 = 24 bytes of data needed
SGE + WR = 88 bytes allocated
Requests may be linked - next must be set to NULL
Must link to separate SGL and initialize count
App must set and provider must switch on opcode
Must clear flags
28 additional bytes initialized
Significant SW overhead

## Slide 27: Verbs Provider Mismatch
For each work request
Check for available queue space
Check SGL size
Check valid opcode
Check flags x 2
Check specific opcode
Switch on QP type
Switch on opcode
Check flags
For each SGE
Check size
Loop over length
Check flags
Check
Check for last request
Other checks x 3
19+ branches including loops
100+ lines of C code 50-60 lines of code to HW
Most often 1 (overlap operations)
Often 1 or 2 (fixed in source)
Artifact of API
QP type usually fixed in source
Flags may be fixed or app may have taken branches

## Slide 28: Verbs Completions Mismatch
struct ibv_wc {
uint64_t wr_id;
enum ibv_wc_status status;
enum ibv_wc_opcode opcode;
uint32_t vendor_err;
uint32_t byte_len;
uint32_t imm_data;
uint32_t qp_num;
uint32_t src_qp;
int wc_flags;
uint16_t pkey_index;
uint16_t slid;
uint8_t sl;
uint8_t dlid_path_bits;
};
Application accessed fields
Provider must fill out all fields, even those ignored by the app
Developer must determine if fields apply to their QP
App must check both return code and status to determine if a request completed successfully
Single structure is 48 bytes likely to cross cacheline boundary
Provider must handle all types of completions from any QP

## Slide 29: RDMA CM Mismatch
struct rdma_route {
struct rdma_addr addr;
struct ibv_sa_path_rec *path_rec;
...
};
struct rdma_cm_id {...};
rdma_create_id()
rdma_resolve_addr()
rdma_resolve_route()
rdma_connect()
Src/dst addresses stored per endpoint
456 bytes per endpoint
Path record per endpoint
Resolve single address and path at a time
All to all connected model for best performance
Want: reliable data transfers, zero copies to thousands of processes
RDMA interfaces expose:

## Slide 30: Progress
Ability of the underlying implementation to complete processing of an asynchronous request
Need to consider ALL asynchronous requests
  Connections, address resolution, data transfers, event processing, completions, etc.
HW/SW mix
All(?) current solutions require significant software components

## Slide 31: Progress
Support two progress models
  Automatic and implicit
Separate operations as belonging to one of two progress domains
  Data or control
  Report progress model for each domain
SAMPLE | Implicit | Automatic
Data | Software | Hardware offload
Control | Software | Kernel services

## Slide 32: Automatic Progress
Implies hardware offload model
  Or standard kernel services / threads for control operations
Once an operation is initiated, it will complete without further user intervention or calls into the API
Automatic progress meets implicit model by definition

## Slide 33: Implicit Progress
Implies significant software component
Occurs when reading or waiting on EQ(s)
Application can use separate EQs for control and data
Progress limited to objects associated with selected EQ(s)
App can request automatic progress
  E.g. app wants to wait on native wait object
  Implies provider allocated threading

## Slide 34: Ordering
Applies to a single initiator endpoint performing data transfers to one target endpoint over the same data flow
  Data flow may be a conceptual QoS level or path through the network
Separate ordering domains
  Completions, message, data
Fenced ordering may be obtained using fi_sync operation

## Slide 35: Completion Ordering
Order in which operation completions are reported relative to their submission
Unordered or ordered
  No defined requirement for ordered completions
Default: unordered

## Slide 36: Message Ordering
Order in which message (transport) headers are processed
  I.e. whether transport message are received in or out of order
Determined by selection of ordering bits
  [Read | Write | Send] After [Read | Write | Send]
  RAR, RAW, RAS, WAR, WAW, WAS, SAR, SAW, SAS
Example:
  fi_order = 0 // unordered
  fi_order = RAR | RAW | RAS | WAW | WAS | SAW | SAS // IB/iWarp like ordering

## Slide 37: Data Ordering
Delivery order of transport data into target memory
  Ordering per byte-addressable location
  I.e. access to the same byte in memory
Ordering constrained by message ordering rules
  Must at least have message ordering first

## Slide 38: Data Ordering
Ordering limited to message order size
  E.g. MTU
  In order data delivery if transfer <= message order size
  WAW, RAW, WAR sizes?
Message order size = 0
  No data ordering
Message order size = -1
  All data ordered

## Slide 39: Other Ordering Rules
Ordering to different target endpoints not defined
Per message ordering semantics implemented using different data flows
  Data flows may be less flexible, but easier to optimize for
  Endpoint aliases may be configured to use different data flows

## Slide 40: Multi-threading and Locking
Support both thread safe and lockless models
  Compile time and run time support
  Run-time limited to compiled support
Lockless (based on MPI model)
  Single – single-threaded app
  Funneled – only 1 thread calls into interfaces
  Serialized – only 1 thread at a time calls into interfaces
Thread safe
  Multiple – multi-threaded app, with no restrictions

## Slide 41: Buffering
Support both application and network buffering
  Zero-copy for high-performance
  Network buffering for ease of use
    Buffering in local memory or NIC
  In some case, buffered transfers may be higher-performing (e.g. “inline”)
Registration option for local NIC access
  Migration to fabric managed registration
Required registration for remote access
  Specify permissions

## Slide 42: Scalable Transfer Interfaces
Application optimized code paths based on usage model
Optimize call(s) for single work request
  Single data buffer
  Still support more complex WR lists/SGL
Per endpoint send/receive operations
  Separate RMA function calls
Pre-configure data transfer flags
  Known before post request
  Select software path through provider