## Slide 1: MPI Requirements of the Network Layer OFA 2.0 Mapping
MPI community feedback assembled
by Jeff Squyres, Cisco Systems
Sean Hefty, Intel Corporation

## Slide 2: Basic things MPI needs
Messages (not streams)
  msg and tagged message APIs
Efficient API
  Allow for low latency / high bandwidth
  Low number of instructions in the critical path
    Direct access to provider
    Calls associated with objects (endpoints, event queues)
    Provider can dynamically adjust function pointers based on object configuration
  Enable “zero copy”
    Depends on provider implementation and HW support

## Slide 3: Basic things MPI needs
Separation of local action initiation and completion
  Data transfers are asynchronous
One-sided (including atomics) and two-sided semantics
  One-sided support – RMA and atomics
  Two-sided – msg and tagged messags
No requirement for communication buffer alignment
  Atomics must be naturally aligned based on their type

## Slide 4: Basic things MPI needs
Asynchronous progress independent of API calls
  Including asynchronous progress from multiple consumers (e.g., MPI and PGAS in the same process)
  Preferably via dedicated hardware
Process
MPI
PGAS
libfabric handles
libfabric handles
Progress
of these
Also causes
progress
of these
Document as provider implementation requirement within a single instantiation
Progress support is exposed by provider, but proposed API needs refining
Notes: Added “ability for multiple consumer async progress” sub-bullet (from feedback in slide 35)

## Slide 5: Basic things MPI needs
Scalable communications with millions of peers
  With both one-sided and two-sided semantics
  Think of MPI as a fully-connected model
    (even though it usually isn’t implemented that way)
  Today, runs with 3 million MPI processes in a job
Move from ‘QP’ to ‘endpoint’ interface
  Endpoint may consist of multiple send/receive queues
  Endpoint type includes ‘reliable datagram message’
Introduce ‘address vector’
  Enable bulk address resolution
  Reduce memory required to address remote nodes
  Share vector among multiple processes
Notes: Added “both 1-sided and 2-sided” to scalability point in this slide (Vs. in a later slide)

## Slide 6: Things MPI likes in verbs
(all the basic needs from previous slide)
Different modes of communication
  Reliable vs. unreliable
  Scalable connectionless communications (i.e., UD)
Endpoint exposes generic type, protocol capabilities (e.g. RDMA support), and low-level protocol
  Support vendor/provider specific protocols
  HW and SW protocols
Notes: Feedback from MPI community:
We like RDMA write with immediate… but 4 bytes isn’t enough
Re-state last bullet better: want completion on peer for an RDMA write

## Slide 7: Things MPI likes in verbs
Specify peer read/write address (i.e., RDMA)
  RMA operations supported
RDMA write with immediate (*)
  …but we want more (more on this later)
  RMA with immediate supported
  API increase immediate to 64-bit
  Could use SGL for arbitrary immediate data size
    E.g. First or last SGE provides immediate data
Notes: Feedback from MPI community:
We like RDMA write with immediate… but 4 bytes isn’t enough
Re-state last bullet better: want completion on peer for an RDMA write

## Slide 8: Things MPI likes in verbs
Ability to re-use (short/inline) buffers immediately
  FI_BUFFERED_SEND flag
  May be implemented as inline data or copied to pre-registered memory
Polling and OS-native/fd-based blocking QP modes
  Support for multiple wait objects with control interface to obtain native wait object (e.g. fd)
Notes: Replaced “inline messages” with “ability to re-use buffer immediately”

## Slide 9: Things MPI likes in verbs
Discover devices, ports, and their capabilities (*)
  …but let’s not tie this to a specific hardware model
Discovery is built around fi_getinfo call
  Need to determine if interface is sufficient
Fabric and domain objects
  Higher-level of abstraction than verbs
  Need to identify application desired attributes
Notes: Replaced “inline messages” with “ability to re-use buffer immediately”

## Slide 10: Things MPI likes in verbs
Scatter / gather lists for sends
  Supported via IOV format
    struct iovec, struct fi_iomv
  Extensible to other IOV formats (not defined)
    E.g. strided operations,
Atomic operations (*)
  …but we want more (more on this later)
  Define a complete set of atomic operations
    8-64 bit ints, float, double, complex, etc.
    min, max, sum, prod, and, or, swap, etc.
  Query mechanism to determine provider support
Notes: Replaced “inline messages” with “ability to re-use buffer immediately”

## Slide 11: Things MPI likes in verbs
Can have multiple consumers in a single process
  API handles are independent of each other
Support multiple providers
Process
Network hardware
Library A
Library B
Handle A
Handle B
Notes: Replaced “MPI + PGAS” example with “API handles are independent of each other”
Split off into its own slide

## Slide 12: Things MPI likes in verbs
Ability to connect to “unrelated” peers
  Active/passive endpoints
  CM operations (connect, listen, accept)
Cannot access peer (memory) without permission
  Protection keys exposed (as 64-bits)
  Memory registration required for RMA target memory
Notes: Translated “Multiple PDs per process” to “ability to connect to ‘unrelated’ peers”
Per feedback on slide 32, add point about being able to block (without consuming CPU, even though that’s not actually specified by verbs)

## Slide 13: Things MPI likes in verbs
Ability to block while waiting for completion
  ...assumedly without consuming host CPU cycles
  User specifies wait object and signaling type
  fi_ec_wait_obj, fi_ec_wait_cond
Cleans up everything upon process termination
  E.g., kernel and hardware resources are released
  Linux kernel requirement
Notes: Translated “Multiple PDs per process” to “ability to connect to ‘unrelated’ peers”
Per feedback on slide 32, add point about being able to block (without consuming CPU, even though that’s not actually specified by verbs)

## Slide 14: Other things MPI wants (described as verbs improvements)
MTU is an int (not an enum)
  TBD – will be an int
  Currently exposed through control interface
Specify timeouts to connection requests
  Design is to use administrative interface for timeout
    E.g. /etc/rdma/fabric/def_conn_timeout
    Control interface may be use to override defaults
  Kernel support for very long timeouts (e.g. MRA)
  …or have a CM that completes connections asynchronously
    Application intervention to configure connected endpoints is desirable for performance reasons

## Slide 15: Other things MPI wants (described as verbs improvements)
All operations need to be non-blocking, including:
  Address handle creation
    Address vector operation is asynchronous
  Communication setup / teardown
    CM operations are asynchronous
  Memory registration / deregistration
    Asynchronous registration
    Deregistration is lazy, but may be forced to complete using sync operation

## Slide 16: Other things MPI wants (described as verbs improvements)
Specify buffer/length as function parameters
  Specified as struct requires extra memory accesses
  …more on this later
  Data transfer operations include calls that take the buffer/length as parameters
Ability to query how many credits currently available in a QP
  To support actions that consume more than one credit
  TBD
    will START/END flags work? reserve queue/credits?
  Application can track credits
  Which level should operation queuing occur?

## Slide 17: Other things MPI wants (described as verbs improvements)
Remove concept of “queue pair”
  Have standalone send channels and receive channels
  Defines endpoint, with send and/or receive capabilities
  Association between send and receive channels needed for connection-oriented communication
  Endpoint has data transfer ‘flows’
    Flow could map to a different queue or priority level

## Slide 18: Other things MPI wants (described as verbs improvements)
Completion at target for an RDMA write
  fid_mr – memory regions have operations
  MR may be associated with an event queue
  Supports event generation against MRs
Have ability to query if loopback communication is supported
  clarify
  Anticipate that loopback support will be a requirement for the provider
Notes: After MPI community feedback:
- Added 1st bullet as reaction to feedback from slide 13

## Slide 19: Other things MPI wants (described as verbs improvements)
Clearly delineate what functionality must be supported vs. what is optional
  Example: MPI provides (almost) the same functionality everywhere, regardless of hardware / platform
  Verbs functionality is wildly different for each provider
  First cut at provider requirements documented
  TBD – support dynamically determining what optional functionality is provided
  fi_getinfo – app requests desired functionality, and provider only responds when met
Notes: After MPI community feedback:
- Added 1st bullet as reaction to feedback from slide 13

## Slide 20: Other things MPI wants (described as verbs improvements)
Better ability to determine causes of errors
In verbs:
  Different providers have different (proprietary) interpretations of various error codes
  Difficult to find out why ibv_post_send() or ibv_poll_cq() failed, for example
Perhaps a better strerr() type of functionality (that can also obtain provider-specific strings)?
fi_errno – extended error code values (errno+)
fi_ec_err_entry: prov_errno, prov_data
EC strerror() operation – provider specific
Notes: This is a new slide from after the MPI community feedback webex

## Slide 21: Other things MPI wants: Standardized high-level interfaces
Examples:
  Tag matching
    tag matching operations
  MPI non-blocking collective operations (TBD)
    TBD
    Idea for triggered operations
  Remote atomic operations
    atomic operations defined
  …etc.
  The MPI community wants input in the design of these interfaces
    APIs will be fully documented (man pages) and reviewed
Notes: MPI community feedback:
- Separate distinction between vendor-specific optimization exposure vs. common functionality that should be standardized (e.g., tag matching should be standardized)
This is a new slide that specifically mentions the common high-level interfaces
I added the ability to run-time query which interfaces are available (e.g., for providers who do not want to provide these high-level interfaces)
Torsten also mentioned that it would be good to specifically call out non-blocking for the collectives support
The next slide is now (pretty much) the original slide that talks about low-level vendor-specific functionality

## Slide 22: Other things MPI wants: Standardized high-level interfaces
Divided opinions from MPI community:
  Providers must support these interfaces, even if emulated
    Enable provider support, but cannot require it
      Market demand must push vendors
    Support for proprietary protocols allows for SW implementations
      Exposed to apps for interoperability
      Framework can provide common implementation
        E.g. tag matching over message queues, MR cache
  Run-time query to see which interfaces are supported
    protocol_cap identifies supported interfaces
Notes: MPI community feedback:
- Separate distinction between vendor-specific optimization exposure vs. common functionality that should be standardized (e.g., tag matching should be standardized)
This is a new slide that specifically mentions the common high-level interfaces
I added the ability to run-time query which interfaces are available (e.g., for providers who do not want to provide these high-level interfaces)
Torsten also mentioned that it would be good to specifically call out non-blocking for the collectives support
The next slide is now (pretty much) the original slide that talks about low-level vendor-specific functionality

## Slide 23: Other things MPI wants: Vendor-specific interfaces
Direct access to vendor-specific features
  Lowest-common denominator API is not always enough
  Allow all providers to extend all parts of the API
    Provider specific operations supported
    Provider reserved data values (enums, flags, etc.)
Implies:
  Robust API to query what devices and providers are available at run-time (and their various versions, etc.)
  Compile-time conventions and protections to allow for safe non-portable codes
    FI_DIRECT allows building against a specific provider
    #define capability flags to support compile time optimizations
This is a radical difference from verbs
Notes: MPI community feedback:
- Separate distinction between vendor-specific optimization exposure vs. common functionality that should be standardized (e.g., tag matching should be standardized)
This slide is pretty much the same as it was; the standardization of common interfaces is now a separate slide (the one before this one)

## Slide 24: Core libfabric functionality
Application (e.g., MPI)
libfabric core
Provider A
Provider B
Direct function
calls to libfabric

## Slide 25: Example options for direct access to vendor-specific functionality
Application (e.g., MPI)
libfabric core
Provider A
Provider B
Provider A extensions
Example 1:
Access to
provider A
extensions
without going
through libfabric
core

## Slide 26: Example options for direct access to vendor-specific functionality
Application (e.g., MPI)
libfabric core
Provider A
Provider B with extensions
Example 2:
Access to provider B
extensions via “pass
through” functionality
in libfabric
Applications have direct access to providers for all calls but small group of core calls (fi_getinfo, fi_fabric)
No common path through core
Core provides helper functions that providers may use

## Slide 27: Other things MPI wants: Regarding memory registration
Run-time query: is memory registration is necessary?
  I.e., explicit or implicit memory registration
  capability flag
  Captured in IOV format
If explicit
  Need robust notification of involuntary memory de-registration (e.g., munmap)
  TBD – not defined
  Supports events on a MR
If the cost of de/registration were “free”, much of this debate would go away 
  Enable provider to hide registration (cache, on-demand)
Notes: MPI community feedback:
- Fix first bullet with: memory reg may not be necessary
- Here’s what we want out of mr: 1) decouple registration and pinning. 2) here’s what we’re going to do in MPI
- Different requirements: whether mr is implict or explicit (depends on OS, too)
- Perhaps choose which to use at runtime? (explicit or implicit)
- There are two different camps in the MPI community 
- If cost of reg/dereg was “free”, much of this debate goes away
I separated memory registration out into its own slide

## Slide 28: Other things MPI wants: Regarding fork() behavior
In child:
  All memory is accessible (no side effects)
  Network handles are stale / unusable
  Can re-initialize network API (i.e., get new handles)
In parent:
  All memory is accessible
  Network layer is still fully usable
  Independent of child process effects
TBD – any effect on API?
Notes: MPI community feedback:
After fork in child: be able to re-init network layer
slab: instead, say amount of receive buffering used directly related to incoming message
I split fork into its own slide

## Slide 29: Other things MPI wants
If network header knowledge is required:
  Provide a run-time query
    Header is determined by endpoint protocol
  Do not mandate a specific network header
  E.g., incoming verbs datagrams require a GRH header
GRH will be hidden by default
  IB routing does not exist
  Provider can direct to discard buffer
  Use setopt function to expose GRH
TBD – exposing source address is non-trivial
  May require lookups, (IB source data is incomplete)
Notes: MPI community feedback:
Datagram bullet is redundant with prior slide
Last bullet seems redundant with prior slide, too
Ordering: potentially on a per-message basis? (e.g., send/recv ordered and RDMA unordered)
Changed “query for datagram payload offset” to be an example
I added sub-bullet about ordered vs. unordered
Last bullet (completions for remote write) is not redundant; I left it

## Slide 30: Other things MPI wants
Request ordered vs. unordered delivery
  Potentially by traffic type (e.g., send/receive vs. RDMA)
  Endpoint type defines some ordering requirements
  TBD – ordering is defined by protocol
    Need generic ordering requirements or controls
Completions on both sides of a remote write
  MR may be bound to event queues
Notes: MPI community feedback:
Datagram bullet is redundant with prior slide
Last bullet seems redundant with prior slide, too
Ordering: potentially on a per-message basis? (e.g., send/recv ordered and RDMA unordered)
Changed “query for datagram payload offset” to be an example
I added sub-bullet about ordered vs. unordered
Last bullet (completions for remote write) is not redundant; I left it

## Slide 31: Other things MPI wants
Allow listeners to request a specific network address
  Similar to TCP sockets asking for a specific port
  fi_getinfo:src_addr allows specifying transport and/or network address
  Support for multiple address formats (IP, IPv6, IB)
Allow receiver providers to consume buffering directly related to the size of incoming messages
  Example: “slab” buffering schemes
  FI_MULTI_RECV flag indicates that a posted buffer may be used to receive multiple messages
  fi_ec_data_entry:buf can support this
  Buffer is released when next receive does not fit or fully consumed (free space drops beneath some threshold)
Notes: MPI community feedback:
slab: instead, say amount of receive buffering used directly related to incoming message
Changed 2nd bullet / sub-bullet to be in the form of a requirement, and just used “slab” as an example

## Slide 32: Other things MPI wants
Generic completion types. Example:
  Aggregate completions
    FI_EC_COUNTER – event counter type
  Vendor-specific events
    fi_ec_format – provider specific event formats available
Out-of-band messaging
  TDB – clarify, URGENT data?
  fi_msg:flow – endpoints may be associated with multiple data flows, selectable by the user
Notes: MPI community feedback:
Little confusing that I mention vendor specified again here
Scalable: point is that MPI is a fully connected model. Support it however you want. Today we run on M’s of processes.
I didn’t find the vendor-specific events confusing…?
I moved the “scalable to millions of peers” up to slide 12

## Slide 33: Other things MPI wants
Noncontiguous sends, receives, and RDMA opns.
  fi_iov_format – extensible to other formats
Page size irrelevance
  Send / receive from memory, regardless of page size
  Page size not exposed
  Provider may have alignment restrictions
    FI_MULTI_RECV?
  TBD – expose other size restrictions
    packet limits, operation limits (RMA, MR)
Notes: MPI Community feedback:
Hints to device about power? (e.g., MPI knows I’m not going to do anything for a while… but it doesn’t) And network power hints may not be valuable over time…?
On prior slide: have efficient mechanism to block in libfabric calls (e.g., poll hard in lower layer, sleep for a while, …etc.)
There was later consensus that power hints are not likely useful, particularly regarding the network device(s)

## Slide 34: Other things MPI wants
Access to underlying performance counters
  For MPI implementers and MPI-3 “MPI_T” tools
  TBD – only control interface defined
  Need to identify desired counters
    Per endpoint? per device? user or kernel service (file)?
Set / get network quality of service
  TBD – endpoint getopt/setopt operations
  QoS / ToS not defined
Notes: MPI Community feedback:
Hints to device about power? (e.g., MPI knows I’m not going to do anything for a while… but it doesn’t) And network power hints may not be valuable over time…?
On prior slide: have efficient mechanism to block in libfabric calls (e.g., poll hard in lower layer, sleep for a while, …etc.)
There was later consensus that power hints are not likely useful, particularly regarding the network device(s)

## Slide 35: Other things MPI wants: More atomic operations
Datatypes (minimum): int64_t, uint64_t, int32_t, uint32_t
  Would be great: all C types (to include double complex)
  Would be ok: all <stdint.h> types
  Don’t require more than natural C alignment
  fi_datatype - all types defined
Notes: Per Jeff Hammond:
Add [u]int32_t
Add <stdint.h> types
…

## Slide 36: Other things MPI wants: More atomic operations
Operations (minimum)
  accumulate, fetch-and-accumulate, swap, compare-and-swap
Accumulate operators (minimum)
  add, subtract, or, xor, and, min, max
fi_op – large set of operators defined
  Provider can convert fi_datatype / fi_op using lookup table
Run-time query: are these atomics coherent with the host?
  If support both, have ability to request one or the other
  FI_WRITE_COHERENT flag with fi_ep_sync() if not
Notes: Per Jeff Hammond:
Add [u]int32_t
Add <stdint.h> types
…

## Slide 37: Other things MPI wants: MPI RMA requirements
Offset-based communication (not address-based)
  Performance improvement: potentially reduces cache misses associated with offset-to-address lookup
  TBD – support user selected fabric address (~riomap)
  Modify or extend MR operations
Programmatic support to discover if VA based RMA performs worse/better than offset based
  Both models could be available in the API
  But not required to be supported simultaneously
  TBD - clarify
  Provider could support multiple APIs, which may not perform equally
  Intent is for provider to return fi_info in order of preference
    fi_info may need capability mask
Notes: This is a new slide from the MPI Forum RMA WG

## Slide 38: Other things MPI wants: MPI RMA requirements
Aggregate completions for MPI Put/Get operations
  Per endpoint
  Per memory region
Event counters may be associated with endpoints and MR’s (and other fabric objects)
Notes: This is a new slide from the MPI Forum RMA WG

## Slide 39: Other things MPI wants: MPI RMA requirements
Ability to specify remote keys when registering
  Improves MPI collective memory window allocation scalability
  MR operation – FI_USER_MR_KEY cap flag
Ability to specify arbitrary-sized atomic ops
  Run-time query supported size
  Supports common data type sizes, and arrays of those sizes
  Query support for a given size and array count
Notes: This is a new slide from the MPI Forum RMA WG

## Slide 40: Other things MPI wants: MPI RMA requirements
Ability to specify/query ordering and ordering limits of atomics
  Ordering mode: rar, raw, war and waw
  Example: “rar” – reads after reads are ordered
  Protocol defines ordering
  TBD – document ordering between operations (message queue, RMA, atomics, etc.)
  TBD – abstract ordering above low-level protocol
Notes: This is a new slide from the MPI Forum RMA WG

## Slide 41: “New,” but becoming important
Network topology discovery and awareness
  …but this is (somewhat) a New Thing
  Not much commonality across MPI implementations
Would be nice to see some aspect of libfabric provide fabric topology and other/meta information
  Need read-only access for regular users
TBD – fabric object class could expose operations regarding topology
  Need to define operations and structures
  Rely on extensibility of framework
Notes: Added: need read-only access for regular users (vs. IB, which requires root access)

## Slide 42: API design considerations
With no tag matching, MPI frequently sends / receives two buffers
  (header + payload)
  Optimize for that
  TBD – modify or extend API sets
    Need details on buffer usage (e.g. FI_BUFFERED_SEND for header buffer)
MPI sometimes needs thread safety, sometimes not
  May need both in a single process
  TBD – compile time option
    Run time configuration option to disable synchronization
Notes: MPI community feedback:
Data point: if we provide a tag matching, then everyone should provide it even if you have to emulate it (this is two opinions)
Expose OOB capabilities from the network
I moved the tag matching data point up to slide 21
Moved OOB capabilities point up to slide 31

## Slide 43: API design considerations
Support for checkpoint/restart is desirable
  Make it safe to close stale handles, reclaim resources
  TBD – determine if this is an API requirement
    Provider documented requirement to cleanup user space resources even if kernel fails (key errno?)
  Forcing apps to close all handles prior to checking is highly undesirable
Notes: MPI community feedback:
Data point: if we provide a tag matching, then everyone should provide it even if you have to emulate it (this is two opinions)
Expose OOB capabilities from the network
I moved the tag matching data point up to slide 21
Moved OOB capabilities point up to slide 31

## Slide 44: API design considerations
Do not assume:
  Max size of any transfer (e.g., inline)
  The memory translation unit is in network hardware
  All communication buffers are in main RAM
  Onload / offload, but allow for both
  API handles refer to unique hardware resources
TBD – determine API requirements
Notes: MPI community feedback:
We need async progress (from the perspective of MPI looking down). MPI-3 demands it.
Pair this with multiple consumers of the interface both being able to have “async progress” from a single place (E.g., MPI and PGAS playing nicely together)
Failures: well-defined a way to reclaim resources from that layer and below
Both async progress points now listed as a “need” in slide 11
Added point about reclaiming resources

## Slide 45: API design considerations
Be “as reliable as sockets” (e.g., if a peer disappears)
  Have well-defined failure semantics
    TBD – document failure semantic
    Endpoint error state, EQ errors
  Have ability to reclaim resources on failure
    Closing an object in the error state should succeed
    Kernel must cleanup all resources
Notes: MPI community feedback:
We need async progress (from the perspective of MPI looking down). MPI-3 demands it.
Pair this with multiple consumers of the interface both being able to have “async progress” from a single place (E.g., MPI and PGAS playing nicely together)
Failures: well-defined a way to reclaim resources from that layer and below
Both async progress points now listed as a “need” in slide 11
Added point about reclaiming resources