## Slide 1: NFS over RDMA
Boris Shpolyansky
Mellanox Technologies Inc.
boris@mellanox.com

## Slide 2: Agenda
NFS overview
NFS over RDMA
Client and server main flows
Current status and plans

## Slide 3: Network File System (NFS) overview
From the Internet:
  A distributed file system that enables users to access files and directories located on remote computers and treat those files and directories as if they were local.
Originally developed by Sun Microsystems
Widely used in Unix- and Linux-based environments
Notes: Transparent: Socket switch selects TCP or SDP
  Administrable policy
Socket semantics: IPv4 addressing, Uses TCP port space, Connect/Accept model, Common socket options, Out of band data
Wire protocol: InfiniBand Specification 1.2 Annex A4

## Slide 4: NFS over RDMA - benefits
Same NFS v2/3 protocol with enhanced performance:
  Highly reduced transport overhead
  Direct I/O access
  Effective interconnect utilization – greater BW
Sample performance over 4x IB interconnect*:
  350MB/sec at 20% of client CPU
May be improved up to almost wire speed
*Tom Talpey, NFS/RDMA Linux Client, February 2004
http://www.citi.umich.edu/projects/rdma/refs/NFS-RDMA_Linux_CThon_2004.pdf

## Slide 5: SW layer structure
Originally running over TCP/UDP sockets
Extended using transport switch to support RDMA transport
NIC

## Slide 6: NFS over RDMA - client
Create transport
  Initialize local resources
Connect to the server
  Find the server in the subnet
  Establish connection
Perform file operations
  Write remote file
    Small amounts – Send with inline data
    Large transfers – RDMA Read (by the server)
  Read remote file
    RDMA Write (by the server)

## Slide 7: NFS over RDMA - server
Create transport
  Initialize local resources
  Create and advertise public service point
  Listen to connections
Accept client connections
  Establish connection
Perform file operations
  Write local shared file
    Send by the client
    RDMA Read from the client’s buffer to a local buffer, which is used by disk controller to write the data to the disk
  Read local shared file
    Gather data from the disk, RDMA Write to the client’s buffer

## Slide 8: Write operation - Send
Rcv
Buf
Client
Server
Send
Buf
Send
Buf
Send Req with inline data
Rcv
Buf
Write to the disk
Completion
Send
Buf
done
Send
Buf
Rcv
Buf
Rcv
Buf
Data
Buf
Data
Buf
Data
Buf
Data
Buf

## Slide 9: Write operation – RDMA
Rcv
Buf
Client
Server
Send Req
Data
Buf
RDMA Read
Completion
Read Response
Rcv
Buf
Send
Buf
Data
Buf
Data
Buf
Data
Buf
Write to the disk
done
Send
Buf

## Slide 10: Read operation
Rcv
Buf
Client
Server
Send Req
Data
Buf
RDMA Write
Rcv
Buf
Send
Buf
Data
Buf
Data
Buf
Data
Buf
Read from the disk
Send
Buf

## Slide 11: Current status and plans
Client
  NetApp over kDAPL gen1
    www.sourceforge.net/projects/nfs-rdma
Server
  NetApp – over kDAPL, proprietary SW/OS (not Linux-based)
  CITI – under development over kDAPL gen 1
  Mellanox – considering OpenIB gen2 API, interoperable with CITI NFS-o-RDMA client
Goals
  Integrating NFS RDMA client and server into Linux kernel
  Storage vendors to provide products incorporating NFS RDMA

## Slide 12: References
NFS RDMA Problem Statement, Tom Talpey, Chet Juszczak
  http://www1.ietf.org/internet-drafts/draft-ietf-nfsv4-nfs-rdma-problem-statement-02.txt
RDMA Transport for ONC RPC, Brent Callaghan, Tom Talpey
  http://www.citi.umich.edu/projects/nfsv4/rfc/draft-callaghan-rpc-rdma-00.txt