## Slide 1: Reliable Datagram Sockets (RDS)
Ranjit Pandit
SilverStorm Technologies
rpandit@silverstorm.com

## Slide 2: Agenda
Goals
Architecture Overview
High Level Design
Future

## Slide 3: Goals
Provide reliable datagram service
  performance
  scalability
  High Availability
  simplify application code
Maintain sockets API
  application code portability
  faster time-to-market
Keep It Simple !!!

## Slide 4: Agenda
Goals
Architecture Overview
High Level Design
Future

## Slide 5: Architecture Overview
Host Channel Adapter
InfiniBand Access Layer
IPoIB
IP
Oracle 10g
Socket
Applications
TCP
UDP
SDP
RDS
Kernel
User
UDP Applications

## Slide 6: Architecture Overview
RDS registers with the kernel as driver for Address Family PF_INET_OFFLOAD and Type SOCK_DGRAM
Application creates a RDS socket with socket(2)
  arg1 = PF = PF_INET_OFFLOAD (0x26)
  arg 2 = Type = SOCK_DGRAM
socket(2) API supported
  socket, bind, ioctl, sendmsg, recvmsg, poll, getsockopt/setsockopt

## Slide 7: Agenda
Goals
Architecture Overview
High Level Design
Future

## Slide 8: Connection model
Addressing
  IPv4 addressing
  uses IPoIB for address resolution
Peer-to-peer connection model
  node-to-node connection
  on-demand connection setup
    connect on first sendmsg()
  disconnect on error or inactivity
Connection setup/teardown transparent to applications

## Slide 9: Data and Control Channel
Uses RC QP
Data and Control QP per connection
Selectable MTU
b-copy send/recv
h/w flow control

## Slide 10: Send
sendmsg() success => guaranteed delivery
  allows send pipelining
  send error is catastrophic
ENOBUF returned if insufficient credits, application retries
  not a common case

## Slide 11: Receive
Identical to UDP recvmsg() behavior
  similar blocking/non-blocking behavior
“Slow” receiver ports are stalled at sender side
  combination of activity (LRU) and memory utilization used to detect slow receivers
  sendmsg() to stalled destination port returns EWOULDBLOCK, application can retry
  recvmsg() on a stalled port un-stalls it

## Slide 12: High Availability (failover)
Use of RC and on-demand connection setup allows HA
  connection setup/teardown transparent to applications
  every sendmsg() could result in a connection setup
  if a path fails, connection is torn down, next send can connect on an alternate path (different port or different HCA)

## Slide 13: /proc interface
/proc/driver/rds/config
  view and change RDS configurable parameters
/proc/driver/rds/info
  info on sessions, stalled ports etc
/proc/driver/rds/stats

## Slide 14: Agenda
Goals
Architecture Overview
High Level Design
Future

## Slide 15: Future
AIO
Z-copy
Shared recv queue