## Slide 1
Roland Dreier
Technical Lead – Cisco Systems, Inc.
OpenIB Maintainer
Sean Hefty
Software Engineer – Intel Corporation
OpenIB Maintainer
Yaron Haviv
CTO – Voltaire
Stack Development Update, Testing Status and Target Release Goals

## Slide 2: Agenda
www.openib.org
Linux Kernel Infrastructure
Linux Userspace Infrastructure
RDMA Enabled Applications
InfiniBand and Beyond
The InfiniBand Software Solution
Notes: Infiniband is the high performance clustering interconnect.
OpenIB will provide the core software to support IB.

## Slide 3: OpenIB Alliance
www.openib.org
Improve interoperability
Reduce the time and cost for deployment
Open-Source InfiniBand RDMA Infrastructure
Notes: Vendors want to validate against a single software stack.
Want Infiniband software integrated with the Linux kernel.

## Slide 4: OpenIB Alliance
www.openib.org
…and the open source community!
Notes: Includes systems vendors, Infiniband specialists, end-users, major national labs (supercomputers and large clusters).
Developers can work directly with customers

## Slide 5: Philosophy
Open source development
  Dual BSD / GPL License
Integrated with OS infrastructure
Working with companion RDMA standards
Anyone can contribute
www.openib.org
Code Quality,
Stability,
Performance
Notes: Main development occurs on openIB mailing lists. Includes direct collaboration with customers.
Work with Linux kernel developers to ensure seamless operation
Carried open source work forward to include Windows.
Working with DAPl, IT-API, OpenRDMA groups.
Key developer goals…

## Slide 6: Achievements
www.openib.org
Jun
Nov
Mar
May
Jul
‘05
‘04
Will support Windows & RDMA enabled Ethernet
Infiniband Leaders Form OpenIB Alliance
Deliver a high-performance, scalable, and interoperable Infiniband software stack
“This will enable … a robust, resilient, and manageable infrastructure for data center, Grid, and HPC.”
“… accelerate the creation of a single Infiniband software stack”
OpenIB Linux release

## Slide 7: Software Architecture
www.openib.org

## Slide 8: Linux Kernel Infrastructure

## Slide 9: Overview
Verbs API derived from VAPI
Best of breed software solution
Support multiple HCA
Optimized for Linux kernel
Support latest stable kernel release
Linux Kernel Infrastructure
Complete InfiniBand infrastructure
Notes: Pulled best pieces from Infiniband vendor software stacks and rewrote others to meet Linux kernel coding guidelines based on feedback.
Fully integrated with Linux features – interrupt handling, threading, user/kernel transitions, etc.
Backport patches are available for some older kernel releases (2.6.9)

## Slide 10: Architecture
Linux Kernel Infrastructure

## Slide 11: Linux Userspace Infrastructure

## Slide 12: Overview
Library exposes verbs to usermode clients
Secure userspace access
Kernel bypass for speed path operations
RDMA to / from application memory
Linux Userspace Infrastructure
Direct hardware access for applications

## Slide 13: Architecture
Linux Userspace Infrastructure
openib.org
2.6.13

## Slide 14: RDMA Enabled Applications

## Slide 15: One Fabric, Many Uses
Low latency IPC for clustering
Variety of high speed file and block protocols, remote boot capable
Bridging to external GbE and FC
Multi-Service Switches
Management
Servers
Parallel
FC / IB / IP Storage
InfiniBand
IB HCA
IPC (MPI & DAPL)
Applications
Network (SDP & IPoIB)
Storage (File & Block)
InfiniBand Host Software Stack
RDMA Enabled Applications
One fabric has it all

## Slide 16: Networking / IPC APIs
RDMA Enabled Applications
Tunnels IP packets over IB
Application APIs unchanged
OpenIB software enables applications
Fabric agnostic RDMA API
Standard API for scientific clustering
Bypasses TCP/IP stack for direct HW access
Notes: Applications use standard sockets, DAPL, or MPI APIs.
Commercial and open source MPI implementations are available.
SDP uses separate address family – a loadable library allows use without need to modify apps.

## Slide 17: Networking / IPC Performance
RDMA Enabled Applications
How well can apps perform?
Ciara VXB-7520J
3.4 GHz Dual EM64T Xeon
4 GB DDR
RedHat EL4.0
OpenIB SVN 2833 backported
10 Gb/sec (4X) - 8X PCI Express HCA
MTS2400
MTLP25208

## Slide 18: Networking / IPC Performance
Performance tests and ratings are measured using specific computer systems and/or components and reflect the approximate performance of Intel products as measured by those tests. Any difference in system hardware or software design or configuration may affect actual performance. Buyers should consult other sources of information to evaluate the performance of systems or components they are considering purchasing.
RDMA Enabled Applications
I.e. your results may vary

## Slide 19: Networking / IPC Performance
RDMA Enabled Applications
Small message latency
IPoIB
SDP
MPI
3.46 us
924 MBps
Verbs
Large message bandwidth

## Slide 20: InfiniBand Revolutionize Storage
High-speed NAS and SAN on the same fabric
Scale out storage through clustering and virtualization
Server Racks
A Bunch of low cost Storage Arrays
A lot of bandwidth (InfiniBand)
Commodity Servers running NAS Gateways or Cluster File System
Switch
RDMA Enabled Applications

## Slide 21: Storage in OpenIB
RDMA Enabled Applications
Storage
NIC
R-NIC
IB HCA
Switch

## Slide 22: NFS/RDMA
High-speed RDMA RPC transport
Maps transparently to NFS and applications
Reside over kDAPL for fabric independence
NFS
RPC/XDR Switch
UDP
TCP
RDMA
RDMA
Standard NIC
Direct Access
kDAPL
RDMA Enabled Applications

## Slide 23: Xen Virtualization over IB
VM1
OS
VM2
OS
VM3
OS
GbE NIC
FC HCA
Software based Network and Storage switching
XEN
Storage
Network
Slower I/O
No isolation
Multiple cards and fabrics
Direct HW access for I/O
One 10Gb/s card for Network, Storage, and IPC
Scale out using clustering (IPC)
VM1
OS
VM2
OS
VM3
OS
IB HCA
XEN
IPC
Direct HW access
Xen with IB
Xen, the traditional way
RDMA Enabled Applications

## Slide 24: Infiniband and Beyond
What’s left?

## Slide 25: Future Efforts
Scale out testing
Scalability enhancements
Integrate upper-layer protocol software
Windows software release
Xen support
InfiniBand and Beyond
Notes: Include ULPs in Linux distribution and OpenIB releases – SDP, SRP, iSER
Enhancements – path migration, QP redirection, OpenSM optimizations, partitioning, QoS…

## Slide 26: Companion Technologies
Working with OpenRDMA Group
Common RDMA interface for Linux
Support InfiniBand and iWarp
InfiniBand and Beyond

## Slide 27: Summary
Solid InfiniBand infrastructure
Available in Linux today, Windows soon
Low latency, high bandwidth applications
OpenIB – Open-Source Infiniband RDMA Infrastructure
OpenIB = InfiniBand software

## Slide 28: Call to Action
Join the open source effort
Request OpenIB software from your Linux distributor
Ask your IB vendor about OpenIB support
InfiniBand and Beyond
Join OpenIB

## Slide 29: Please fill out the Session Evaluation Form. Thank You!

## Slide 30: Glossary
CM – communication manager
DAPL – direct access provider library
GSI – general services agent
HCA – host channel adapter
IPC – interprocess communication
IPoIB – IP over Infiniband
iSER – iSCSI extensions for RDMA
PMA – performance management agent
SDP – sockets direct protocol
SM – subnet manager
SMI – subnet management interface
SRP – SCSI RDMA procotol
OpenIB – Open-Source Infiniband RDMA Infrastructure

## Slide 31: Additional Resources for this Session
Session presentation can be downloaded from the IDF web site – when prompted enter:
    Username: idf
    Password: fall2005
More web based info: www.openib.org