## Slide 1: IBTA Developers’ Conference Link Working Group - QoS
September 25th 2006
Eitan Zahavi
LWG-QoS

## Slide 2: QoS v. Congestion Control
Congestion Control
  The objective of congestion control is to avoid if possible, and eliminate if it has already occurred, congestion spreading.
  Response is in “hardware” time
    Assumes a hardware solution
    Assumes no knowledge of relative priorities, response time goals, etc.
QoS
  The objective of QoS is to allow a host to control the performance attributes of the work it manages, within bounds specified by an administrator.
  Response may be measured in seconds
    Allows for a software solution
    Requires knowledge of relative priorities, response time goals, etc.

## Slide 3: Workload Types
Transactional
  Goal: Response Time
  Bandwidth requirements unknown
  Tolerant of jitter
  Control via Relative Priority
Streaming
  Goal: Quality of sound or picture
  Bandwidth requirements typically known
  Sensitive to bandwidth, latency and jitter
  Control by reserving bandwidth
We are focusing on Relative Priority only

## Slide 4: QoS in InfiniBand Today
VL1
VL3
VL2
VL0
Virtual Lanes:
VLArbitrationTable
VL15
SL1
SL7
SL11
SL2
SL13
SL14
SL15
SL3
SL4
SL5
SL6
SL12
Service Levels:
SLtoVLMappingTable

## Slide 5: QoS in InfiniBand Today
Switch
Switch
Path Selection:
- LID Mask Control
00
00
01
00
01
10
11
00
01
10
Switch
Channel
Adapter A
Channel
Adapter B
Switch

## Slide 6: Why a QoS Manager?
Not all workloads are of equal importance
Not all servers’ high importance workloads are equal
Ability to fail a request, rather than impact existing workload on fabric (streaming)
Numerous knobs and dials must be set
Initial settings need to be adjusted

## Slide 7: Functions of QoS Manager
Select paths that meet requester’s QoS requirements
  Service Level (SL)
  Traffic Class (TClass)
  LID
Prevent over commitment of VLs by streaming workloads
Monitor fabric
  Are workloads still receiving requested QoS levels
Adjust fabric configuration
  Turn knobs and dials to maintain QoS
  May set some initial configuration values

## Slide 8: QoS Philosophy
Application presents QoS Manager with its required path attributes
  QoS Manager selects potential path(s)
  No predefined meaning to SLs and TClass
  Transactional and streaming workloads do not share VLs
Focus workgroup on how QoS Manager will work
  Use existing functions, performance counters, and MADs
  Add only where necessary
Allow for various levels of sophistication

## Slide 9: Passive vs. Active Management
A Passive QoS Manager:
  fabric configuration is relatively static
  certain SLs are defined as “high priority”
  assigns requests based on requested priority
    possibly limiting servers to a range of priorities
An Active QoS Manager:
  configures fabric
  assigns requests based on requested priority
    possibly limiting servers to a range of priorities
  monitors fabric
  interacts with other managers to modify fabric and assure relative priorities are maintained

## Slide 10: Knobs Available to the QoS Manager
Subnet Administration (*):
  Selecting the SL the client should use
    and eventually TClass
  Path choices among existing paths (LMC)
Subnet Management (*):
  SLtoVLMappingTable values
  VLArbitrationTable values
  Re-routing of the network (forwarding tables)
Congestion Control (†):
  CCT Time Interval (decay time)
  BECN Index Increase
  CCTI_min (lowest CCTI allowed)
  Congestion control table values
Configuration Management (†):
  SL Enforcement
  Client Priority
* Release 1.1
† Release 1.2
Notes: Is changing the “SL to VL Mapping Table values” and the “Forwarding Tables” too difficult, due to cyclic loop problem? Due to overloading?

## Slide 11: Status
Defining the communication mechanism between the fabric client and the QoS Manager
Scope includes Passive and Active Management
Scope limited to Relative Priority Only
  Not Bandwidth Reservation
Notes: Stretch Goal: Defining the communication mechanism between the QoS Manager and other managers (e.g. Congestion Control Manager, Device Manager, etc.)