## Slide 1: Simple Connectivity Between InfiniBand Subnets
Yaron Haviv, CTO, Voltaire
yaronh@voltaire.com

## Slide 2: Agenda
Defining the problem and scope
Getting to the other side
Mapping names/IPs to GUIDs
Forwarding tables and paths
Establishing connections
Multi-Path & HA
Host, SM implementation requirements
Management/Administration

## Slide 3: Requirements for Simple Inter Subnet Connectivity
Requirements
  Connect two IB islands, next to or far apart from each other
  Pass native IB protocols (Lustre, iSER, MPI, SDP, ..) at high-speeds
  Keep islands isolated from each other for scalability, stability, security
  Allow bandwidth aggregation over multiple links
Assumptions
  Require highly reliable intermediate fabrics
  No reordering, no deadlocks
  Typically few remote sites, not the Internet
  Allow some manual configuration
  Not addressing dynamic routing protocols for now !, well known MTU

## Slide 4: Getting To The Other Subnet
Subnet A
Subnet B
SM
SM
DGID -> Router DLID ?
Send to Router
Send to Next Hop
DGID -> DLID ?
Send to Destination
And Back …

## Slide 5: IP Addresses & Partitions
InfiniBand PKey is a QP (Transport) attribute
Simpler to have IP subnets that map over both IB subnets
Making IB routers split IP subnets (be also IP routers) is challenging, require CMA changes, and use of GID tables
IB Subnet A
IP Subnet X (Partition x)
IB Subnet B
IP Subnet Y (Partition y)

## Slide 6: IB ARP Across Subnets
Subnet A
Subnet B
SM
SM
ARP Request (Multicast)
Send to Next Hop
DGID -> MLID,
Send to Destination
ARP Response (Unicast)
* Assume router register to the multicast group
DGID -> Router DLID ?
Register IP to GID mapping

## Slide 7: Global Path Resolution
Client ULP or CMA issue SA PathRecord Request
  Map S/DGID + TClass to destination LID, MTU, SL, …
Path can be returned locally based on GID Prefix (if not the same as local), by looking into a local table
  Save SM accesses
Or be sent to SA (like today), and SA will return the path
  Allow central management, potentially use caching
  Can select between multiple routers based on S/DGID+TClass
Dst GID | Tclass | IB Router | SL | MTU
5.6.*.* | * | G 1.2.3.98 | 1 | …
5.7.*.* | * | G 1.2.3.99 | 1 | …
Sample Host/SM Routing Table

## Slide 8: IB L2-3 Headers 101
LRH
Variant CRC
GRH
Transport Header(s)
Packet Payload
Invariant CRC
LRH (Local Header)
GRH (Global Header), just like IPv6

## Slide 9: IB Router Logic
Route Table
DGID (128)
TClass (8)
Hop Limit’ (8)
Egress Port
SL’ (4)
DLID’ (16)
SLID’ (16)
VL’ (4)
Hop Limit (8)
Hop Limit Logic
PortInfo*
SL to VL*
Longest-match prefix (0-64 or 128)
VCRC
CRC Logic
Updates

## Slide 10: Establishing Connections
IB CM REQ message incorporate Local & Remote LIDs
Passive side use the CM REQ LIDs to respond
Need to change the Passive side, make sure it lookups up the return path rather than use the CM REQ fields
CM REQ Fields (from IB Spec)

## Slide 11: Multi-Path & HA Example
Topology
Routing Table

## Slide 12: Failure Detection and Fail-Over
Initiator is key in determining failures, it should migrate to alternate path, and inform others/SM is possible

## Slide 13: Required Host & SM Changes
Host Implementation
  Determine if path request is local or remote, retrieve path attributes from cache or manual entries, or from SM (in such case no change to PR)
  Update CM to resolve returned path dynamically rather than us CM REQ information
  Make sure ULPs/CM use GRH Header and provide relevant fields
  Make sure ULPs/CM use PathRecords and the returned values (MTU, SL, PKey, etc.)
SM
  Map distinguish global PathRecord queries from local, and provide path information based on manual tables and possibly allow multi-path
  Allow configuration of routing tables by users and external scripts/tools

## Slide 14: Management
Require insertion/update of IB routing tables via standard mechanism
Provide exception handling (e.g. MTU Problems, unreachable, ..)
In future can address automated SM-Router interaction to minimize configuration
Try and leverage on IPv6 later on to allow automated/simpler configuration

## Slide 15: Q & A