## Slide 1: iWARP Status
Tom Tucker

## Slide 2: iWARP Branch Status
OpenFabrics SVN
  iWARP in separate branch in SVN
  Current with trunk as of SVN 7626
  Support for two iWARP RNICs currently in the tree:
    Chelsio T3 - single and dual port 1 and 10GbE RNICs
    OGC AMSO1100 - single port 1GbE RNIC
  Also includes all IB devices from main trunk
Kernel.org
  Currently being merged into Roland’s for-2.6.19 branch
  Includes:
    Core changes to ib_verbs and rdma_cm
    iWARP Connection Manager
    AMSO1100 device driver

## Slide 3: iWARP Device Support
In order of likely kernel.org integration…
AMSO1100 1Gb RNIC
  Good starting point for new development.
  Open source driver in iWARP branch now
  Targeted for kernel.org 2.6.19
Chelsio
  Single and dual port 1GbE and 10GbE RNIC
  Open source driver in in iWARP branch now
  Targeted for kernel.org in 2.6.20?
NetEffect
  Single port 10GbE RNIC implementation
  Driver available through Beta evaluation agreement

## Slide 4: iWARP Branch Merge Plan
Complete upstream merge into 2.6.19 kernel.org
Back-port upstream code into SVN main trunk
Move Chelsio and any other devices not upstream to main trunk
Include iWARP support in subsequent OFED releases

## Slide 5: iWARP Branch Activities
Device Drivers
  Unannounced activity from other RNIC vendors?
Help from interested developers?

## Slide 6: Future Development
Expanded core support for optional device features
New verbs, WR and devices
New iWARP CM features
Expanded device attributes database
Additional ULP, storage and middleware application support
User-mode Transport Neutral API

## Slide 7: Optional Feature Support
Goals
  Consistent, well understood mechanisms
  Application can run on any device and transport
  Application can take advantage of transport and/or vendor optimizations
  Capabilities queried at run-time, not discovered by trial and error.

## Slide 8: Optional Feature Support
Mechanisms
  Bit fields in a capabilities mask
  Function pointers (potentially null) in the device function table
Bit fields used to indicate whether a particular feature implemented as an SQ WR is present, e.g.:
  Invalidate STag
  Bind Memory Window
  RDMA Read and Invalidate
  RDMA Write with Immediate
Function Pointers used for features implemented as Verbs, e.g.:
  Create Memory Window

## Slide 9: Expanded Device Attributes
Not all relevant device attributes are exported currently, for example:
  RDMA_READ SGE limit
  DMA_MR size limit
These attributes need to be added to the device attributes structure
Namespace cleanup
  Consistent naming of min/max
  More descriptive names

## Slide 10: New iWARP CM Features
Native stack port space integration
  TCP ports consumed by native stack will be seen by the iWARP CM and vice versa
IRD/ORD Negotiation
  RDMA Read inbound and outbound limits exchanged in private data at connection establishment -- needs IETF changes
  Option #1
    Best-can-do approach implemented with conn_req parameters.
  Option 2#
    CM events expanded to included peer’s advertised limits
    conn_req parameters are absolutes and connect/accept fails if they can’t be honored

## Slide 11: iWARP CM Continued
Streaming mode connection establishment
  llp_listen, llp_connect, llp_accept, llp_send, llp_recv (needed for iSER spec. compliance)
Socket migration
  rdma_create_from_fd - returns bound rdma_cm_id from socket

## Slide 12: Transport Neutral API
Developed by Krishna Kumar <krkumar2@in.ibm.com>
Set of patches against iWARP branch
User-mode only
ibv_  rdma_ for all data types and verbs
Needs wider review, discussion

## Slide 13: RDMA System Management
iWARP is not an IP protocol so it shares the TCP port space like imap, or http
Users need the ability to specify when to use RDMA vs. TCP for multi-transport services
Proposal
  Use /etc/services, portmapper
  IETF proposal for RDMA services names and port numbers, e.g. “rnfs”

## Slide 14: Help!
Adapter Vendor Participation
  You should contribute more than just your device driver
$$$$
  We feed our engineers under the door, but their kids at home eat too
Warm bodies
  If you interested, let us know. There’s plenty to do…

## Slide 15: Questions?