## Slide 1: Congestion Control
Ian Colloff
LWG
San Francisco
September 25, 2006

## Slide 2: Congestion Control Agenda
What is congestion
Terminology
Control of Congestion
Legacy Device support
Conclusion

## Slide 3: What is Congestion
Within the switching fabric:-
  Two or more ports target a single port with a sustained flow that is greater than the link bandwidth
    Buffers fill, limits credit return to neighbor device
      Result: head of line blocking
  A long link in the fabric
    The link capacity is close to or greater than the maximum buffer credits at one or both ends
    Credit “starvation”
      Link is not able to run at full rate, head of line blocking
      Static form, but needs to be considered in a general solution
At an Endpoint
  When an endpoint can’t receive data at full link rate
    Limits credit return to its connecting switch port
      Result: head of line blocking

## Slide 4: Diagram of a Congestion Situation
Flows in the middle of a fabric
“Source” of congestion
Backup if Switch B input buffer fills
Switch A
Switch B

## Slide 5: Terminology
FECN : Forward Explicit Congestion Notification
  Signal from the switch to the destination endpoint of data
BECN : Backward Explicit Congestion Notification
  Signal from the destination endpoint to the source of data
Root of Congestion :
  Queues or buffers fill, directed to an output port, but the data flows at link rate
Victim of Congestion :
  Queues or buffers fill, directed to an output port, but the data can’t run at link rate due to lack of credits

## Slide 6: Congestion Control Specification
Congestion control is in Annex 10 in Volume 1 version 1.2 of the InfiniBand Specification
  The functionality is Optional
Does not define a Congestion Manager
  Defines the base mechanisms a Congestion Manager may use to control congestion
Basic mechanisms to:-
  Control injection rate in “Hardware” time frame
    Little or no software intervention required
  Enable comprehensive Management features to be developed using the controls
  Maybe used by a QoS Manager to control rates
  Performance metrics, for congestion analysis

## Slide 7: Control of Congestion I
Limited by protocol & device complexity
  Control Flows at endpoints on:-
    QP or Port/SL basis (mutually exclusive)
  Use FECN
    Switches mark congested flows randomly at a Root of congestion (identification and marking is configurable)
      Override to mark on a Victim
      Prohibitive cost of issuing a BECN directly from a switch port
  Endpoint receiving a FECN returns a BECN
    Either in a Congestion Notification Packet or ACK(optional)
  Endpoint receiving a BECN
    Reduces the rate of injection for a flow into the fabric
      Rate is increased over time

## Slide 8: Control of Congestion II
At the source endpoint
  Rate reduction
    Table per port each has 128 or more entries
      Tables are configurable
      Each entry contains an inter-packet delay value for a flow
      Subsequent entries in the table should reduce the flow
      Can control rates between 100% and 0.006% of link rate
    Receipt of a BECN increases index into the table
      Index per QP or SL/Port
      This increase is configurable, and each SL can be different
  Rate increase
    Timer (configurable on an SL/Port basis)
      On expiry, an index into the table is reduced by 1.
  The mechanism is flexible and highly configurable
    Can be used for linear and non-linear response functions

## Slide 9: Legacy Devices
Interaction with Legacy Devices
  The Congestion Notification Packet
    The packet to be silently dropped (op-code)
  Switch: control credit return (optional)
    Credit starvation
      Average “buffer occupancy” threshold breached, Limit rate of credit return
    Controlled on a VL basis
      All VL’s for a port have the same threshold, and rate limit
      Different ports may have different values
    Affect flows that don’t contribute to congestion

## Slide 10: Conclusion
No Congestion Control scheme is perfect
  Provides a very flexible mechanism to help control congestion
  Options to help control legacy endpoints
    In a coarse way
  Relatively easy to implement
  Simulation indicates that the scheme can successfully control congestion (under the trial conditions)

## Slide 11: Backup Slides

## Slide 12: Congestion Avoidance
Over provision the fabric
  More paths between endpoints
    Load balancing techniques
  Wider links within the fabric
  Higher link speeds within the fabric
  Provide a fabric that has the blocking characteristics of a single switch
    More expensive than a conventional CCB Fat Tree
Load balance
  Using multiple paths through the fabric between two endpoints