## Slide 1: Physical Layer Update – EWG
Presenting:
Ian Colloff, EWG

## Slide 2: Outline: Physical Layer Update Session
EWG Activities Overview
  DDR/QDR
  Rel. 1.2 Signaling Review
  Spec changes since Jan.06 on Compliant Channels & Copper Cables
  Pluggable Devices
Following this presentation:
  EWG Member Company Presentations

## Slide 3: DDR, QDR: Compatibility & Data Rates
Interoperable with all previous IB ports
  All copper links capable of SDR operation as well (when SDR eye opening specs are met)
  Optical link rules for SDR interoperability:
    All 1x-SX, 4x-SX, and 12x-SX SDR, DDR, and QDR devices must interoperate at SDR
    All 1X-LX SDR, DDR, and QDR optical transceivers must interoperate at SDR
    4X-LX (4x-SDR serialized to 10Gbps) not required to interoperate with any other speed or width
Same (intermateable) connectors
Some SDR cables or backplanes may not function at the higher bit rates
  Noise/Crosstalk, & Signal Integrity (insertion, return loss) at DDR/QDR
DATA RATES | 1x | 4x | 8x | 12x
SDR (Orig.) – 2.5 Gb/s / direction / lane | (2.5+2.5) Gbps | (10+10) Gbps | (20+20) Gbps | (30+30) Gbps
DDR – 5.0 Gb/s / direction / lane | (5+5) Gbps | (20+20) Gbps | (40+40) Gbps | (60+60) Gbps
QDR – 10.0 Gb/s / direction / lane | (10+10) Gbps | (40+40) Gbps | (80+80) Gbps | (120+120) Gbps

## Slide 4: Review: Rel 1.2 Signaling Approaches
Specified Transmit Characteristics at chip
Specified Receive Characteristics at chip
Interconnect specified separately
Loss Budget/compliance points
“EYE” open at receiver
Pre-emphasis or filter for equalization
Signal Detect
Compliance channel: a defined filter, inserted between Tx & Rx for test and verification
Compliant Channel: actual HW which meets defined requirements to allow operation at specified BER
Receiver specified by transmitter, & channel S-parameters
  Eye may be closed at receiver input
Assume pre-emphasis at Tx, & DFE or similar at Rx
  Adaptive equalization using training pattern on initialization
Heartbeat/Latency ordered set
No high-speed signal detect (beacon at SDR rate)
DDR: Changes to improve Interconnect Distance
  Increased loss budget by 5 dB to compensate for higher-frequency losses (skin effect, dielectric absorption) and increased crosstalk
  DDR copper nearly same distance as SDR copper
QDR: Newer materials probably needed for QDR backplanes
SDR – Defined in Rel. 1.1
DDR/QDR – Defined in Rel 1.2

## Slide 5: DDR/QDR Channel: S-Parameter changes
 | DDR |  |  |  | QDR |  |  | 
f, MHz | Old Sdd21 min. (Jan. errata) | New Sdd21 min. (modified) | Old Sdd11 (Jan. errata) | New Sdd11 (unchanged) | Old Sdd21 min. (Jan. errata) | New Sdd21 min. (modified) | Old Sdd11 (Jan. errata) | New Sdd11 (unchanged)
100 | -7 * (sdd21 min./17) | -8 | -10 | -10 | -7 * (sdd21 min./17) | -8 | -10 | -10
200 | -7 * (sdd21 min./17) | -8 | -10 | -10 | -7 * (sdd21 min./17) | -8 | -10 | -10
625 | -7 * (sdd21 min./17) | -8.5 | -10 | -10 | -7 * (sdd21 min./17) | -8 | -10 | -10
1250 | -10 * (sdd21 min./17) | -12.1 | -10 | -10 | -7.5 * (sdd21 min./17) | -9 | -10 | -10
1875 | -13 * (sdd21 min./17) | -14.7 | -10 | -10 | -8.5 * (sdd21 min./17) | -10.4 | -10 | -10
2500 | -17 * (sdd21 min./17) | -17 | -10 | -10 | -10 * (sdd21 min./17) | -12.1 | -10 | -10
3750 |  |  |  |  | -13 * (sdd21 min./17) | -14.7 | -10 | -10
5000 |  |  |  |  | -17 * (sdd21 min./17) | -17 | -10 | -10
Scaling of min. values to lower freqs. no longer required
DDR Common mode (sdc21, sdc11) requirements dropped
Channel covers Test Points TP2 to TP4. Informative specifications for Serdes-to-Serdes S Parameters allow ~2dB margin at high-frequencies for card wiring
DDR & QDR compliant channel changes from January errata:

## Slide 6: DDR/QDR Cable: S-Parameter changes
 | DDR |  |  |  | QDR |  |  | 
f, MHz | Old Sdd21 min. (Jan. errata) | New Sdd21 min. (modified) | Old Sdd11 (Jan. errata) | New Sdd11 (unchanged) | Old Sdd21 min. (Jan. errata) | New Sdd21 min. (modified) | Old Sdd11 (Jan. errata) | New Sdd11 (unchanged)
100 | -7 | -8 | -10 | -10 | Not spec.’d | -8 | -10 | -10
200 | -7 | -8 | -10 | -10 | Not spec.’d | -8 | -10 | -10
625 | -7 | -8.5 | -10 | -10 | Not spec.’d | -8 | -10 | -10
1250 | -10 | -12.1 | -10 | -10 | Not spec.’d | -9 | -10 | -10
1875 | -13 | -14.7 | -10 | -10 | Not spec.’d | -10.4 | -10 | -10
2500 | -17 | -17 | -10 | -10 | Not spec.’d | -12.1 | -10 | -10
3750 |  |  |  |  | Not spec.’d | -14.7 | -10 | -10
5000 |  |  |  |  | Not spec.’d | -17 | -10 | -10
Max. insertion loss (envelope) limits dropped
Scaling of min. values to lower freqs. no longer required
Common mode (sdc21, sdc11) requirements dropped
DDR & QDR copper cable changes from January errata:

## Slide 7: New Pluggable Form Factor
4x Pluggable specified for SDR only
4X pluggable based on XPAK MSA
  Uses XPAK mechanical and Low Speed Electrical
  Uses IBTA High Speed Electrical, Optical, 4X Connector, and 4X cable
  www.xpak.org
Required Port Type 2
  Improved jitter at transmitter
SDR, DDR, ..
Based on QSFP MSA
  Smaller, better heat mgmnt, better electricals
No Port Type 2 this time
  All signal conditioning done in pluggable device
Multiple distance-specific device types possible
  Passive copper slug (part of cable)
  Passive copper module (no extra connector allowed)
  Active copper (extra connectors allowed)
  Active cables (copper or optical)
  Optical Transceiver
4x Pluggable – Rel. 1.2
4x Pluggable-QSFP -- Design Goals

## Slide 8: Thank you…