## Slide 1: OpenFabrics Enterprise Distribution (OFED) Update
Jamie Riotto, Cisco
Sujal Das, Mellanox
September 25, 2006
IBTA-OFA DevCon Presentation

## Slide 2: Topics
OFED – background, purpose
Development process
Success story
OFED v1.1
The Future
Call to Action

## Slide 3: Background, Purpose
Enterprise work group formed – April, ’06
Collaboration among InfiniBand suppliers
  Cisco, IBM, Mellanox, QLogic, SilverStorm, Voltaire
  Also support from Sandia, Intel, OS vendors, others
Single stack, commercially supportable
Interoperable
Synergy with kernel and OS vendor needs
OFED v1.0 released in June

## Slide 4: Development process
Discussions in openfabrics-ewg@openib.org and teleconferences
  Feature agreements, process discussions, test status reporting, release candidates, source freeze, collaborative
Build process:
  User space: https://openib.org/svn/gen2/branches/1.1/src/
  Kernel: git://www.mellanox.co.il/~git/infiniband ofed_1_1
Bug reporting: bugzilla: http://openib.org/bugzilla/

## Slide 5: Success Story – OFED 1.0
Great collaborative development and test
Processes, schedules worked well
Widespread testing, adoption of OFED 1.0
  End users, Server OEMs, Red Hat, Novell/SUSE
  Virtualization software and ISV support
Many public announcements showing support

## Slide 6
OpenFabrics Software Vision
SA | Subnet Administrator
MAD | Management Datagram
SMA | Subnet Manager Agent
PMA | Performance Manager Agent
IPoIB | IP over InfiniBand
SDP | Sockets Direct Protocol
SRP | SCSI RDMA Protocol (Initiator)
iSER | iSCSI RDMA Protocol (Initiator)
RDS | Reliable Datagram Service
UDAPL | User Direct Access Programming Lib
HCA | Host Channel Adapter
R-NIC | RDMA NIC
Common
InfiniBand
iWARP
Key
InfiniBand HCA
iWARP R-NIC
Hardware
Specific Driver
Hardware Specific
Driver
Connection Manager
MAD
InfiniBand OpenFabrics Kernel Level Verbs / API iWARP
SA Client
Connection
Manager
Connection Manager
Abstraction (CMA)
InfiniBand OpenFabrics User Level Verbs / API iWARP
SDP
IPoIB
SRP
iSER
RDS
SDP Lib
User Level MAD API
Open SM
Diag
Tools
Hardware
Provider
Mid-Layer
Upper Layer Protocol
User APIs
Kernel Space
User Space
NFS-RDMA
RPC
Cluster
File Sys
Application Level
SMA
Clustered
DB Access
Sockets
Based Access
Various
MPIs
Access to
File
Systems
Block
Storage
Access
IP Based
App
Access
Apps & Access Methods for using OF Stack
UDAPL
Kernel bypass
Kernel bypass

## Slide 7
OFED 1.0 and 1.1 Contents
SA | Subnet Administrator
MAD | Management Datagram
SMA | Subnet Manager Agent
PMA | Performance Manager Agent
IPoIB | IP over InfiniBand
SDP | Sockets Direct Protocol
SRP | SCSI RDMA Protocol (Initiator)
iSER | iSCSI RDMA Protocol (Initiator)
RDS | Reliable Datagram Service
UDAPL | User Direct Access Programming Lib
HCA | Host Channel Adapter
R-NIC | RDMA NIC
Common
InfiniBand
iWARP
Key
IBM HCA
Hardware
Specific Driver
Connection Manager
MAD
InfiniBand OpenFabrics Kernel Level Verbs / API
SA Client
Connection Manager
Abstraction (CMA)
InfiniBand OpenFabrics User Level Verbs / API
SDP
IPoIB
SRP
iSER
SDP Lib
User Level MAD API
Open SM
Diag
Tools
Hardware
Provider
Mid-Layer
Upper Layer Protocol
User APIs
Kernel Space
User Space
Application Level
SMA
Various
MPIs
Apps & Access Methods for using OF Stack
UDAPL
Kernel bypass
Block
Storage
Access
Sockets
Based Access
IP Based
App
Access
Mellanox HCA
Hardware
Specific Driver
QLogic HCA
Hardware
Specific Driver
RDS

## Slide 8: OFED v1.1 Enhancements (1 of 3)
Component/Platform | OFED 1.1 enhancements
OS support (kernel 2.6.17) | SLES 9 SP3, SLES 10, RHEL 4 U3 and U4
CPU support | x86_64, x86, IA64, PPC64
32 bit libraries | For x86_64 and PPC64
Drivers/HCAs | IBM, Mellanox, QLogic
Verbs | Kernel hot plug support in uverbs

## Slide 9: OFED v1.1 Enhancements (2 of 3)
Component/Platform | OFED 1.1 enhancements
Open SM | Partition manager, pre-computed routing load
IPoIB | High availability (HA) using user level daemon
SRP | Stability fixes, HA with DM, MPP, XVM
iSER | Stability, performance, PPC64 and IA64 support
UDAPL | Scalability for Intel MPI

## Slide 10: OFED v1.1 Enhancements (3 of 3)
Component/Platform | OFED 1.1 enhancements
OSU MPI | Message rate improvements
Open MPI | http://svn.open-mpi.org/svn/ompi/trunk/NEWS
MPI tests/ benchmarks | Intel Pallas, Presta, OSU (new versions)
SDP | Improved BW, latency, stability, OOB Snd/Rcv
Tools | SA Query, Grouping in IB Net Discover, IB Utilities (Port error/performance counters check/dump, Link width and link speed check by flag), Mad Eye

## Slide 11: OFED v1.1 Status
RC6 regression testing in progress
Release imminent – End of Sep 06
To be used for OFA Interoperability Event at UNH (week of Oct 9th)
Process improvement discussions / post mortem planned after release
SLES and RHEL updates with OFED 1.1

## Slide 12: OFED Futures
High availability improvements: IPoIB, SRP
Performance, scalability improvements: IPoIB, SDP, MPI
Oracle open source RDS
Quality of service
iWARP integration
NFS-RDMA client
OFED for Windows
Please send feature requirements to openfabrics-ewg@openib.org

## Slide 13: Call to Action
InfiniBand suppliers:
  Make OFED part of your core offering
  Drive “enterprise readiness”
  Drive full interoperability and help accelerate standardization
iWARP suppliers:
  Join OFA, open source your drivers and integrate with OF S/W
OS Vendors:
  Thanks for adopting, please upgrade with new OFED releases
ISVs and End-users:
  Please provide feedback on what is lacking
  Discourage proprietary stacks – let’s move quickly toward standardized RDMA stacks

## Slide 14
Questions?