## Slide 1: iSER Support Annex
Arkady Kanevsky, Ph.D.
IBTA SWG
San Francisco
September 25, 2006

## Slide 2: Why?
Provide an option to support iSER on IB!
IBTA support for iSCSI extension for RDMA
  IETF draft http://www.ietf.org/internet-drafts/draft-ietf-ips-iser-05.txt
  Enable RDMA Read and Write to be used to transfer SCSI I/O data
IETF draft requires features that are optional in IBTA standard
  Zero-Based Virtual Address (ZBVA)
  Send with Invalidate
What to do when optional semantics not supported?

## Slide 3: How?
Protocol to negotiate IBTA optional iSER functionality during IBTA connection setup
  iSER Initiator advertises its capabilities for optional functionality in CM REQ that iSER expects
  iSER Target responds with CM REP stating which optional functionality it will use
iSER extension header for VA
Use RDMA IP CM Service for iSER connection establishment
  Source IP address and IP port shall be filled by privileged kernel mode. Privileged Q-key is 0x80010000 (to prevent spoofing).
  Target first checks IB and IP connection information correctness
    If destination does not support iSER, IP protocol, or destination port – generate CM REJ with Invalid Service ID (reason)
      Initiator can attempt to use iSCSI over IPoIB

## Slide 4: iSER Service ID format
Byte Location | Description | Value
0-4 | Service ID for an RDMA-Aware ULP | 0x0000000001
5 | IP Protocol Number | 0x06 (TCP)
6-7 | Destination IP port number | Existing values used for iSCSI/iSER

## Slide 5: iSER CM REQ Message Private Data Format
Byte | Bit | Description | Value
0-35 |  | CM REQ Message Extension | Defined by RDMA IP CM Service Annex
36-39 | 31 | Zero-Based Virtual Address Exception | 0 – Initiator supports ZBVA 1 – Initiator does not support ZBVA
 | 30 | Send with Invalidate Exception | 0 – Initiator supports Send with Invalidate 1- Initiator does not support Send with Invalidate
 | 29-0 | reserved | Set to 0 on iSER Initiator side and ignored by iSER Target side
40-91 |  | reserved | Set to 0 on iSER Initiator side and ignored by iSER Target side

## Slide 6: iSER CM REP Message Private Data Format
Byte | Bit | Description | Value
0-3 | 31 | Zero-Based Virtual Address Exception | 0 – Initiator shall use ZBVA 1 – Initiator shall use VA
 | 30 | Send with Invalidate Exception | 0 – Target will use Send with Invalidate 1- Target will use Send and NOT send with Invalidate
 | 29-0 | reserved | Set to 0 on iSER Target side and ignored by iSER Initiator side

## Slide 7: iSER Connection establishment - Extras
iSER Connection establishment - Extras
  After IB connection establishment do iSCSI login exchanges
    Negotiate RDMAExtension to Yes
  Use IB CM negotiated RDMA Read Responder Resources and Initiator Depth for negotiating iSER RDMA parameters
iSER protocol extension to handle lack of optional semantic
  If either side does not support Send with Invalidate then only Send will be used
    Up to the Initiator to invalidate STag(s) (R-key)
  If either side does not support ZBVA then VA will be used instead
    Extended iSER header for VA to be used by both iSER Initiator and Target

## Slide 8: Extension iSER Header for VA support
Byte | Bit | Name | Value
0-3 | 31-28 | Operation code | 0x1 – iSCSI control type PDU
 | 27 | Write STag Valid (WSV) | 0x1 – indicates that Write Stag and Write VAs are used
 | 26 | Read STag Valid (RSV) | 0x1 – indicates that Read Stag and Read VAs are used
 | 25-0 | reserved | Set to 0 on Send and ignored on Receive
4-7 | 31-0 | Write STag | Contains IB R-key for SCSI Write command when WSV is set Otherwise, set to 0 on Send and ignored on Receive
8-11 | 31-0 | Write VA high | If WSV is set contains IB VA bits 63-32 for SCSI Write Command Otherwise, set to 0 on Send and ignored on Receive
12-15 | 31-0 | Write VA low | If WSV is set contains IB VA bits 31-0 for SCSI Write Command Otherwise, set to 0 on Send and ignored on Receive
16-19 | 31-0 | Read STag | Contains IB R-key for SCSI Read command when RSV is set Otherwise, set to 0 on Send and ignored on Receive
20-23 | 31-0 | Read VA high | If RSV is set contains IB VA bits 63-32 for SCSI Read Command Otherwise, set to 0 on Send and ignored on Receive
24-27 | 31-0 | Read VA low | If RSV is set contains IB VA bits 31-0 for SCSI Read Command Otherwise, set to 0 on Send and ignored on Receive