## Slide 1: RDMA IP CM Service Annex
Arkady Kanevsky, Ph.D.
IBTA SWG
San Francisco
September 25, 2006

## Slide 2: Why?
Leveraging existing world IP Addressing infrastructure for RDMA CM
  Define mapping between TCP port space and IB Service IDs for RDMA-aware ULPs.
  RDMA-Aware ULP:
    explicitly use RDMA semantic: memory registration, preposting recv buffers, RDMA operations and so on.
    RDMA transport independent
      run on IB and iWARP without transport dependent code
Provide support for a socket-like connection model for RDMA-aware ULPs:
  IB Consumer use the socket 5-tuple for connection establishment
    IP protocol number
    source IP
    source port
    destination IP
    destination port

## Slide 3: How?
RDMA IP CM Service is a layer above IBTA CM
RDMA IP CM Service Annex defines a protocol:
  RDMA IP CM Service uses IBTA CM REQ private data:
    Source and destinations IP addresses
    Source Port
  IP protocol ports mapping into IBTA Service IDs
    maps IP protocol number and destination IP port into IBTA Service IDs
  Reserves a range of IBTA service IDs for RDMA IP CM Service

## Slide 4: CM REQ Message Private Data Format
Source IP Address (31 – 0)
Source IP Address (63 – 32)
Source IP Address (95 – 64)
Source IP Address (127 – 96)
Source Port
IP
Version
Version
Major
Consumer Private Data
Destination IP Address (31 – 0)
Destination IP Address (63 – 32)
Destination IP Address (95 – 64)
Destination IP Address (127 – 96)
reserved
Version
Minor
3 2 1 0
1 0 9 8 7 6 5 4 3 2 1 0 9 8 7 6 5 4 3 2 1 0 9 8 7 6 5 4 3 2 1 0
Bytes
4-7
0-3
12-15
8-11
20-23
16-19
24-27
36-91
28-31
32-35
See next slide for dest SID which encodes dest port number and protocol

## Slide 5: RDMA IP CM Service IBTA SID format
SID range indicates that private data is formatted
API or verbs that use IETF addressing indicate that IETF protocol # and port are mapped into IB SID
Byte Location | Description | Value
0 | IBTA AGN | 0x00
1-3 | Prefix of RDMA-aware SID range | Each byte 0x00
4 | RDMA-aware ULP SID range | 0x01
5 | IP Protocol Number | See IANA
6-7 | Destination IP port number | ULP well-known port number

## Slide 6: Error Handling - I
Byte Location | Description | Value
0 | Rejection Layer | 0x00 – RDMA IP CM Serv. 0x01 – RDMA-Aware ULP
1-71 | Layer ARI | (see table below for RDMA IP CM Service)
Byte Location | Description | Value
0 | Rejection Layer | 0x00 – RDMA IP CM Service
1 | RDMA IP CM Service layer ARI | (next table)
2 | Suggest value length in bytes | 0x00 – no suggested value X – suggested value
3 | Alignment filler | reserved
4-71 | Suggested value | undefined
RDMA IP CM Service Error Format

## Slide 7: Error Handling – II RDMA IP CM Service layer ARI codes
ARI code | Name | Description
0x00 | Unspecified | Unspecified reason for RDMA IP CM Service rejection
0x01 | Major Version | Specified major version not supported by remote side
0x02 | Minor Version | Specified minor version not supported by remote side
0x03 | IP version | IP version not supported
0x04 | Source IP Address | Format of source IP address does not match IP version
0x05 | Destination IP Address | Format of destination IP address does not match IP version
0x06 | Unknown IP Address | Destination IP address does not match Server IP address

## Slide 8: Backup

## Slide 9: How?
Standard IBTA CM REQ with private data format extension
  CM REQ provides IP address and port (analog) of the requestor, and IP address of the destination
    TCP Port of the destination is available from receiver Service ID
  Use SID range to identify that private data is formatted
Maximize Consumer-usable private data

## Slide 10: Why do we support IETF Protocol number?
Since IETF post spaces are independently managed based on protocol number it is better to support it to avoid issues in the future when RDMA will be defined/used over non-TCP protocol
Protocol # is in SID – to maximize Consumer Private Data
Clean and complete IETF 5-tuple support

## Slide 11: Why do we need to pass Destination Port?
CM can do the mapping between Service IDs and ports to provide Destination Port to a Responder.
  The conversion is an API issue is outside the scope of the spec
    The same is true for populating Private Data CM formatted fields.
  IBTA does not define CM verbs.

## Slide 12: How to handle the use of IP addresses reserved for privileged/kernel users?
Not an issue since CM REQ message privileged Q-key is setup by CM appropriately. IBTA spec already covers it.
  provided by IB security model

## Slide 13: Alignments
64 bit IP addresses alignment
private data starts at 140 byte
  IP addresses start at 144 byte
  This is 8 byte aligned
IP addresses are 8 byte aligned

## Slide 14: Relationship to CM APM Support
CM connection stays the same under Alternative Path Migration
  Design does not provide separate IP addresses for Alternative Path