## Slide 1: iSER update
2014 OFA Developer Workshop
Sunday, March 30 - Wednesday, April 2, 2014
Monterey CA
Eyal Salomon
Mellanox Technologies

## Slide 2: Agenda
iSER Advantages and Status
Support for new targets
  LIO, SCST, TGT enhancements
Initiator features and updates
  Linux, VMware
  Performance acceleration: iSER-BD and Block MultiQ
iSER in OpenStack (Cinder)

## Slide 3: iSER Advantages and Status
Advantages
  Enterprise Storage Solution (Security, HA, Discovery, ..)
  OS tools and integration based on iSCSI
  Ethernet (RoCE, iWarp) + InfiniBand
  faster than SRP (on IOPs & Latency)
Status and Adoption
  In the kernel for few years, and constantly improving
  Seamless integration into OpenStack (from Havana)
  Adopted by many cloud providers
  Will be available from multiple Tier1-2 storage vendors in the coming months

## Slide 4: Storage Targets Support
 | SRP | iSER | FCoE (Mlnx)
SCST (Kernel, external) | Yes | Yes | No
TGTD (User) | No | Yes | No
LIO (Kernel, inbox) | Yes | Yes | In-progress
GPL free, standalone reference (for storage OEMs and other OSes) | No, can base on SCST | Yes (can be obtained from Mellanox) | No, can base on LIO

## Slide 5: LIO iSER
iSER available from kernel 3.10
T10-DIF
  Implemented T10-DIF framework in target core
  Implemented for iSER – fully offloading transport
    Can do ADD/STRIP/PASS and verify of T10-DIF info
  Implemented for File backing store
    Can keep DIF interleaved in the data file (so one file has it all)
    Can keep DIF in separate file (so data file stays clean with data only)
    Good for development & debug (can inject errors…)
working on performance optimizations

## Slide 6: SCST
SCST: A leading Linux target implementation
iSCSI in SCST extended to support RDMA transport as well as TCP
Transport API to abstract away from transport implementation
High IOPs and bandwidth
Supports Infiniband, RoCE and iWARP
Available at http://scst.sourceforge.net/target_iser.html

## Slide 7: Example Linux SCST Target Transport Comparison
Single Initiator to Single Target
Using HP DL380 with 2 x Intel 2650 CPUs
ConnectX-3 Adapter (40GbE or IB FDR)

## Slide 8: TGT iSER features
sophisticated polling strategies to maximize IOPS
support iSCSI Discovery over iser
usage of Huge pages to minimize HCA cache misses
support multiple instances for IOPS scalability
  support larger IO queue depth
  Configurable memory buffer
  Configurable CQ affinity

## Slide 9: Initiator recent features
Linux
  ability to work in a VM over SRIOV VF
  support fast registration (FRWR)
  support iSCSI Discovery over iser
  optimized fast-path locking scheme in libiscsi
  support larger IO queue depth
  support SCSI T10 signature/protection
  misc stability fixes
VMware ESX
  iSER integrated into ESX 5.1/5.5 as an iSCSI HW offload
  Work on native port to ESX 6 kernel

## Slide 10: Accelerating IO Performance (Accessing a Single LUN)

## Slide 11: Accelerating IO Performance (Accessing 4 LUN in parallel)

## Slide 12: MultiQ
The iSER initiator exposes a SCSI Block device to the OS
Both the Block and SCSI layers are performance bottlenecks e.g. for IOPS scalability
in Linux 3.13 BLK-MQ was introduced to the block layer for generic block devices
SCSI MQ is under the works by the community and iSER is planned to leverage on that
The results in the previous slides were obtained by a prototype that emulated BLK/SCSI MQ

## Slide 13: iSER in OpenStack
Using OpenStack Built-in components and management (Open-iSCSI, tgt target, Cinder), no additional software is required, RDMA is already inbox and used by our OpenStack customers !
Mellanox enable faster performance, with much lower CPU%
Next step is to bypass Hypervisor layers, and add NAS & Object storage

## Slide 14: Thank You