## Slide 1: Management Scalability
Author: Todd Rimmer
Date: April 2014

## Slide 2: Agenda
Projected HPC Scalability Requirements
Key Challenges
  Path Record
  IPoIB
  Mgmt Security
  Partitioning
  Multicast
  Notices
  SA interaction
Call to Action

## Slide 3: Projected HPC Scalability Requirements
Perf increase 2x/year
Rapidly increasing node counts
  HPC and Cloud
Due to slower pace of interconnect speed growth
  need multi-rail clusters
  HCA counts will grow even faster
Chart: Time
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
#1 Traditional CPU chips | 64150 | 64150 | 85533 | 128300 | 205280 | 342133 | 586514
#10 Traditional CPUs | 20415 | 20415 | 27220 | 40830 | 65328 | 108880 | 186651
#1 Many Core CPUs | 12830 | 19245 | 19245 | 25660 | 38490 | 61584 | 102640
#10 Many Core CPUs | 4083 | 6125 | 6125 | 8166 | 12249 | 19598 | 32664

## Slide 4: Key Mgmt Scalability Bottlenecks
PathRecord Query
IPoIB ARP

## Slide 5: PathRecord Query Today
User apps
  Use rdma CM
    ibacm optional cache
  Use libumad and hand craft
  Use UD QPs
  Hand build PR (MPIs)
  Other (via IPoIB …)
Kernel ULPs
  Call ib_sa
No single place to put PR optimizations

## Slide 6: PathRecord Query Scalability
Need to 1st standardize a user space API
  Libfabrics (OFI WG) and RDMA CM are logical choices
Use API in all ULPs, benchmarks, demos, tools, diagnostics, etc.
  Both kernel and user space
  So everyone benefits from scalability improvements
Decouple API from IPoIB
  Multi rail clusters may not want IPoIB on all rails

## Slide 7: PathRecord Query
Need a plugin architecture behind the API
Need a variety of plugins
  Small clusters can do direct PathRecord query
  Modest clusters can do PathRecord caching
  Large clusters need PathRecord replicas or ibssa
  Huge clusters need algorithmic approaches
    Topology dependent optimizations
  Permit research and experimentation
Start with direct, ibssa and cached plugin
One size does not fit everyone

## Slide 8: IPoIB ARP Scalability
Need a multi-tiered approach in IPoIB
  Modest clusters can do standard ARP/broadcast
    Perhaps with long ARP timeouts (hours, days)
  Large clusters need pre-loaded ARP tables
  Huge clusters need algorithmic approaches
    Topology dependent
Need to 1st standardize a plug-in API
API needs to tie into PathRecord Plug-In
Implement std ARP and pre-loaded plugins 1st

## Slide 9: Other Mgmt Issues
Umad security
Partitioning
Multicast
Notices
SA interaction pacing

## Slide 10: Mgmt Security
Umad security issues
  Requires root access by default
  Use of umad by applications forces opening security
  Umad is too easy a vehicle to attack server or cluster
First steps
  Rapidly move applications away from using umad
  Simplify API, remove apps hand building packets
    Multicast membership, Notices, etc
  Remove need for SM and diagnostics to be root
    Need ability for secured umad use

## Slide 11: Partitioning
Proper Operation will be necessary for HPC Cloud
Don’t assume full membership in default partition
  Carefully reading of IBTA 1.2.1 reveals:
  Default partition is just a power on default, not a guarantee
  If it was a guarantee, IBTA partitioning would be useless
    everyone could use 0xffff to talk to anyone
  Only guarantee is membership in 0x7fff to permit SA query
Fix P_Key assumptions in SA queries, ibacm, tools, etc
  Proper use of PathRecord query will solve most of this
  Search local P_Key table to decide if 0x7fff or 0xffff present
IPoIB react to P_Key table changes during Port Initialize
  especially entry 0
PKey indexes can change between boot and port Active
Part A
Part B
Part C
0x7fff Part

## Slide 12: Multicast
Multicast in IBTA
  Each node can join/leave a group only once
  Multicast join/leave are for whole node
Multicast use goes beyond just IPoIB
  ibacm, MPI collectives, kernel bypass for FSI
  RDMA CM has some APIs, needs to coordinate w/kernel
Need API w/kernel muxing of multicast membership
  IBTA compliant node level interactions with SM/SA
  Allow multiple processes, kernel and user to join a group
  Automated cleanup when processes die
  Also removes another need for umad access by apps

## Slide 13: Notices
Use of Notices by applications is scalability issue
  Can force O(N) messages from SM on each event
  Example: turn off 100 nodes in 10K fabric -> 1M notices
  Example: turn off 50K nodes in 100K fabric -> 2.5B notices
At host need Notice muxing
  Each node register/receive/deregister only once
  Need kernel muxing of notice registration
  Need kernel muxing of notice delivery/ack
  Need cleanup when processes die
  Also removes another need to umad access by applications
Should we restrict or disable use of notices?

## Slide 14: SA Interaction Scalability
Centralization of PR, Multicast and Notices is 1st step
This then permits tuning of SA interactions based on scale
SA Response Timeout/Retry Handling
  Clients today use fixed timeouts
  Timeouts chosen a priori without knowledge of SA nor fabric load
Need centralized config of timeouts and retry settings
  As opposed to per application constants
Retries should perform non-linear backoff
SA Busy Response Handling
  Present OFA code does immediate retry
  Prevents SA from using BUSY to pace its workload
  SA forced to discard
BUSY should cause client backoff before attempting retry
  Non-linear backoff also recommended

## Slide 15: Next Steps
Lets all collaborate to solve these challenges
Your participation in discussion is encouraged
Lets be committed to solving these long standing issues

## Slide 16: Summary
Cluster sizes will grow year over year
OFA has some long standing scalability issues
Solutions are possible
Lets all commit to making it happen

## Slide 17: Thank You