## Slide 1: QoS Update and Implementation RFC
Eitan Zahavi,
Mellanox Technologies
Nov 2006
Notes: <number>

## Slide 2: IBTA QoS Annex Update
2/7/06
Mellanox Technologies – Developers Summit @ SC06
Page <number>
Client
CMA/ CM
SM/SA
QM
Draft annex is in LWG final review
    ETA IBTA 1.2.1 release Q1 2007
QoS enforcement by Client to QM negotiation
The main mechanism is for QM to hide behind SA PathRecord
PathRecord

## Slide 3: IBTA QoS Annex Details
QoS PathRecord/MultiPathRecord:
  Additional query fields
    [Type, TClass]: requested priority (if the client knows)
      Type == 0 means TClass is DSCP
    ServiceID (same as the one used in CM REQ)
  Additional response fields
    Response status: granted or failed due to policy
2/7/06
Mellanox Technologies – Developers Summit @ SC06
Page <number>

## Slide 4: IPoIB QoS Support
Available today (OFED 1.1)
Specified by IETF IPoIB RFC: 4391/4392
QoS is assigned by SM per IPoIB subnet
  IPoIB Subnet = P_Key
IPoIB uses broadcast group parameters for UDAV
  SL, MTU, RATE, TClass
2/7/06
Mellanox Technologies – Developers Summit @ SC06
Page <number>

## Slide 5: CMA Enhancements
Query SA for QoS capability
  SA ClassPortInfo.CapabilityMask.IsQoSSupported
Fill in QoS fields in PathRecord
  ServiceID – available today
    Given as rdma_resolve_addr args: dst_addr.sin_port, id.ps
  TClass – if optionally provided
    As (sockaddr_in6*)&dst_addr->tclass
Handle error code in case path is not granted
2/7/06
Mellanox Technologies – Developers Summit @ SC06
Page <number>

## Slide 6: ULP Enhancements
ULPs using CMA already handled
  SDP, iSER, RDS
ULPs owning their CM sequence
  SRP, MPI, …
  Fill in the ULP specific ServiceID
  Fill in DSCP if specific one is defined in TClass
    Configuration is ULP specific
2/7/06
Mellanox Technologies – Developers Summit @ SC06
Page <number>

## Slide 7: OpenSM Enhancements
Implement integrated “Passive QM”
Support QoS Policy
  Node groups
  Fabric setup rules
  Matching rule setup
Perform Fabric Setup
  Validate requested policy is realizable
  Optimize setup runtime
Match incoming PathRecord/MultiPathRecord
  Match against predefined QoS levels
  Provide back QoS level: SL, LID, MTU, RATE
2/7/06
Mellanox Technologies – Developers Summit @ SC06
Page <number>