## Slide 1
VNIC
OpenFabrics Developers Summit SC06
Ramachandra Kuchimanchi
Qlogic Corporation
Presented by: Madhu Lakshmanan, Qlogic Corporation

## Slide 2
VNIC – Ethernet Virtual I/O Controller Device Driver
Supports QLogic Virtual Ethernet I/O Controllers
  VEx (1GE), EVIC (10GE) and IBM Blade Center cards
  Existing Customer installations since 2002
VNIC is device driver for Virtual I/O Controller (VIC) card
VIC card presented as true Ethernet NIC via VNIC driver
  IB treated as an IO bus path from Host to VIC
  Full Ethernet NIC semantics
  VIC is a remote fabric device

## Slide 3
Q05
VEx – Basics of operation
LAN
VEx
IB Link
Ethernet Link
veth0
Load VNIC driver

## Slide 4: The VNIC driver
  The VNIC driver runs on the host as a Linux Kernel module
  It provides a standard Ethernet interface to the system
  It communicates with the VIC card via IB
    Control and Ethernet data transfered via IB “bus”

## Slide 5: VNIC – Operation (on OFED)
  User loads the VNIC kernel driver
  User runs a tool to discover VIC controllers available on the fabric
  User creates a virtual Ethernet interface using the driver by specifying a target VIC Ethernet port
  User can configure the virtual Ethernet interface like any other interface
    ifconfig, vconfig for VLANs, etc
    Supports any ethernet protocol: IPv4, IPv6, netware, custom ...
  The virtual Ethernet interface operates normally like any other interface
    ping, ssh, scp, netperf etc

## Slide 6: VNIC driver - Design

## Slide 7: Concluding Remarks
VNIC software undergoing extensive Beta testing
Targeted for inclusion in the OFED 1.2 release
Targeting Linux kernel version 2.6.20 or later for inclusion
Ready for inclusion into any OFED 1.1.x release