## Slide 1: Core Changes
Tom Tucker

## Slide 2: Optional Feature Support
Goals
  Consistent, well understood mechanisms
  Application can run on any device and transport
  Application can take advantage of transport and/or vendor optimizations
  Capabilities queried at run-time, not discovered by trial and error.

## Slide 3: Optional Feature Support
Mechanisms
  Bit fields in a capabilities mask
  Function pointers (potentially null) in the device function table
Bit fields used to indicate whether a particular feature implemented as an SQ WR is present, e.g.:
  Invalidate STag
  Bind Memory Window
  RDMA Read and Invalidate
  RDMA Write with Immediate
Function Pointers used for features implemented as Verbs, e.g.:
  Create Memory Window

## Slide 4: Expanded Device Attributes
Not all relevant device attributes are exported currently, for example:
  RDMA_READ SGE limit
  DMA_MR size limit
These attributes need to be added to the device attributes structure
Namespace cleanup
  Consistent naming of min/max
  More descriptive names

## Slide 5: New iWARP CM Features
Native stack port space integration
  TCP ports consumed by native stack will be seen by the iWARP CM and vice versa
IRD/ORD Negotiation
  RDMA Read inbound and outbound limits exchanged in private data at connection establishment -- needs IETF changes
  Option #1
    Best-can-do approach implemented with conn_req parameters.
  Option 2#
    CM events expanded to included peer’s advertised limits
    conn_req parameters are absolutes and connect/accept fails if they can’t be honored

## Slide 6: CM Continued
Streaming mode connection establishment
  llp_listen, llp_connect, llp_accept, llp_send, llp_recv (needed for iSER spec. compliance)
Socket migration
  rdma_create_from_fd - returns bound rdma_cm_id from socket

## Slide 7: API Next
User-mode only
ibv_  rdma_ for all data types and verbs
Needs wider review, discussion

## Slide 8: RDMA System Management
iWARP is not an IP protocol so it shares the TCP port space like imap, or http
Users need the ability to specify when to use RDMA vs. TCP for multi-transport services
Proposal
  Use /etc/services, portmapper
  IETF proposal for RDMA services names and port numbers, e.g. “rnfs”

## Slide 9: Help!
Adapter Vendor Participation
  You should contribute more than just your device driver
$$$$
  We feed our engineers under the door, but their kids at home eat too
Warm bodies
  If you interested, let us know. There’s plenty to do…

## Slide 10: Questions?