## Slide 1
SRP
OpenFabrics Developers Summit SC06
Presented by: Madhu Lakshmanan, QLogic Corportation
On behalf of: Ishai Rabinovitz, Mellanox Technologies
Roland Dreier, Cisco Systems, Inc.
Madhu Lakshmanan, QLogic Corporation

## Slide 2
SRP – SCSI RDMA Protocol
Published T10 standard for SCSI over RDMA transport – supported version SRP v2 r00a
The SRP Initiator currently supports:
Basic SCSI Primary Commands -3 (SPC-3) r21b
Basic SCSI Block Commands -2 (SBC-2) r16
  Basic functionalities, task management and limited error handling

## Slide 3
SRP – Basics of operation
Transport SCSI commands/responses over RDMA channel
Data movement done via RDMA operations initiated by target
OpenIB SRP initiator in Linux kernel 2.6.15 and onwards
Target discovery done in userspace – ibsrpdm or srp_daemon

## Slide 4
SRP – Supported targets
SRP has been tested and verified with the following targets
  Cisco SFS 3000 InfiniBand-to-Fibre Channel Gateway Module
  Mellanox SRP target - reference implementation development platform MTD1000/MTD2000
  QLogic Fibre Channel Virtual I/O Controller (VFx, FVIC)
  Engenio 6498 controller and storage system
The above SRP targets attach to a wide variety of industry standard storage devices

## Slide 5: SRP High Availability (SRP HA)
Ishai Rabinovitz,
Mellanox Technologies
Nov 2006
Notes: <number>

## Slide 6: SRP without HA
Assuming there are two physical paths from port A to port B
If there is a fail in the path
  SRP switches to the second path (After SM reroute the fabric)
If A or B fails
  there is no failover
Init.
Tar.
A
B

## Slide 7: SRP HA
  There are multiple paths (thru multiple ports/HCAs)
  When A or B fails, there is no path from A to B
    SRP HA automatically switches to another path using other port(s)/HCA(s)
Init.
Target
Switching fabric
Init.
A
C
B
D
Notes: 1) To explain that in this example there are 4 different paths between each initiator and target.

## Slide 8: HA stucture
HA is build of two parts:
  Srp_daemon – Discovers and sets up connections for all possible paths to SRP targets on the fabric
  Multipath tool – Switches to a different path when a path fails. Current version uses Device Mapper multipath
Notes: Need to say that by all possible paths we mean paths according to current SM routing

## Slide 9: srp_daemon
Based on ibsrpdm
Behavior:
  On boot scans the fabric and sets up connection for all possible paths to SRP targets on the fabric
  Continue to monitor the fabric, and sets up connection to new SRP targets that joins the fabric.
Has more features (Details in man page)

## Slide 10: Device Mapper (DM) multipath
Device Mapper (DM) driver is in vanilla linux kernel tree.
dm-multipath + udev provide persistent binding and HA
dm-multipath identifies different paths to the same device and group them together.
  Uses the device scsi_id – a unique identifier for each SCSI devic.
Notes: The explain that this is one possible multipath tool (There are also MPP and XVM)

## Slide 11: DM-multipath (cont)
Behavior:
  DM-multipath operates on active-passive mode
    ie. there should be at most one active path to access a lun.
  When the current active path fails,
    dm-multipath switches to the next passive path in its list
  When the first path resumes
    dm-multipath fails back to it.
It is possible to tune dm-multipath to use different paths for different devices gaining some load balancing.

## Slide 12: Issues
Need to set the initiator extension
  2 connections between Target and Initiator.
  SRP Target_port is the same on both paths.
  Need to have different initiator extensions depending on the Target port.
  Convention:
    Using the target port guid as the initiator extension
    Convention can be overridden by the user
Initiator
Target
Notes: Otherwise the target think that both connection are the same and they can not co-exist.
It starts a ping-pong between them (Connecting one and disconnecting the second)

## Slide 13: Issues (2)
There is no SRP HA support for RHEL4.
  The reason: RHEL4 does not support DM-multipath
    one of DM-multipath prerequisites is udev version > 050
    RHEL4 has udev 039
    Dm-multipath and our solution uses the “RUN+=“ option of udev that is not supported in early versions of udev

## Slide 14: Future plans
Support Engenio's MultiPath Proxy Driver (MPP)
  MPP is Engenio's proprietary multipath solution which only work with Engenio storage
  Supports also fail-over/fail-back between two target controllers, working with Engenio's out-of-band storage management tool.
Qualify SRP HA from Beta to GA
Try to migrate DM-multipath solution to Red-Hat
Improve error handling and recovery
Add support for hot-swappable SRP targets