## Slide 1: IPoIB Update
Michael Tsirkin, Eli Cohen, Roland Drier, Eitan Zahavi
Nov 2006
Notes: <number>

## Slide 2: What is NAPI ?
  Alternatively switch from interrupt driven mode to polling mode.
    Driver: First interrupt switches to polling mode
      Interrupts are disabled.
      Register with NAPI for polls
    NAPI: calls device driver for polling for incoming packets
      Up to a predefined quota
      TX interrupts are optionally handled here as well.
      This is done in the same kernel thread the IP layer uses
    Driver: when quota is finished or nothing more to poll, switch back to interrupt mode
2/7/06
Mellanox Technologies – Developers Summit @ SC06
Page <number>

## Slide 3: IPoIB NAPI
  Best utilized at high packets rate
  Provides higher bandwidth
  Does not hurt latency
  Better CPU usage
  Interrupt rate significantly reduced
    Less CPU time is wasted on context switch
  Roland’s implementation went upstream
2/7/06
Mellanox Technologies – Developers Summit @ SC06
Page <number>
Notes: <number>

## Slide 4: NAPI Performance
2/7/06
Mellanox Technologies – Developers Summit @ SC06
Page <number>
Notes: Conditions:4 parallel netperf, TCP_STREAM, MSIX, 2.6.17.1, 8 Intel core 2.4GHz, 4xDDR MT25204
<number>

## Slide 5: IPoIB CM - Roadmap
Specification available as IETF draft
Initial implementation show > 800MB/sec
First implementation
  A new network interface
  Supports unicast only and does not fallback
  Available by 1 Jan 07
Production implementation
  Single interface that handles IPoIB (CM with fallback)
  Available 1Q 07 (with higher risk)
2/7/06
Mellanox Technologies – Developers Summit @ SC06
Page <number>
Notes: Learn about how Netstat is implemented
<number>

## Slide 6: IPoIB CM - Challenges
Path based MTU
  Different targets might require a different MTU
    Multicast or just legacy IPoIB
  Solution space:
    Enhance Linux to obtain path MTU from neighbor
    Rely on Path MTU discovery – not clear if feasible
    Perform packet fragmentation
SRQ for UC
  Not in IBTA spec
  Solution space
    Use RC
    Specify and implement
2/7/06
Mellanox Technologies – Developers Summit @ SC06
Page <number>
Notes: Learn about how Netstat is implemented
<number>