## Slide 1: Windows OpenFabrics (WinOF) Update
Gilad Shainer, Mellanox Technologies
November 2007

## Slide 2: Windows OpenFabrics (WinOF)
Collaborative effort to develop, test & release OFA software for Windows
Components – Kernel & User Space
Broader test participation
Add-on components for vendors to differentiate above WinOF

## Slide 3: Supported Platforms
Architectures
  x86, x86_64, IA64
Operating systems
  Windows XP 32&64
  Windows Server 2003
  Windows Cluster Compute Server 2003
  Windows HPC Server 2008*
WHQL’ed
  Windows Server 2003
  Windows Cluster Compute Server 2003

## Slide 4: WinOF Software Stack
Embedded
Legacy
Storage
Fabric management
Data center
HPC
HPC (MPI)
Video, medical, communication
IP/LAN
Block Storage
IB admin tools
Database
App tier
MPI 2
OpenSM
uDAPL
WSD
SDP
Kernel
Kernel API
User
WinSock Direct Socket Switch
TCP
UDP
IP
NDIS
SRP Initiator
ICMP
SCSI Mid layer
User access layer
User access layer
HCA Low Level Driver
HCA Hardware
Markets
Applications
Windows server 2003 CCS
WinOF
Kernel bypass
Windows server 2003
InfiniBand Fabric
Access Layer
MPI
IPoIB

## Slide 5: WinOF 1.0.1 Components
HCA Drivers
  MTHCA (Mellanox)
Access Layer (IBAL)
NDIS 5.1 (IPoIB)
WSD provider *
SRP initiator **
uDAPL
OpenSM
VNIC
MSI installer
Tools
  Verbs perf Benchmarks
  FW update tools
  More
MPI Components
  Microsoft CCS
  Intel
  HP
SDP
Cluster management
CORE
ADD-ONs
Components supported by individual vendors may vary
* Not available on Windows XP
** Not available on Windows XP 32 bit

## Slide 6: SDP
Requires license
Plan to have binary version available in WinOF 1.0
Alpha level
Currently BCopy only, limited set of API

## Slide 7: Microsoft WHQL
Microsoft qualification program
WHQL can be obtained only by IHV
  Can not get WinOF qualified
IB WHQL includes IPoIB and WSD
  Low level drivers and hardware
WinOF 1.0 - WHQL version

## Slide 8: WinOF Application Performance
Notes: <number>

## Slide 9: Futures
WinOF 1.1 planed for March-April 2008
  ConnectX support
  Windows Server 2008
  Windows HPC Server 2008
Includes NetworkDirect component
  Performance optimization Windows HPC 2008
Windows Server 2008 WHQL

## Slide 10: Windows HPC Server 2008
<number>
Maximizing InfiniBand Features For Latency
Notes: <number>

## Slide 11: Windows HPC Server 2008
<number>
Maximizing InfiniBand Features For HPC Application
Notes: <number>

## Slide 12
THANK YOU!