## Slide 1: IB Scalability
Sean Hefty – Intel

## Slide 2: Many-to-Many Connections
Obtain GID of remote endpoint
  RDMA CM uses ARP for address mapping
  ARP message sent over IPoIB broadcast multicast group
  IPoIB obtains path record to DGID
Obtain path record (PR) to endpoint
Exchange QP information
  3-way CM protocol

## Slide 3: Address Resolution
ARP messages are sent over IPoIB’s broadcast multicast group
  Creates ARP storm
    IPoIB starts dropping packets
  Longer time-outs and deeper queues help, some…
  E.g. 1000 nodes  1 million ARP entries fabric wide
    15 minute timeout  1000 entries timeout / second
    24 hour timeout  12 entries timeout / second

## Slide 4: Route Resolution
Obtain path record to endpoint
  Wait, didn’t IPoIB just do that?
    Yes, it did
    And the path records were cached locally
  Queries take minutes to complete
    1000 nodes hit SA with 500,000 queries
  PR caching is provided by QLogic and Cisco stacks – Voltaire?
Path record caching is critical for scalability

## Slide 5: Connection
CM message exchanges occur within seconds
Apps may be slow to respond to CM messages during processing
  MRA patch added to address this
CM protocol time is relatively small
unless using ARP and PR caching

## Slide 6: Other Issues
ARP only works within a single IP subnet
  IB routers separating IP subnets will call for a different mapping method
SA query retries use different TIDs
  Each request - response pair looks unique
Is connection scaling across subnets a requirement?

## Slide 7: Other Issues
QoS makes distributing PR data more difficult (but not impossible)
  But also increases the burden on a centralized SA
Need CM testing on larger clusters
  Discourage non-CM solutions
OFA should examine vendor/application solutions

## Slide 8: Options
Merge OFED local SA solution upstream
  Path record caching only
  Does not support QoS
  IPoIB still caches (but uses local SA)
Allow manual redirection of SM LID
  Moves local SA solution to userspace
  Enables non-local caching
Assuming most users prefer RDMA CM over IB CM

## Slide 9: Options
Define new group connection capability
  Leave existing connection model alone
  Combine address and route resolution into a single, more efficient step
    Avoid ARP storm, support multiple IP subnets?
  Need new APIs, protocols
    Interaction with job schedulers is unknown
  E.g. connect to 192.168.10.0 / 24 port 7174
Speaker is just winging it now