## Slide 1: OFED 1.3 InfiniBand Management Update
Hal Rosenstock
Notes: Hal Rosenstock <hal@xsigo.com>

## Slide 2: “Landscape” Changes
PathForward program as relates to OpenIB/OpenFabrics has completed
  Funded much of the IB management development
    Other things as well
Transition of maintainerships
  management (libraries, OpenSM, infiniband-diags)
    From me to Sasha
  ibutils
    From Eitan to Oren

## Slide 3: Kernel Related Developments
MAD module
  Switch SMI support
User MAD module
  Partition support
  Method mask workaround
    Bit ordering and 32 on 64 issue on big endian archs
Futures
  Combined route support in MAD layer
    Mainly needed for switches

## Slide 4: Core Management Libraries
libibcommon 1.0.6
libibumad 1.1.4
  Support for multiple opens
  Valgrind support
  Library is now thread safe
  Partition support
  Method mask workaround
    Bit ordering and 32 on 64 issue on big endian archs
  ABI version
    Currently 5
    Will be bumped to 6 in Sept 08
      New layout will be default
      PKey ioctl to be removed
libibmad 1.1.3
  Support for IB_DEVICE_MGMT_CLASS

## Slide 5: OpenSM for OFED 1.3
Release Info
  git://git.openfabrics.org/~ofed_1_3/management.git
  opensm-3.1.6 (OFED 1.3 Beta)
Maintainer: Sasha Khapyorsky (Voltaire)
New Functionality
Bug Fixes
Base used as core for Windows
  No word on equivalent Windows release

## Slide 6: New Functionality
Quality of service manager – experimental (Mellanox contrib)
  Based on IBTA annex
  Covered in Dror’s talk
  Summary
    QoS Policy Parser
    SA PathRecord/MultiPathRecord support
    Limited SL2VL/VLArb support
    Now qos rather than no-qos option
Performance management – experimental
  Now supports when SM not master (or no SM)
“Native” daemon mode
More performance improvements
  More routing speedups
    Min hops, up/down, LASH
    optimized port and switch tables update policy
  SA speedups
Better packaging/installation

## Slide 7: New Functionality
Unification of node name map with infiniband-diags
Routing
  Dimension order routing (SGI contrib)
  LASH performance improvement
  Some fat tree improvements
Console
  More commands added
  loopback support
Local policy support for link speed
“Babbling” ports handling
  Suppression of trap storms for non-conformant SMAs
Duplicated GUID/moved port improvements

## Slide 8: Bug Fixes (since OFED 1.2)
See OFED 1.3 OpenSM release notes for details
Also, for non compliances

## Slide 9: Upcoming (beyond OFED 1.3)
More prestandard IBA router enablement
  Static routing table needed for more flexible topologies
“Secure” OpenSM console
  work in progress at LLNL
QoS/Partitioning
  Port groups definition unification
  Port QoS setup (VLArb, SL2VL)

## Slide 10: Upcoming (beyond OFED 1.3)
Performance manager scaling
MKey manager
Mirroring support
SM Failover/Handover improvements
Routing engine chain
  opensm -R ftree –R updn -R minhops ...
NodeDescription changed trap handling
Other “Selected” IBA 1.2.1 enhancements
  Optimized SL2VLMapping ?
Better IPv6 solicited node multicast (SNM) handling
  Multiple groups share same MLID
Handle local events ?

## Slide 11: Larger Needs
Management interfaces/plugins
SM DB replication
Distributed SA
Congestion manager

## Slide 12: Diagnostics
infiniband-diags 1.3.3 (Maintainer: Sasha Khapyorsky, Voltaire)
  Now work on any CA/port
  Node name support for additional diags
  Enhancements to support routers
    scripts need more testing
  perfquery fixes/enhancements
    CapMask
    support for single port CAs without all port select support
  ibnetdiscover
    Topology output format now contains port GUIDs
    Grouping for Xsigo chassis
  set_nodedesc.sh rather than set_mthca_nodedesc.sh
ibutils 1.2 (Maintainer: Oren Kladnitsky, Mellanox)
  QoS support
  Partitioning support

## Slide 13: Upcoming for Diagnostics
Unified diag tools command line/config

## Slide 14: Related
ibsim 0.4 (Maintainer: Sasha Khapyorsky, Voltaire)
  OpenSM and infiniband-diags work unmodified with this simulator
    uses ibnetdiscover format for topology
  git://git.openfabrics.org/~sashak/ibsim.git

## Slide 15: Futures
What do you think is needed ?
What would you like to see added ?
Comments general@lists.openfabrics.org

## Slide 16
Thank You

## Slide 17
Backup

## Slide 18: IB Router Enablement
Experimental
  ROUTER_EXP not enabled in build by default
  Much of IBA missing for routers
Fix handling of router ports
Support for off subnet GIDs in SA PathRecord
Support for non link-local scope in MGID in SA MCMemberRecord

## Slide 19: Dimension Order Routing
The Dimension Order Routing algorithm is based on the Min Hop algorithm and so uses shortest paths. Instead of spreading traffic out across different paths with the same shortest distance, it chooses among the available shortest paths based on an ordering of dimensions. Each port must be consistently cabled to represent a hypercube dimension or a mesh dimension. Paths are grown from a destination back to a source using the lowest dimension (port) of available paths at each step. This provides the ordering necessary to avoid deadlock. When there are multiple links between any two switches, they still represent only one dimension and traffic is balanced across them unless port equalization is turned off. In the case of hypercubes, the same port must be used throughout the fabric to represent the hypercube dimension and match on both ends of the cable. In the case of meshes, the dimension should consistently use the same pair of ports, one port on one end of the cable, and the other port on the other end, continuing along the mesh dimension.