## Slide 1: Quality of Service Support
Dror Goldenberg - Mellanox
Sean Hefty – Intel

## Slide 2: Motivation for QoS
Network as a service
  Virtual networks over a single wire
Fabric consolidation QoS requirements
  Different classes of service
  Dynamic adjustment
  Dynamic reconfiguration
  Service Provisioning
Administrator
Storage
Net.
IPC
Gateway
Mgt.
Servers
Filer
Block Storage
InfiniBand Subnet
Logical View

## Slide 3: QoS Overview
Traffic can be divided into different classes
  Dedicated BW and latency, dedicated BW, best effort, low priority, …
Classes are assigned to high/low priority queues
  Weights are given to traffic sharing a queue
IB supports QoS through VLs and high/low priority VL arbitration

## Slide 4: Mapping to QoS
Application 
Service ID Range, SGID, DGID, PKey 
QoS, SGID, DGID, PKey 
Traffic Class, SGID, DGID, PKey 
SL, SLID, DLID, PKey 
VL, MTU, Rate, Packet Life Time, …
Communicate desired QoS to SM

## Slide 5: Host Software Support
SA Client
  Path record adds QoS and service ID fields
  Interpretation left up to SM
SRP
  Adds service ID to path record
IPoIB
  Based on global multicast group settings
  Adds traffic class to path record
SDP / iSER
  Use RDMA CM service

## Slide 6: Host Software Support
RDMA CM
  Maintains transport neutral interface
    Refers to QoS as Type of Service (ToS)
    Provide Infiniband QoS features
  IPv4 – new interface to set ToS
    Maps directly to IB QoS
  IPv6 – uses traffic class in address
  Includes service ID with IB queries
  Multicast already supports traffic class

## Slide 7: SM Configuration
Configuration options
  /etc/ofa/opensm-qos-policy.conf
  Simplified model ULP/application -> SL
  Sophisticated model
Configuration is dynamic
  SM will reconfigure when config file changes

## Slide 8: Simple SM Policy File
Simplified QoS configuration
Per ULP mapping into SL
First rule takes precedence
qos-ulps
sdp, port-num 30000 : 1
sdp, port-num 10000-20000 : 2
sdp : 0
srp, service-id 0x1234-0x1235 : 2
rds, port-num 25000 : 2
rds : 0
iser : 4
ipoib, pkey 0x0001 : 5
ipoib : 6
any, service-id 0x6234 : 2
any, pkey 0x0ABC : 3
default : 0
end-qos-ulps
* Not supported yet in OFED 1.3

## Slide 9: Configuring Port Groups
Port Groups based on
  GUID
  Node description/port
  Partition
  Type (CA/Switch/etc.)
port-groups
port-group
name: Storage
use: SRP storage targets
port-guid: 0x100000000000FFFF
end-port-group
port-group
name: Virtual Servers
use: node desc and IB port num
port-name: vs1 HCA-1/P1, vs2 HCA-1/P1
end-port-group
port-group
name: Group for Partition 1
partition: Part1
end-port-group
port-group
name: Switches and SM
node-type: SWITCH, SELF
end-port-group
end-port-groups
Port
Group
VLArb,
SL2VL
QoS
Level
Policy

## Slide 10: Configuring SL and VL Tables
SL/VL Table Configuration
  SL to VL mapping
  VL arbitration tables
# QoS default options
qos_max_vls 15
qos_high_limit 0
qos_vlarb_high 0:4,1:0,2:0,3:0,4:0,5:0,6:0,7:0,8:0,9:0,10:0,11:0,12:0,13:0,14:0
qos_vlarb_low 0:0,1:4,2:4,3:4,4:4,5:4,6:4,7:4,8:4,9:4,10:4,11:4,12:4,13:4,14:4
qos_sl2vl 0,1,2,3,4,5,6,7,8,9,10,11,12,13,14,7
# QoS CA options
qos_ca_max_vls 15
qos_ca_high_limit 0
qos_ca_vlarb_high 0:4,1:0,2:0,3:0,4:0,5:0,6:0,7:0,8:0,9:0,10:0,11:0,12:0,13:0,14:0
qos_ca_vlarb_low 0:0,1:4,2:4,3:4,4:4,5:4,6:4,7:4,8:4,9:4,10:4,11:4,12:4,13:4,14:4
qos_ca_sl2vl 0,1,2,3,4,5,6,7,8,9,10,11,12,13,14,7
Port
Group
VLArb,
SL2VL
QoS
Level
Policy
* Currently in /var/cache/opensm/opensm.opts

## Slide 11: Defining QoS Level
QoS Levels
  Names PathRecord attributes per QoS level
qos-levels
qos-level
name: DEFAULT
use: default QoS Level
sl: 0
end-qos-level
qos-level
name: Low Priority
use: for the lowest prio
sl: 15
end-qos-level
qos-level
name: WholeSet
sl: 1
mtu-limit: 4
rate-limit: 5
packet-life: 4
end-qos-level
end-qos-levels
Port
Group
VLArb,
SL2VL
QoS
Level
Policy

## Slide 12: QoS Rules
Rules
  Map
    Class
    Source port group
    Dest port group
    Service ID
    Pkey
  Into
    QoS Level
qos-match-rules
qos-match-rule
use: by class 7-9 or 11
qos-class: 7-9,11
qos-level-name: WholeSet
end-qos-match-rule
qos-match-rule
use: Storage targets
destination: Storage
service-id: 22,4719-5000
qos-level-name: DEFAULT
end-qos-match-rule
qos-match-rule
use: match by all parameters (AND)
qos-class: 7-9,11
source: Virtual Servers
destination: Storage
service-id: 22,4719-5000
pkey: 0x0F00-0x0FFF
qos-level-name: WholeSet
end-qos-match-rule
end-qos-match-rules
Port
Group
VLArb,
SL2VL
QoS
Level
Policy

## Slide 13: Current Status
Integrated into OFED 1.3
Planned for OFED 1.3
  Simple policy file
  Integration of VL arbitration into qos-policy file

## Slide 14: Future Work
Host based QoS
  Schedule queues configuration
Simplified interface for VL arbitration tables
  Flexible VL arbitration setup in the fabric (e.g. port groups)

## Slide 15: Questions?
We can take questions for the next 23 seconds

## Slide 16: QoS Overview
Service reservation outside scope
Host
Target
SM
Fabric programmed with different service levels (BW/latency abilities)
Obtain path meeting service requirements