## Slide 1: OFED Management Tools
Ira Weiny
Lawrence Livermore National Lab
OFED Developer Workshop
November 16, 2007

## Slide 2: Clusters
Peloton: Zeus 288; Rhea 576; Atlas 1152; Minos 864
Visualization: Gauss 257; Prism 129; Mobius 17; Vertex 17; Stagg 10; Boole 6; Grant 6
Total Infiniband connected nodes at LLNL: 3322
  Not including test resources
  And more on the way!

## Slide 3
LLNL OFED improvements
node-name-map support in diags/OpenSM
Performance Manager
OpenSM event plugin (libopensmskummeeplugin)
OpenSM console (working on secure connection)

## Slide 4
node-name-map for better logging
BEFORE
SUBNET UP
...Found 3 Xmit Discards in 5 sec on node 0x2c90200219e64 port 1
...Found 2 Xmit Discards in 5 sec on node 0x2c90200222728 port 1
...Found 2 Xmit Discards in 5 sec on node 0x2c902002265ec port 1
AFTER
SUBNET UP
...Found 3 Xmit Discards in 5 sec on wopri (0x2c90200219e64) port 1
...Found 2 Xmit Discards in 5 sec on wopr4 (0x2c90200222728) port 1
...Found 2 Xmit Discards in 5 sec on wopr3 (0x2c902002265ec) port 1

## Slide 5
OpenSM PerfMgr OpenSM $ perfmgr
Performance Manager status:
state : Enabled
sweep state : Sleeping
sweep time : 5s
outstanding queries/max : 0/500
loaded event plugin : opensmskummeeplugin
OpenSM $ help perfmgr
perfmgr [enable|disable|clear_counters|dump_counters|sweep_time[seconds]]
perfmgr -- print the performance manager state
[enable|disable] -- change the perfmgr state
[sweep_time] -- change the perfmgr sweep time
[clear_counters] -- clear the counters stored
[dump_counters [mach]] -- dump the counters (optionally in
[mach]ine readable format)
OpenSM $

## Slide 6
Skummee Skummee is an open source, web based cluster monitoring package.
http://sourceforge.net/projects/skummee/

## Slide 7
libopensmskummeeplugin mysql> select name,port,xmit_data,rcv_data from port_data_counters,nodes where port_data_counters.guid=nodes.guid;
+--------------------------------------------+------+-------------+-------------+
| name | port | xmit_data | rcv_data |
+--------------------------------------------+------+-------------+-------------+
| wopri | 1 | 5039089238 | 5039201617 |
| MT25218 InfiniHostEx Mellanox Technologies | 1 | 36936 | 36996 |
| wopr4 | 1 | 20104882471 | 19682066922 |
| MT25218 InfiniHostEx Mellanox Technologies | 1 | 36792 | 36852 |
| wopr3 | 1 | 5038101616 | 5037953444 |
| wopr5 | 1 | 19682162591 | 20104971945 |
| SW1 wopr ISR9024D (MLX4 FW) | 1 | 37140 | 37080 |
| SW1 wopr ISR9024D (MLX4 FW) | 2 | 36996 | 36936 |
| SW1 wopr ISR9024D (MLX4 FW) | 3 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 4 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 5 | 5037943084 | 5038089256 |
| SW1 wopr ISR9024D (MLX4 FW) | 6 | 20104833780 | 19681956046 |
| SW1 wopr ISR9024D (MLX4 FW) | 7 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 8 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 9 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 10 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 11 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 12 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 13 | 5039043380 | 5038892151 |
| SW1 wopr ISR9024D (MLX4 FW) | 14 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 15 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 16 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 17 | 19681300979 | 20104381517 |
| SW1 wopr ISR9024D (MLX4 FW) | 18 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 19 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 20 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 21 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 22 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 23 | 0 | 0 |
| SW1 wopr ISR9024D (MLX4 FW) | 24 | 0 | 0 |
+--------------------------------------------+------+-------------+-------------+
30 rows in set (0.00 sec)

## Slide 8: Issues
Diags are better now, but still need work
Require sweeping the network
  Ok for diagnosing some problems but can be time consuming and increase load for normal monitoring.
Subnet must be “up” for tools to work

## Slide 9: Possible Solutions
Integrate more with OpenSM
  OpenSM knows more about the subnet, leverage this information for “normal” monitoring
  Use event plugin and console
Improve diags through the use of out of band information
  At LLNL this involves the use of an ethernet “management” network
  Other solutions may be to use known subnet configuration to compare against

## Slide 10
Where's the code?
Still can be hard to determine actual source for OFED kernel
ofed_makedist.sh is a BIG help!
However, how do we know if it is pulling the correct OFED version?

## Slide 11: Thanks to
Hal Rosenstock (Xsigo)
Sasha Khapyorsky (Voltaire)
Tim Meier (LLNL)
Al Chu (LLNL)