## Slide 1: Interop WG report
Arkady Kanevsky – Network Appliance
Rupert Dance – Lamprey Networks
Bob Noseworthy – UNH-IOL

## Slide 2: IWG - agenda
Overview
Logo
Oct ’07 interop feedback
future plans

## Slide 3: IWG Overview
Charter: To Define and Execute interoperability testing policies, processes and procedures of the OpenFabrics software stack
Interop Test Plan v1.12
  tests suites defined
    Mandatory tests
    Beta tests
  product categories defined
    tests specific to each product category

## Slide 4: IWG Overview - II
Each IWG interop event is preceded by IBTA conformance/interop event and iWARP conformance/interop event
Tests are applicable to both Linux (OFED) and Windows (OFW)
  Other platforms/OSes can be tested as black boxes
4th interop event Oct’07
  Used latest Linux OFED 1.2.5.1
Tentatively next interop event March ’08

## Slide 5: IWG Logo
LOGO is granted to a product when it passes all the interop tests in its product category
List is held at UNH-IOL and is cross listed with OFA web site - http://www.iol.unh.edu/services/testing/ofa/interoplist/interoplist.php
Logo is granted for a year
  If problems with the tests are found then product need to be recertified
Logo is specific for OFED version and lists which test plan version used

## Slide 6: Test Procedures Performed
IB Link Initialize
IB Fabric Initialize
IB IPoIB
TI iSER
IB SRP
TI SDP
TI MPI Intel
TI uDAPL
iWARP Connectivity
Fibre Channel Gateway (IB)
(TI – Transport Independent)
Test Procedure | InfiniBand Devices | IWARP Devices | Transport Independent
IB Link Initialization | Mandatory | Not Applicable | 
IB Fabric Initialization | Mandatory | Not Applicable | 
IB IPoIB | Mandatory | Not Applicable | 
TI iSER |  |  | Beta
IB SRP | Mandatory | Not Applicable | 
TI SDP | Mandatory | Beta | 
IB SM Failover/Handover | Beta | Not Applicable | 
TI MPI - OSU |  |  | Beta
TI MPI Intel |  |  | Beta
TI uDAPL |  |  | Beta
IWARP Connectivity | Not Applicable | Mandatory | 
Fibre Channel Gateway (IB) | Beta | Not Applicable | 
Ethernet Gateway (IB) | Beta | Not Applicable | 

## Slide 7: The Logo Tests By Equipment Type
Equipment Type | Link / Connect | IPoIB / VNIC | SRP | iSER | SDP | Open SM (IB) | MPI | UDAPL | NFS-RDMA
HCA | X | X | X | X | X | X | X | X | X
R-NIC | X |  | X |  | X |  | X | X | X
IB Switch | X | X | X | X | X | X (Also OEM SM) |  |  | 
Non-OFA Server | X | X | X | X | X | X | X | X | X
SRP Target | X |  | X |  |  | X |  |  | 
iSER Target | X | X | X |  |  | X |  |  | 
IB-Eth GW | X | X |  |  |  | X |  |  | 
IB-FC GW | X |  | X |  |  | X |  |  | 
NFS-RDMA Server | X |  |  |  |  | X |  |  | X
OEM SM Server (IB) | X | X | X | X | X |  |  |  | 

## Slide 8: Feedback
IB Link Initialize - Interoperability issues observed with prototype active cables.
IB Fabric Initialization - OpenSM stability issue observed with a fabric switch.
IB IPoIB – Issue observed with a device support for IP frames > than 2k.
Block Storage - An issue observed with simultaneous disk access from multiple initiators.
MPI - Issues observed with uDAPL support in iWARP
TI uDAPL
  iWARP issue(above),
  intermittent errors on IB in 3.1 test (multiple threads, RDMA Read and Write). Remaining tests fail from the start after it.
Notes:     dapltest: dapl/common/dapl_ep_free.c:114: dapl_ep_free: Assertion `ep_ptr->param.ep_state == DAT_EP_STATE_DISCONNECTED || ep_ptr->param.ep_state == DAT_EP_STATE_UNCONNECTED' failed.
    Test Error: Send-reaping DTO problem, status = FAILURE
    Test Error: Recv-reaping DTO problem, status = FAILURE
    Length mismatch (xfer 0x1000 wanted 0x100)
    Warning: conn_event_wait DAT_CONNECTION_EVENT_NON_PEER_REJECTED
    DT_cs_Client: bad connection event

## Slide 9: Future steps
TI iSER and Fiber Channel Gateway (IB) testing performed smoothly. Additional input to test plan generated to improve test process.
  Likely that these two tests will advance to Mandatory, enabling Logo qualification for these device classes.
Recommend uDAPL and dependent elements (MPI) to remain Beta.
Extent IPoIB tests to CM mode.
OFW for next event