## Slide 1: Extending InfiniBand Globally
November 2010
Eric Dube (eric@baymicrosystems.com)
Senior Product Manager of Systems

## Slide 2: Bay Microsystems Overview
About Bay
  Founded in 2000 to provide high performance networking solutions
  Silicon Engineering & Headquarters:
    San Jose, CA
  Systems Engineering & Business Development:
    Germantown, MD; MA
Corporate Focus
  Development of complex integrated circuits for high performance packet processing and optical transport applications
  Systems that deliver high performance protocol agnostic inter-working and Data Center Transport Extension (DCTE) (via InfiniBand)

## Slide 3: Extending InfiniBand Globally
0100110
Campus, Metro, or Wide Area Network
(from 1 to 1000’s of miles)
With InfiniBand’s adoption rate steadily growing for high performance computing, financial services, and high-speed storage applications, the need to extend InfiniBand between data centers is essential for providing disaster recovery, multi-site backups, and real-time data access solutions.
While InfiniBand’s crediting mechanism is an excellent and reliable way to provide flow control, existing InfiniBand hardware doesn’t provide enough port buffering for deployment beyond a single site.
  A reduction in sustained bandwidth starts occurring at just a few hundred meters due to inadequate port buffering if the number of virtual lanes aren’t reduced.
  Even with the minimum amount of virtual lanes configured, not enough packets can be kept in-flight due to the port buffer credit starvation that starts occurring at around 500-600 meters or less (depending on the data rate.)

## Slide 4: ABEx 2020 Global InfiniBand Extension Platform
Specialized devices are needed that provide enhanced buffering and end-to-end flow control to extend native InfiniBand over campus, metro, and wide area networks to any point on the globe.
  IB Device Type: 2-Port Switch
  IB Data Rate: 4X InfiniBand SDR (Full 8 Gbps line-rate performance)
  IB Virtual Lanes: 4 Operational (VL0-3) + 1 Management (VL15)
  Ethernet Encapsulation: Up to two 1G Ethernet links can be encapsulated over the same wide area network connection
  Pluggable Optics: SFP (1/2.5G) & XFP (10G) slots provide flexible connectivity options
  Range: Production fabrics running at 15,000km today; simulated up to 35,000km
InfiniBand
(4X SDR)
Gigabit Ethernet 1
Gigabit Ethernet 2
InfiniBand
(4X SDR)
Gigabit Ethernet 1
Gigabit Ethernet 2
Metro / Wide Area Network
SONET/SDH/ATM OC-48 to 192,
10G Ethernet (LAN/WAN), IP, dark fiber
Native IB Port
IB Pseudo-Port
2-Port IB Switch
ABEx 2020
ABEx 2020

## Slide 5: InfiniBand Applications and Multi-site Deployments
Global File Systems & Storage Architectures
  High performance/high volume data sharing and storage virtualization between sites
High Performance Computing (HPC)
  Clustered applications and cloud computing
  Post-processing and visualization
Financial Services
  Disaster recovery solution for low latency trading and market data feed applications
Clustered Databases and Warehouses
  Multi-site failover and data mirroring
  Real-time local access and information sharing
Distributed Healthcare Applications
  High resolution imaging deployments

## Slide 6: Large Data JCTD Petascale Global Storage Architecture
Site 3
Site 2
Site 4
Site 5
15km
4000km
4000km
Site 7
15,000km
Large distributed network of compute and storage resources on a single IB infrastructure
10’s of terabytes of traffic transmitted daily
  Petascale storage and transport
  Very large data set gathering, archiving, processing, and rendering for the US Government
In production since late 2006
Global InfiniBand Network
Sustains >250MB/sec.
across an OC-48 link
Site1
Site 6
Security
Element
Storage
Server
Nodes
Storage Array
(Petabytes)

## Slide 7: Large Data JCTD Lustre File Transfer Over Distance
Distance / Delay | Connection Line Rate | # of Files Transferred | % of Theoretical Max / Bandwidth
~150 fiber miles (2.5 ms latency) | SONET OC-192 | Single | 62.8% (590.6 MBps)
 |  | Multiple | 99.6% (935.7 MBps)
~2000 fiber miles (34.5 ms latency) | SONET OC-192 | Single | 59.1% (555.2 MBps)
 |  | Multiple | 91.1% (856.4 MBps)
~13,000 fiber miles (206 ms latency) | SONET OC-48 (Partial) | Single | 86.0% (182.3 MBps)
 |  | Multiple | 94.6% (200.7 MBps)
Maximum Theoretical Data Transfer Rate for SONET OC-192 = 939.7 MBps; for Partial SONET OC-48 = 212.0 MBps 1 MB = 1,048,576 bits (2^20) |  |  | 
* Slide content and performance data obtained from Large Data JCTD Public Presentation

## Slide 8: Large Data JCTD IB Performance Comparison
TESTS ON 1 Gbps CIRCUIT (~8000 miles)
[ ~13,000 fiber miles]
Typical
RDMA/IB
Performance
Typical
TCP/IP/ETHERNET
Performance
RDMA over IB provides very efficient use of available bandwidth with near linear scaling
RDMA/IB performance ≥ 80%
TCP/IP performance ≤ 40%
RDMA/IB CPU usage estimated 4x less
InfiniBand connection is lossless with nearly perfect fair sharing of bandwidth across multiple, concurrent data flows
TESTS ON 8 Gbps CIRCUIT (~1200 miles)
[~2000 fiber miles]
Typical
RDMA/IB
Performance
* Slide content and performance data obtained from Large Data JCTD Public Presentation

## Slide 9: InfiniBand Pseudowire Services for Converged Network Cores
InfiniBand
Ethernet
ATM
With more and more Service Provider’s moving towards converged network cores (such as IP/MPLS), supporting those core network services will be important in order to provide cost-effective global InfiniBand extension
  InfiniBand over MPLS Networks
    Draft specification has been submitted and presented to IETF for review and consideration
  InfiniBand Tunneling using Layer 2 Tunneling Protocol version 3 (L2TPv3)
    L2TPv3 is an IETF standard that provides a robust control plane for dynamically establishing and maintaining sessions
    Draft specification has implemented for InfiniBand tunneling over IP
Ethernet
InfiniBand
ATM
Service Provider
IP/MPLS
Core Network

## Slide 10: InfiniBand Extension over Packet Switched Networks via L2TPv3
InfiniBandSubnet
IP
Network
Service
Wide Area Network
InfiniBandSubnet
ABEx 2020
Physical View
InfiniBand Pseudowire via L2TPv3
ABEx 2020
Bridges the two InfiniBand Subnets into a single seamless network
Core network IP service is transparent to InfiniBand network and applications
InfiniBand View
InfiniBandSubnet
InfiniBandSubnet
Appear as two 2-port InfiniBand Switches
ABEx 2020
ABEx 2020

## Slide 11: SC09: Univ. of Utah / AMES Lab InfiniBand Pseudowire Demo
~1000 Fiber Miles!
~5000 Fiber Miles!
Global high performance storage demonstration using PVFS2 file system to transfer large files over InfiniBand between sites
Native InfiniBand is extended via L2TPv3 between sites over a shared packet switched network running IP

## Slide 12: InfiniBand to Wide Area Network Data Rates Mapping
Connection Type | Actual Data Rate | WAN Speed | WAN Transport
1X InfiniBand SDR | 2Gbps | 2.5G | OC-48 / OTU1
4X InfiniBand SDR | 8Gbps | 10G | OC-192 / OTU2 / 10GE
12X InfiniBand SDR | 24Gbps | ? | -
1X InfiniBand DDR | 4Gbps | ? | -
4X InfiniBand DDR | 16Gbps | ? | -
12X InfiniBand DDR | 32Gbps | 40G | OC-768 / OTU3 / 40GE
1X InfiniBand QDR | 8Gbps | 10G | OC-192 / OTU2 / 10GE
4X InfiniBand QDR | 32Gbps | 40G | OC-768 / OTU3 / 40GE
8X InfiniBand QDR | 64Gbps | ? | -
12X InfiniBand QDR | 96Gbps | 100G | OTU4 / 100GE
1X InfiniBand EDR | 25Gbps | ? | -
4X InfiniBand EDR | 100Gbps | 100G | OTU4 / 100GE
8X InfiniBand EDR | 200Gbps | ? | -
12X InfiniBand EDR | 300Gbps | ? | -

## Slide 13: Introducing the InfiniBand Extension (IBEx) Products
Metro (/Campus) IB Extension
1-350 km
1/10/40G Ethernet, IPv4/IPv6,
Dark Fiber
Global IB Extension
1-15,000 km
1/10/40G Ethernet, IPv4/IPv6,
SONET/SDH OC-48/192/786,
ITU-T G.709 OTU3, Dark Fiber, WDM

## Slide 14: IBEx G40 4X/8X InfiniBand QDR Extension Platform
IBEx G40 Main Features
  40G InfiniBand extension platform providing connectivity for:
    4X/8X InfiniBand QDR (up to 40Gbps) [2 x QSFP] and 10G Ethernet [1 x XFP]
  Utilizes Bay’s own Newport 40G framer ASIC to supports extension over:
    40G Ethernet, IPv4/IPv6, SONET/SDH OC-768, ITU-T G.709 OTU3, dark fiber, WDM
  Enhanced internal port buffering and flow control capabilities enabling global InfiniBand extension at full line rate from 1-15,000km
  Strong embedded Advanced Encryption Standard (AES-256)
    Complete WAN-side encryption for all LAN-side interfaces including InfiniBand and Ethernet
  Full support for all InfiniBand Virtual Lanes: 8 Operational (VL0-7) + 1 Management (VL15)
  Compact, low power, 1U 19-inch rack mountable chassis with redundant, hot-swappable power supplies and fans
Serial
Management
40G WAN
IB Port 1
IB Port 2 /
40G Ethernet
10G Ethernet
LAN
Availability Q1’2011

## Slide 15: Contact and Additional Information
Contacts
  Chuck Gershman, President & CEO
    chuck@baymicrosystems.com
    (408) 437-0400 x105
  Eric Dube, Senior Product Manager of Systems
    eric@baymicrosystems.com
    (301) 944-8149
Please stop by and see our 4X InfiniBand QDR over 40G wide area network demonstration in the InfiniBand Trade Association (IBTA) Booth #1161 at SC10!

## Slide 17: Performance Data: Bandwidth vs. Message Size
Chart: Unreliable Connection (UC)
| 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576 | 2097152 | 4194303.9999999991 | 8388608
HCAs Only | 2.14 | 5.22 | 10.5 | 20.57 | 40.82 | 80.76 | 152.51 | 276.7 | 633.15 | 881.82 | 914.59 | 926.58 | 932.62 | 935.62 | 937.26 | 938.02 | 938.4 | 938.59 | 938.67 | 938.72 | 938.75 | 938.76 | 938.77
HCAs+SW | 2.09 | 5.24 | 10.49 | 20.58 | 40.83 | 80.75 | 152.5 | 277.63 | 632.46 | 874.01 | 911.15 | 916.86 | 929.72 | 932.86 | 934.57 | 935.39 | 935.78 | 935.95 | 936.06 | 936.11 | 936.14 | 936.16 | 936.16
HCAs+ABEx | 2.02 | 5.26 | 10.53 | 20.62 | 40.85 | 81.01 | 152.85 | 277.18 | 630.93 | 882.3 | 915.17 | 921.28 | 933.18 | 936.16 | 937.78 | 938.53 | 938.93 | 939.12 | 939.21 | 939.26 | 939.29 | 936.4 | 934.97
HCAs+SW+ABEx @ 0km | 1.77 | 5.27 | 10.54 | 20.68 | 40.91 | 81.09 | 153.38 | 277.57 | 653.18 | 874.39 | 910.71 | 923.56 | 929.72 | 932.88 | 934.56 | 935.39 | 935.78 | 935.96 | 936.07 | 936.12 | 933.26 | 931.84 | 931.13
HCAs+SW+ABEx @ 10km | 1.16 | 5.27 | 10.54 | 20.66 | 40.86 | 81.02 | 153.23 | 277.66 | 636 | 873.77 | 911.13 | 923.53 | 929.71 | 932.87 | 934.57 | 935.4 | 935.78 | 935.95 | 936.06 | 936.12 | 933.25 | 931.83 | 931.11
HCAs+SW+ABEx @ 100km | 1.66 | 5.25 | 10.49 | 20.55 | 40.83 | 80.7 | 152.19 | 277.23 | 634.39 | 873.83 | 911.13 | 923.45 | 929.73 | 932.85 | 934.57 | 935.41 | 935.77 | 935.96 | 936.07 | 936.12 | 933.18 | 931.71 | 930.98
HCAs+SW+ABEx @ 1000km | 1.81 | 5.24 | 10.48 | 20.55 | 40.82 | 80.53 | 151.82 | 276.72 | 628.73 | 874.15 | 911.21 | 923.57 | 929.75 | 932.88 | 934.57 | 935.39 | 935.78 | 935.95 | 936.07 | 936.12 | 932.39 | 932.4 | 930.53
HCAs+SW+ABEx @ 10,000km | 2.61 | 5.24 | 10.46 | 20.62 | 40.78 | 80.8 | 152.17 | 276.7 | 633.85 | 874.68 | 911.39 | 923.59 | 929.79 | 932.86 | 934.59 | 935.4 | 935.78 | 935.96 | 936.07 | 936.12 | 924.58 | 924.59 | 924.6
7.5 Gbps
Sustained bandwidth over any distance!

## Slide 18: Performance Data: Bandwidth vs. Distance
Chart: Reliable Connection (RC) vs. Unreliable Connection (UC)
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 1000 | 2000 | 4000 | 8000 | 10000
RC 8k byte | 927.48 | 924.31 | 920.95 | 913.64 | 911.56 | 902.78 | 885.79 | 841.43 | 772.89 | 705.96 | 77.36 | 38.87 | 19.48 | 9.73 | 7.7
RC 64k byte | 933.7 | 933.42 | 933.14 | 932.85 | 932.58 | 932.31 | 932.04 | 931.75 | 931.47 | 931.19 | 608.37 | 308.27 | 155.19 | 77.47 | 62
RC 4M byte | 934.38 | 934.36 | 934.37 | 934.36 | 934.33 | 934.32 | 934.31 | 934.31 | 934.34 | 934.29 | 933.95 | 933.51 | 931.98 | 928.52 | 922.24
UC 512 byte | 645.54 | 637.91 | 638.36 | 637.18 | 630.47 | 634.56 | 633.24 | 635.51 | 634.18 | 634.4 | 630.62 | 629.82 | 632.22 | 632.22 | 636.5
UC 64K byte | 938.54 | 938.55 | 938.54 | 938.55 | 938.54 | 938.55 | 938.55 | 938.54 | 938.54 | 938.55 | 938.55 | 938.55 | 938.55 | 938.55 | 938.55
RC 512 byte | 292.92 | 182.49 | 133.29 | 102.7 | 86.2 | 73.06 | 63.65 | 56.32 | 50.38 | 45.63 | 4.85 | 2.43 | 1.22 | 0.6 | 0.47