## Slide 1: A Unified Approach to Networks
The OFED stack
Paul Grun
Chief Scientist
System Fabric Works, Inc.
pgrun@systemfabricworks.com

## Slide 2: Abstract
RDMA is a message passing paradigm.
Messages are independent of the I/O protocol.
The OFED stack presents a standards-based message passing interface for kernel and user applications, independent of the underlying wire protocol.
In this session, we discuss how OFED implements a true unified fabric.
We will also look at the three transport protocols and discuss their usages.

## Slide 3: Message Passing
app
LUN
app
*Message passing …is a form of communication used in parallel computing, object-oriented programming, and interprocess communication. In this model processes or objects can send and receive messages …to other processes. By waiting for messages, processes can also synchronize.
*http://en.wikipedia.org/wiki/Message_passing

## Slide 4: A message passing service
Consumer
Provider
app
LUN
app
Message Passing Service

## Slide 5: OFED verbs API
Message Passing Service
app
LUN
app
verbs
The OFED Verbs API is how an application accesses the message service
verbs
verbs
Consumer
Provider

## Slide 6: The RDMA Service
LUN
The RDMA service can pass messages across a network
verbs
RDMA service
verbs
RDMA service
verbs
RDMA service
wire
wire
wire
RDMA Protocols
Reliable Transport
Physical Wire
app
app

## Slide 7: The RDMA Service
LUN
verbs
RDMA service
verbs
RDMA service
verbs
RDMA service
wire
wire
wire
The provider appears to the consumer as a black box.
a well known set of inputs and outputs (e.g. verbs),
a well defined set of services
app
app

## Slide 8: The RDMA Service
LUN
verbs
RDMA service
verbs
RDMA service
verbs
RDMA service
wire
wire
wire
This means we can easily change what is inside the black box…
…with no impact to the consumer.
app
app

## Slide 9: The RDMA Service
InfiniBand
iWARP
RoCE
IB network
IP network
Enet fabric
app
verbs
OFED fully supports three wire protocols

## Slide 10: I/O versus message passing?
SCSI app
Message passing service
Verbs
I/O protocol
Messages
I/O protocol agnostic
??
message passing shouldn’t be confused with an I/O protocol

## Slide 11: OFED upper layer protocols
SCSI app
Message passing service
Verbs
I/O protocol
Messages
I/O protocol agnostic
??
OFED-supported Upper Layer Protocols
SRP, iSER

## Slide 12: A unified wire
Verbs
SDP
Lustre
skts apps
MPI
storage apps
file systems
native apps
Message passing service
MPI
SRP, iSER
A Unified Wire!

## Slide 13: Actually, a choice of 3 unified wires
Verbs
SDP
MPI
SRP, iSER
Lustre
skts apps
MPI
storage apps
file systems
native apps
InfiniBand
iWARP
RoCE
IB network
IP network
Enet fabric

## Slide 14: 3 Transport Protocols
verbs
IB transport
IB network
IB
link/phy
verbs
IB transport
IB network
Enet MAC
verbs
TCP transport
IP network
Enet MAC
RDDP
MPA
IB fabric
Enet fabric
IP network

## Slide 15: Why RoCE?
Networking via TCP/IP
Storage via FCoE
Low latency via RoCE
application
Ethernet
TCP
IP
FCoE
RDMA
This completes the Ethernet Trilogy – networking, storage, IPC

## Slide 16: OFED – a complete solution
Verbs
SDP
Lustre
skts apps
MPI
storage apps
file systems
native apps
MPI
SRP, iSER
InfiniBand
iWARP
RoCE
www.openfabrics.org

## Slide 17
RDMA has been shown to deliver value propositions that are not available through any other communications paradigm
These value propositions are compelling, particularly in the HPC space
  Low latency, improved resource utilization, flexible resource allocation,, scalability, unified fabric…

## Slide 18
RDMA as an excellent message passing service
Verbs – a standards-based interface for passing messages
Upper layer protocols: A true unified fabric
Seamless support for three different wires

## Slide 19: A shameless plug
Open Fabrics Alliance announces the January availability of a new course called
Application Programming for RDMA
Targeted at application programmers who want to learn how to write applications for RDMA
Registration is now open: http://www.openfabrics.org/training/index.html

## Slide 20: System Fabric Works
System Fabric Works, Inc. delivers engineering, system integration and strategic consulting services to organizations seeking to deploy high productivity computing and storage systems, low latency high performance networks and the optimal software to meet our customer’s application requirements. SFW also offers custom integration and deployment of commodity servers and storage systems at levels of performance, scale and cost effectiveness that are not available from other suppliers. SFW personnel are widely recognized experts in the fields of high performance computing, networking and storage systems particularly in OpenFabrics Software, InfiniBand, Ethernet and energy saving, efficient computing technologies such as RDMA.
www.systemfabricworks.com