## Slide 1: Neterion 10 Gigabit NIC Solutions
Delivering Virtualization to HPC and the Cloud
SC 2010 Booth #4654
John.Hagerman@Exar.com
Leonid.Grossman@Exar.com

## Slide 2: Exar Introduction
Enterprise Technology Solution Provider
  Founded in 1971
  NASDAQ: EXAR
  Acquired Neterion in Q1’2010
Industry-Leading Solutions
  10GbE I/O Virtualization
  Data Encryption
  Data Compression
  Data Deduplication

## Slide 3: I/O Trends for Data Centers and Cloud
I/O Virtualization
Server I/O virtualization on volume servers
  Software “para-virtualized” IOV in hypervisors
  Hardware IOV and PCI-SIG SR IOV standard
Network Convergence - network, storage and cluster controllers in a single pci-e slot
Dedicated hardware I/O offload engines for running I/O protocols like iSCSI, FCoE, RoCE and IPSec
10GbE IOV-compliant “plumbing” enables virtualization for most I/O intensive HPC applications
Notes: Prior to Exar, I was one the founders of a venture backed company called Neterion. Neterion was founded in 2001 and produced 3 generations of ASICs and software for 10GbE server adapters. Earlier this year, in April 2010 Neterion was acquired by Exar.
Today I’d like to present one of Neterion/Exar projects, called “TOE-less iSCSI offload for 10GbE IOV”.
As the name implies, the project had two objectives, that ended up being two incremental ASICs.
In the first phase, we’ve built and shipped a standard-based 10GbE IOV product that supports moving even most demanding IO applications from dedicated servers to virtual machines.
Second phase of the project is still work in progress.
This phase is adding an iSCSI offload silicon and related iSCSI initiator and target software that works well in IOV environments.
To build such IOV-friendly iSCSI accelerator, we had to come up with an original design that offloads most intensive parts of iSCSI protocol without using TOE engine. In addition to doing without a parallel TCP stack on the card, the design works with a system TCP stack without requiring any changes. The same approach of running accelerated iSCSI over unmodified system TCP software is applicable to targets as well , but for the purpose of this talk I will concentrate more on the initiator side.
The project started few years ago, when it became apparent that 10GbE adoption cycle moves quite differently from all earlier cycles of Ethernet Server Networking. Gigabit and prior generations of Ethernet NICs were deployed very rapidly, because both the acqusition cost and overhead to run at line rate was a rounding error. In contrast, 10GbE adoption cycle has been going for about 10 years with no end in sight, in part because it overlapped with other innovation trends in server I/O. One such major trend that profoundly affected 10GbE adoption curve is of course Server I/O virtualization. Development of hypervisors and para-virtualized networking facilitated hardware IOV, in particular SR (and MR) IOV extensions to pci-e specification, created by PCI SIG. Another major trend that has been affecting 10GbE Ethernet is I/O fabric convergence. Having separate fabrics for netwrking, storage and potentially cluster I/O fabric in a datacenter, is quite expensive. Also, virtualized servers require a lot of memory and as a result many modern blade and rack server models has one I/O slot only. In such servers it is simply not possible to put both 10GbE and FC adapters; single converged adapter becomes a must have rather than an optimization. Since iSCSI is the leading protocol candidate for the storage part of the converged fabric, and as such efficient support for iSCSI protocol became a key part of the project.
Last major datacenter trend related to the project is continuing use of specialized silicon for accelerating I/O protocols used in the converged fabric. Despite advances in generic processors, the use of dedicated offload engines is still desirable for cost and power reasons. Specifically, iSCSI has proven to be a protocol that is both very desirable and very difficult to offload or accelerate.

## Slide 4: Evolution of Software IOV
Virtual I/O in “Native” and Guest OS
Limitations of sharing I/O device in software prevent HPC applications from running in VMs
  Virtualization overhead
  Loss of “native” features
  Lack of SLA guarantees
Notes: Let me go into some more details of each trend.
Datacenter virtualization affected all major parts of the server, including I/O subsystem - with initial implementation done in software. Predominant inplementations today are software-based para-virtual interfaces, where a soft switch sits on top of one or more physical interfaces and exports multiple virtual interfaces used for both host and guest I/O.
Use of virtual IOV interfaces like vlans and failover teams that share the same physical adapter is actually quite common in standalone Oses.
However volume hypervisors like Vmware ESX and Linux KVM made use of virtual interfaces mandatory, and also amplified the limitations of sharing a single I/O device between multiple tenants.
First, the overhead of I/O para-virtualization in a hypervisor is much higher than the overhead associated with creating virtual interfaces in a native OS. This overhead results in lower throughput, higher cpu% or both. Latency goes up a well. Second, different traffic types do not co-exist well on the same adapter (iSCSI and vmotion). Lastly, some features typically supported by the native OS stack may not be supported by para-virtual stack (IPSec task offload in Windows). SLA is more important, so traditional 10GbE is less than perfect fit as most of the extra bw is wasted on overprovisioning.
Such limitations associated with software para-virtualization slowed down moving I/O intensive applications from dedicated servers to virtual machines. They also facilitated some practices for development and deployment of hardware IOV devices that affected our project.

## Slide 5: Evolution of Hardware IOV
PCIe multi-port and multi-function solutions
Single-Root (SR IOV) PCI-SIG specification
  Many products are implemented an “poor man” multi-function
  Not supported in Microsoft and VMware hypervisors
Direct Hardware Access (pass-thru)
Notes: Initial solution for isolation and SLA issues associated with para-virtual I/O was to use separate physical adapters for each virtual adapter. For example Vmware best practices documents call for a separate physical NIC behind each virtual NIC used for a distinct traffic type like vmotion or iSCSI. Using large number of GbE interfaces soon became impractical, in part because of economics and in part because many servers have only one I/O slot and can’t accommodate more than one quad port GbE.
Multi-function 10GbE adapters became a better solution, however implementing traditional multifunction was deemed too expensive. In retrospect, this conclusion turned out to be not entirely true. SR IOV extension to the base pci- spec was ratified by PCI SIG (with active neterion participation) in 2008, as a way to address the cost of traditional multi-function. There is a very comprehensive presentation on SR IOV right after this talk; essentially SR IOV is a lightweight to implement multiple pci-e functions on a single card. It is also coupled with ARI and provides bigger number of pci-e functions on a single device.
Our project ended up supporting both traditional pci-e multifunction and SR IOV. Support for SR IOV in hypervisors has been somewhat slow; today vast majority of shipping servers (including ESX 4.x and Hyper-V) do not support SR IOV, so for now traditional multi-function remains the only way to present multiple I/O interfaces to a host.
Another technique called Direct hardware access (or passthru) was introduced to solve performance and features limitations of para-virtual I/O.
Most hypervisors today support delegation of a pci device/function to a Guest (VMDirectPath in ESX 4.x).

## Slide 6: I/O Virtualization and Hardware SLA
2 Gbps
2 Gbps
2 Gbps
2 Gbps
2 Gbps
Bandwidth Over-Provisioning
T0
T1
T2
VM1: High
VM2: Low
VM2
VM1
VM1
VM1
VM2
Example:
  5 Virtual Machines – SLAs require 2 Gbps per VM
    Low Priority VM2 Receive: 5 Gbps spike
  Incoming traffic surge and no QoS results in SLAs being violated
Traditional Solution:
  Over-provision bandwidth to attempt to meet SLAs
  Reduces VM count by 50% or more
Over-Provisioning Bandwidth
T0
T1
T2
VM1: High
VM2: Low
VM3: Low
VM4: High
VM4
VM3
VM2
VM1
VM4
VM3
VM1
No or Limited QoS
VM4
VM3
VM1
VM2
VM5
Time
Time
Bandwidth ‘Buffer’
VM5: High
VM5
VM5
VM2
Bandwidth ‘Buffer’
VM2
VM2

## Slide 7: Exar X3100 with IOQoS™
By VM or Protocol Policies
  Prioritization
  Bandwidth limits
  Receive & transmit
High Priority Traffic
  Bandwidth & SLAs maintained
  Low Deterministic Latency
Low Priority Traffic
  Bandwidth allocated as available
Maintain SLAs Without Over-Provisioning
Exar X3100 with IOQoS
2 Gbps
2 Gbps
2 Gbps
2 Gbps
2 Gbps
T0
T1
T2
VM4
VM3
VM2
VM1
VM4
VM3
VM1
VM4
VM3
VM1
VM2
VM5
VM2
Time
VM1: High
VM2: Low
VM3: Low
VM4: High
VM5: High
VM5
VM5

## Slide 8: Virtualization and HPC
Optimum Resource Utilization
Single X3120
  Replace multiple HBA and NICs with single dual port 10GbE adapter
    Clustering – RoCE
    IP Storage
    Data – 10GbE
IOQoS™
  Easy management of Prioritization and Bandwidth Allocation
Direct Access for Latency sensitive (clustering) fabric
KVM Host
VM1
O/S
Application
VMxnet
Driver
VMn
O/S
Application
Neterion
X3120
NIC 1
NIC 3
Integrated L2 Switch
X3120 configured with Multiple PCI Functions
IOQoS Priorities and Bandwidth Allocation
NIC 0 Management - Priority 0 / 1Gbps
NIC 1 Clustering - Priority 1 / 2Gbps
NIC 2 Clustering - Priority 1 / 2Gbps
NIC 3 Data Network - Priority 2 / 3Gbps
NIC 4 IP Storage - Priority 3 / 4Gbps
NIC 2
NIC 4
Exar Guest
OS Driver
NIC 0
MPI
MPI
VMxnet
Driver
Exar Guest
OS Driver
Virtual L2 Switch
Exar Host Driver

## Slide 9: Summary
Exar 10 Gigabit Ethernet Adapter Leadership
  Most complete silicon IOV implementation
    Each function (SR IOV or traditional pci-e) is a complete NIC
    Compliments para-virtual mode with passthru mode – for any OS
    Runs “native” driver on each function in passthru mode
    Delivers hardware SLA for each interface
    Delivers near native throughput, latency and SLA to a Guest
    Allows hypervisor to manage privileged operations on passthru interfaces
  Qualified at top-tier server OEMs
  Enables virtualization for most I/O intensive applications
Datacenter and Cloud Solutions for Today and Tomorrow

## Slide 10: Thank You! Visit us at Booth #4654
John.Hagerman@Exar.com
Leonid.Grossman@Exar.com