## Slide 1: January 2006 Pre-Plugfest Interop Session
Tuan Phamdo – Intel – Co-Chair IBTA CIWG
Sujal Das - Director, SW Product Mgmt, Mellanox
Rupert Dance – Lamprey Networks

## Slide 2: Event Summary
Interop Session 1/16/06 1/18/06 was hosted by Lamprey Networks in Durham NH.
All major IBA vendors participated: Cisco, Mellanox, PathScale, SilverStorm, Voltaire, etc.
Most devices passed the interoperability procedures; bugs/patches will be posted separately to each vendor or OpenIB community
Presentation by Bob Noseworthy UNH-IOL Technical director; UNH IOL is considering participating in the next IB PlugFest
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Devices Tested
Cisco
  TS120 Switch
Flextronics
  24 port DDR unmanaged switch
Mellanox
  3 Dell 1850 with 2 DDR port HCAs (Lion Mini)
PathScale
  InfiniPath HCA
SilverStorm
  9024 24 port SDR Anafa II Managed Switch
Voltaire
  ISR 9024 - 24 port SDR Managed Switch
  ISR 9096 - 96 port SDR Managed Switch
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Event Goals
Develop and enhance an Interoperability Test Plan for March 06 IBTA-OpenIB PlugFest event
Software testing is the main focus, IPoIB, SDP, SRP, iSER, OpenSM, Voltaire SM (VSM), SilverStorm SM, Cisco SM
Running OpenIB stack on all HCAs with every available managed and un managed switches
Investigate the possibility of UNH IOL involvement ( http://www.iol.unh.edu )
  For future on-demand interoperability testing facilities
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Event Activities
Day 1
  Test plan was reviewed by all participants and via phone conference
  UNH IOL Presentation by Bob Noseworthy
  Fabric initialization running the SM from each one of the managed switches and the OpenSM
  Lab tour at UNH IOL
Day 2
  IPoIB Interop procedure
  SDP Interop procedure
Day 3
  iSER and SRP Interop procedure
  SM Handover procedure
  Test Plan final review
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Attendance
Cisco
  Aaron Miller
  Nikhil Kelshikar
Mellanox
  Amit Krig
  Nimrod Gindi
PathScale
  Johann George
SilverStorm
  Bob Jaworski
  John Seraphin
Voltaire
  Chris Perrault
  Hal Rosenstock
Lamprey Networks
  Rupert Dance
  Vidhya Sriram
UNH IOL
  Bob Noseworthy
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Test Configuration
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Open SM and OEM SM Configurations
OpenIB
OEM 1 SM
OEM 2 SM
OEM 3 SM
OpenIB
OpenIB
OpenIB
OpenSM
We refer to these configurations as “SM Configurations” in the upcoming slides
OpenSM

## Slide 9: Initialization Tests
For all “SM Configurations”
  Perform device discovery
  Check all ports for Armed and Active States
    Use protocol analyzer
  Check port error counters (link errors)

## Slide 10: IPoIB Tests
For all “SM Configurations”
  IPoIB interface and subnet creation
  Multicast group creation and joining
  Multicast Forwarding Table creation, validation
  Ping procedures
    various sizes, ARP resolution, fragmentation
    Connecting and disconnection HCA nodes
  FTP procedures (put, get, compare files)

## Slide 11: Single Vendor SM or Open SM Failover Tests
All active SMs on fabric from single vendor only (including Open SM from Open IB)
Disable all SMs except one
Use Agilent Exerciser to:
  Verify all disabled SMs are NOT ACTIVE
  Verify that SM not disabled is MASTER
  Run Cluster Initialization tests
Start another SM and verify MASTER/SLAVE election based on priority
Run Cluster Initialization tests and OSMTest to validate the SA
Disable MASTER and verify that the existing SLAVE is elected as MASTER
Run Cluster Initialization tests and OSMTest to validate the SA
Run above tests for all vendor SMs and Open SM

## Slide 12: SRP and iSER Tests
For all “SM Configurations” and multiple SMs (Host and/or Switch) in primary/slave modes
  Connect Initiator and Target to Switch
  Load Target, Host, check connection
  Run basic dd application from Initiator node
  Kill Master SM while test is running. Check that test completes (with Slave SM taking over as new Master)
  Unload Initiator and check that connection terminated properly
  Repeat above steps (with new Master)
  Disconnect and reconnect Initiator node and run basic dd application from Initiator node

## Slide 13: SDP Tests
Installation requirements
  Vsftpd – FTP and sshd – SCP
  Set environment variables per requirements
For all “SM Configurations”
  Run NetPerf procedures with message size variations
  Run FTP procedures
  Run SCP procedures
  Verify SDP connections

## Slide 14: CIWG Compliance Tests
You should know what they are!

## Slide 15: Some stuff not covered
OpenSM OpenIB v1.0
OEM 1 SM OpenIB v1.0
OEM 2 SM OEM 2 PM OpenIB v2.0
OpenSM OpenIB v1.0
OEM 3 SM OpenIB v2.1

## Slide 16: High Level Test Results
Detailed test results not issued publicly for vendor confidentiality commitments at this pre-plugfest event
High level results
  Fabric shows some switch relay errors when both ports of the HCAs are connected to the same network
  Some ULPs like IPoIB are stable
  Other ULPs like SDP are close but need refinement
  One issue with single vendor SM failover
  CIWG Compliance test pack uncovered some bugs with the OpenIB stack – these will be submitted as patch requests
Issues discovered reported to the vendor contacts in OpenIB for review and consideration as patches for future releases.

## Slide 17: Other Results
The Interop test plan was reviewed at the start of the event and has been updated after the event and submitted for approval
Test plan and other event docs are in www.OpenIB.org
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: Next Steps / Call to Action
IBTA / CIWG is willing to participate with OpenIB for larger scale Software Interoperability workshop in March 2006
  UNH IOL ready to host and committed to doing physical layer testing. Funding – WIP
OpenIB members can help in improving the Interoperability Test Plan
  There are many areas still not covered
  Needs to be an on-going effort
Help set-up on-demand testing facilities at UNH IOL
  What OpenIB release version, firmware, vendor SM, HCA, Switch revisions are certified to be interoperable and compatible at any given time
Get ready for a SC06 InfiniBand Blast!

## Slide 19: Thank You!