## Slide 1: MemFree Technology
Gilad Shainer
Mellanox Technologies Inc.
shainer@mellanox.com

## Slide 2: Agenda
What is MemFree technology
Benefits of MemFree
How MemFree works
MemFree driver implementation
ULP tuning
Devices supporting MemFree mode

## Slide 3: What is MemFree Technology ?
HCA No Longer Requires Attached Memory
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Benefits of MemFree Technology
Reduces overall add-in card and system cost
Reduces power consumption
HCA has smaller footprint
Better utilization of system memory
Facilitates Landed On Motherboard (LOM) design
InfiniHost III
HCA
Dual InfiniBand
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: MemFree Use
Top500
  Rank #130, November 2005
  256 nodes, 562 processors
  MemFree InfiniBand HCAs
  Highest efficiency on x86 architecture (84%)
Personal supercomputing
  Enable “cubical” intensive compute solutions

## Slide 6: How the Mem HCA Works
Data/WQE is fetched from main memory
HCA resource context is fetched from local attached memory (LAM)
  HCA caches context
CPU
Mem
CTL
DRAM
PCIX
CTL
HCA
DRAM
InfiniBand
PCI-X
Chipset
CPU
DRAM
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Understanding the LAM Role
Stores physically contiguous HCA context objects
Device driver allocates and organizes physically contiguous objects
DRAM dictates HCA capabilities
LAM
…
HCA
MPT
MPT Base
QPC
QPC Base
MTT
MTT Base
FW
FW Base

## Slide 8: Migrating HCA Contexts to Host Memory
Host memory is made available in non-contiguous pages
Driver allocates these physical pages in host memory for context
Driver passes the pages to the HCA
DRAM
FW
QPC
MPT
MTT
…
HCA
Host Mem

## Slide 9: Migrating HCA Contexts to Host Memory
HCA turns the physical pages into virtually contiguous spaces for the HCA objects
DRAM
FW
QPC
MPT
MTT
…
HCA
Host Mem
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Introducing ICM
ICM – InfiniHost Context Memory
Creates a virtually contiguous space for HCA context tables
DRAM limitation of HCA capabilities is removed
Enables allocation of objects at run-time
ICM
FW
QPC
MPT
MTT
…
HCA
Host Mem
ICM Translation
Logic
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Leveraging PCI Express Technology
System architecture provides lower latency access from IO device to memory and thus enables MemFree
Increased IO Bandwidth makes context cache replacement painless
CPU
Mem
CTL
DRAM
PCIX
CTL
HCA
DRAM
InfiniBand
PCI-X
Chipset
CPU
CPU
Mem
CTL
DRAM
HCA
DRAM
InfiniBand
PCI-Express
Chipset
CPU
DRAM
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: MemFree Driver Implementation
MemFree support is part of mthca device driver
  Single driver support for all Mellanox HCAs
  Driver takes decisions at runtime depending on the physical device
No impact on upper layer software
Maintainer: Leonid Keller (Mellanox)
IBAL
TVPD
ULPs
HCA HW
IBAL
MTHCA
ULPs
HCA
MemFree
HCA
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: ULP and MemFree
MemFree Technology has no impact on upper layer software
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Devices Supporting MemFree Mode
Device | Dev ID | FW | MemFree | TVPD
InfiniHost (Tavor) | 23108 | 3.3.3 |  | 
InfiniHost III-Ex (Arbel) InfiniHost Mode | 25208 | 4.7.400 |  | 
InfiniHost III-Ex (Arbel) InfiniHost III Mode | 25218 | 5.1.0 |  | 
InfiniHost III-Lx (Sinai) | 25204 | 1.0.700 |  | 
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: MemFree Performance
Negligible to NO performance impact!
MemFree Whitepaper available for further information

## Slide 16: Status and Schedule
Kernel level porting of MTHCA is done
Code available for review on OpenIB repository
User level porting on going
MTHCA release expected early Q2/06

## Slide 17: Resources
OpenIB WiKi
  https://openib.org/tiki/tiki-index.php?page=OpenIB+Windows
Openib-windows mailing list
  http://openib.org/mailman/listinfo/openib-windows
Sign up to contribute
  http://windows.openib.org/openib/contribute.aspx

## Slide 18: Q & A