## Slide 1: iSER Update
OpenIB Workshop, Feb 2006
Yaron Haviv, Voltaire yaronh@voltaire.com
John Hufferd, Brocade
jhufferd@Brocade.COM

## Slide 2: Agenda
Quick iSER intro
iSER Update
  iSER Status in IETF and IBTA
  iSER OpenIB Initiator
  iSER OpenSource Target initiative
  iSER 3rd party copy study
Simple ways to boot using iSER
iSER OpenIB Roadmap

## Slide 3: Why is iSER needed ?
One high speed SCSI solution for both IB & iWarp
Comprehensive storage networking and management capabilities derived from iSCSI
  Discovery, naming, security, error-recovery, booting, etc’
Leverage on the wide following of iSCSI
  OS code and storage products
  Management tools and standard interfaces
  Standardization, Testing and protocol maturity
  End-user training

## Slide 4: iSCSI Mapping to iSER / RDMA Transport
iSER eliminates the traditional iSCSI/TCP bottlenecks :
  Zero copy using RDMA
  CRC calculated by hardware
  Work with message boundaries instead of streams
  Transport protocol implemented in hardware (minimal CPU cycles per IO)
BHS
AHS
HD
Data
DD
Protocol frames (RDMA)
iSCSI PDU
RC Send
RC RDMA Read/Write
X
In HW
X
In HW

## Slide 5: iSER protocol overview (Read Example)
SCSI Reads
  Initiator Send Command PDU (Protocol data unit) to Target
  Target return data using RDMA Write
  Target send Response PDU back when completed transaction
  Initiator receives Response and complete SCSI operation
iSCSI Initiator
iSER
HCA
HCA
iSER Target
Target Storage
Send_Control (SCSI Read Cmd)
RDMA Write for Data
Send_Control + Buffer advertisement
Control_Notify
Data_Put (Data-In PDU) for Read
Control_Notify
Send_Control (SCSI Response)

## Slide 6: iSCSI Configuration, Discovery and Availability
iSER leverages on iSCSI management and discovery
  Zero-Configuration, global storage naming (SLP, iSNS)
  Change Notifications and active monitoring of devices and initiators
  High-Availability, and 3 levels of automated recovery
  Multi-Pathing and storage aggregation
  Industry standard management interfaces (MIB)
  3rd party storage managers
  Security (Partitioning, Authentication, central login control, ..)
Working with iSER over IB Doesn’t require changes !!!
  Enable investment protection (software, education, training, ..)
  Reduce the fear-factor of IB

## Slide 7: iSCSI/iSER over IB Storage Discovery Flow
iSCSI discovery map storage name+zone+user credentials to IP’s+TCP Port’s (called Portals)
Initiator connect to Target using CMA
  IP is mapped to Port GID by CMA through ARP (over IPoIB)
In IB iSCSI Login and SCSI commands travel over the same iSER IB RC connection
Host
Portal IP -> GID (IB ARP)
IB SA
Storage/ Gateway
GID->LID & Path
ARP
SA Path Record Query
CM Connect to Target
iSER over an IB RC connection
Discover Portals and Targets* (optional)
iSNS or SLP Server
iSNS/SLP queries over IPoIB/GbE
* Gateway can also provide iSNS/SLP services, if the Host already has the gateway address this can be skipped, a client can also issue simple iSCSI discovery (SendTargets) instead of iSNS/SLP
SA – Subnet Admin, CMA – Abstract Communication Manager (for IB & iWarp)
CMA

## Slide 8: iSCSI Discovery – Direct SLP
FC Routers discover FC SAN
Client Broadcast: I’m xx where is my storage ?
Relevant iSCSI Targets & FC gateways respond
Client may record multiple possible targets & Portals
GbE Switch
FC Switch
IB to IP Router
Native IB RAID
IB to FC Routers
iSCSI Client
Portal – a network end-point (IP+port), indicating a path

## Slide 9: iSCSI Discovery – iSNS
FC Routers discover FC SAN
iSCSI Targets & FC gateways report to iSNS Server
Client ask iSNS Server: I’m xx where is my storage ?
iSNS responds with targets and portals
resources may be divided to domains
Changes notified immediately (SCNs)
GbE Switch
FC Switch
IB to IP Router
Native IB RAID
IB to FC Routers
iSCSI Client
iSNS or SLP run over IPoIB or GbE, and can span both networks
iSNS Server

## Slide 10: iSER Update

## Slide 11: iSER Update in IETF & IBTA
iSER Spec in IETF
  Recent iSER spec covers InfiniBand, iWarp, and gateways
  Status: last call, expert review
  See: http://www.ietf.org/internet-drafts/draft-ietf-ips-iser-05.txt
iSER Annex in IBTA
  Define communication establishment (CM) and messages over IB
  Define the work with both 1.1 and 1.2 IB hardware (with and without ZBVA or FMR)

## Slide 12: Open-iSCSI Architecture and iSER
iSER
Thin layer implementing iSCSI over RDMA

## Slide 13: iSER Architecture Changes (from kDAPL to CMA)
iser
kDAPL
CMA
Verbs
CM
iscsi_iser
open_iscsi
scsi_mod (mid layer)
Code shrinked significantly in the last few months
IB HCA
iWarp RNIC

## Slide 14: iSER Open Source Target
The need:
  Open source package for native RDMA (IB & iWarp) storage
  That would be simple to operate and manage
  And can be used as a reference for storage vendors
iSER Open Source Target Goals
  An RDMA acceleration layer under iSCSI Enterprise Target (IET)
    http://iscsitarget.sourceforge.net/
  Operates over both IB & iWarp (over CMA)
  Adhere to Linux coding standards
Key Milestones
  First version on April
Contributors
  Voltaire, NetApp, DoE, OGC, others are welcomed

## Slide 15: iSER Open Source Target Architecture
Using Open source iSCSI target code as the main infrastructure
Add iSER as a transport
Support both InfiniBand and iWarp via CMA
iSCSI Enterprise Target (IET)
iSCSI TCP
IB HCA
RNIC
NIC
Management
iSER
Datamover API
CMA
Verbs
Net IF
SCSI ML
Drivers
TCP/IP
Storage
Drivers
LVM / MD
Optional
Adapters

## Slide 16: Example: 3rd Party Transfer and Distributed RAID5 with iSER
The host sends a command to the RAID controller.
Host
RAID
controller
0
1
2
3
4
CMD
CMD
CMD
RDMA
RDMA
(parity calculation)
The RAID controller sends commands to the targets.
The targets perform RDMA operations to the host.
The RAID controller sends commands to recalculate the parity block (only for WRITE requests).
The targets calculate the new parity block.
Targets
CMD
RDMA
(parity calculation)
Source: A Phd study by Erez Zilber, Israel Technion
Using unmodified iSER Initiator

## Slide 17: Distributed RAID with iSER
RAID 5 Write Performance
3000 MB/s Sustained RAID 5 Write !
Using few commodity based storage appliances
Setup

## Slide 18: Simple Diskless iSCSI/iSER Booting
IPoIB
Not required with Bios that supports iSCSI or iSER Boot (Int13h BIOS Extension)
Source: Cisco iSCSI boot
iSER Storage or iSER to FC/GbE Routers
Can boot of simple PXE, or more advanced BIOS (PXE supported by most IB vendors today)

## Slide 19: iSER Development Roadmap Summary
iSER Initiator for Linux
  Push to kernel starting soon
  Expected additional optimizations
  More work on Open-iSCSI management utilities
  Testing with iWarp hardware
iSER Initiators for other OSs
  Windows and Solaris in progress
iSER Target Project
  Complete iSER Target reference code and integration with IET

## Slide 20: Resources and Links
iSCSI Specification | http://www.ietf.org/rfc/rfc3720.txt
iSER and DA Introduction | http://www.rdmaconsortium.org/home/iSER_DA_intro.pdf
Latest iSER Specification | http://www.ietf.org/internet-drafts/draft-ietf-ips-iser-05.txt
Open-iSCSI Project | http://www.open-iscsi.org/index.html
Enterprise iSCSI Project (IET) | http://iscsitarget.sourceforge.net/