## Slide 1: Range Extension Sonoma’06
David Southwell, Jason Gunthorpe – Obsidan
Linden Mercer – Naval Research Labs
Bill Boas – OpenIB/ SC|05

## Slide 2: Background
Encapsulating IB over WANs – concept established at Naval Research Labs, D.C.
Developed into prototypes shown at SC|04 by team now known as Obsidian
Integrated with SCinet/OpenIB fabric at SC|05, connecting Seattle to Dupont, Livermore and Washington D.C.

## Slide 3: Longbow prototype
Appears on IB fabric as a two-port switch
  4x SDR CX-4 copper port
  OC-192c SONET optical WAN port

## Slide 4: Longbow WAN port
Physical layer is not IB conformant, but…
…at the link layer has all the required IB attributes with sufficient credits to span very long distances (> circumference of Earth)
Interoperates with subnet managers; remote fabric islands unify into a single large subnet

## Slide 5: Production – Longbow XR
Integrates IB router function
Tentative support for ATM+10GbE WANs
HA architecture

## Slide 6: Technical issues…
Upper Level Protocols
Queue Pair timeouts
Router support
Heterogeneous fabrics

## Slide 7: 1. Upper Level Protocols
ULPs are built around an assumption of inexpensive round-trip signaling
ULPs with RDMA reads tend to use three phase exchanges…
…65 milliseconds across the country

## Slide 8: 1. Upper Level Protocols
? Rely on custom & proprietary ULPs for long haul applications ?
? Develop new ULPs for efficient long haul IB transport ?

## Slide 9: 2. Queue Pair timeouts
Long haul links must be accommodated by Queue Pair timeout settings
Reliant on manual timeout fudging unless the 1.2 specification’s SM link latency measurement and automatic timeout adjustment mechanism is widely deployed…

## Slide 10: 3. Router support
Router function routes on IPv6 headers, with LID path and caching…
…Subnet manager must be configured with a routing table; applications must be looking up with IPv6 GIDs, not LIDs…

## Slide 11: 4. Heterogenous fabrics
Long haul merges vendor – homogeneous sites into possibly heterogeneous multi-site subnets
Important that interoperability testing supports such configurations!

## Slide 12: Evaluation Opportunities…
Global data center replication
Native IB supercomputer GRID connectivity
Remote IB storage
Campus/ Metro area IB clustering
Remote visualization applications
Streaming media transport