## Slide 1: Reliable Datagram Sockets (RDS)
Ranjit Pandit
SilverStorm Technologies
rpandit@silverstorm.com

## Slide 2: Agenda
Goals
High Level Design
Current status
Preliminary performance data
Future work

## Slide 3: Goals
Provide reliable datagram service
  performance
  scalability
  high availability
  simplify application code
Maintain sockets API
  application code portability
  faster time-to-market
Keep It Simple !!!

## Slide 4: Stack Overview
Host Channel Adapter
Openib Access Layer
IPoIB
IP
Oracle 10g
Socket
Applications
TCP
UDP
SDP
RDS
Kernel
User
UDP Applications

## Slide 5: High Level Design
RDS registers with the kernel as driver for Address Family PF_INET_OFFLOAD and Type SOCK_DGRAM
Application creates a RDS socket with socket(2)
  arg1 = PF = PF_INET_OFFLOAD
  arg 2 = Type = SOCK_DGRAM
socket(2) API supported
  socket, bind, ioctl, sendmsg, recvmsg, poll, getsockopt/setsockopt

## Slide 6: Connection model
Application connectionless
Rds maintains node-to-node connection
IP addressing
Uses CMA
on-demand connection setup
  connect on first sendmsg()or data recv
  disconnect on error or policy like inactivity
Connection setup/teardown transparent to applications
Application connectionless

## Slide 7: Data and Control Channel
Uses RC QP for node level connections
Data and Control QPs per session
Selectable MTU
b-copy send/recv
h/w flow control

## Slide 8
P2
Kernel
User
Node 1
P1
sendmsg(node2)
…
Pn
Node 2
RC QP
RC QP
s1
s2
sn
P1
S1
recvmsg()
Rds
Rds

## Slide 9: Send
Connection established on first send
sendmsg()
  allows send pipelining
ENOBUF returned if insufficient send buffers, application retries

## Slide 10: Receive
Identical to UDP recvmsg()
  similar blocking/non-blocking behavior
“Slow” receiver ports are stalled at sender side
  combination of activity (LRU) and memory utilization used to detect slow receivers
  sendmsg() to stalled destination port returns EWOULDBLOCK, application can retry
    Blocking socket can wait for unblock
  recvmsg() on a stalled port un-stalls it

## Slide 11: High Availability (failover)
Use of RC and on-demand connection setup allows HA
  connection setup/teardown transparent to applications
  every sendmsg() could “potentially” result in a connection setup
  if a path fails, connection is torn down, next send can connect on an alternate path (different port or different HCA)

## Slide 12: Preliminary performance Rds on Openib
*Dual 2.4GHz Xeon
2G memory
4x PCI-X HCA
**Sdp ~3700Mb/sec
TCP_STREAM

## Slide 13: Preliminary performance Rds on OpenIB
*Dual 2.4GHz Xeon
2G memory
4x PCI-X HCA
**Sdp ~3700Mb/sec
TCP_STREAM

## Slide 14: Preliminary performance Rds on OpenIB

## Slide 15: Status in OpenIB
Z-copy
Functionally 98% complete
Running Netperf
Running Oracle unit test (crload) stable today
Code checked into contrib/silverstorm/ https://openib.org/svn/trunk/contrib/silverstorm/rds/

## Slide 16: Future
AIO
Z-copy
Shared recv queue

## Slide 17: Q&A