## Slide 1: InfiniBand Storage: Luster™ Technology and HP StorageWorks Scalable File Share (HP SFS)
February 2006
Kent Koeninger and Grant Grundler
Lustre is a trademark of Cluster File Systems, Inc. in the United States

## Slide 2: InfiniBand-Storage Approach?
Choose InfiniBand for storage SAN instead of FC or GbE?
Choose storage IB storage after choosing InfiniBand for clustering?
HPC-Linux clusters:
  Large market for fast IB message-passing interconnects
  IB-storage may want track this HPC-Linux focus
Compute Farm
HP SFS
InfiniBand

## Slide 3: InfiniBand or Ethernet for Storage?
  InfiniBand is a leading choice for fast server-to-server message passing interconnects
    InfiniBand storage is an excellent choice for these clusters
  If Ethernet is sufficient for message passing, then Ethernet is usually sufficient for storage
    Exception: When individual servers (e.g. large SMPs) require several hundred MB/s of storage bandwidth

## Slide 4: SAN versus NAS: InfiniBand works both ways IB on New Scalable NAS: Object Based Storage (e.g. Lustre)
NAS Cluster Scalability
SAN SMP & FC scalability
Small to medium number of compute servers
  Tens to a few hundred
High bandwidth to individual large SMPs
QoS: Guaranteed bandwidth
Low-latency transactions
Less emphasis on price/performance
Large number of small compute servers
  Thousands of clients
Optimized for price/performance
Low to medium individual-client bandwidth
  ~100 to 600 MB/s
Ubiquitous access
  NFS and CIFS & other protocols
Ethernet, InfiniBand, Myrinet, Quadrics
Fibre Channel, iSCSI (Ethernet), InfiniBand
Notes: Comparing NAS and SAN:
NAS storage works well to connect a handful to thousands of small servers, workstations, and PCs to a shared filesystem within a machine room or among continents. NAS is well suited to interconnect high-speed shared storage with multiple gigabytes-per-second (GB/s) using the new scalable storage servers such as HP SFS and Clustered Gateway.
NFS and CIFS are ubiquitous NAS protocols for Unix/Linux and Windows clients (respectively). New protocols, such as the Lustre™ protocol supported by HP SFS can deliver POSIX compliant coherent interfaces with parallel read/write locking behavior similar to that found on SMPs and shared SAN filesystems. This eliminates the locking and performance issues inherent in the more ubiquitous NFS protocol.
HP SFS supports the object-based Lustre protocol over GbE interconnects and over gigabyte-per-second (GB/s) interconnects such as InfiniBand, Myrinet, and Quadrics. Thus NAS can now deliver hundreds of MB/s of bandwidth to individual compute servers with aggregate cluster storage bandwidths of tens of GB/s. With these new advanced protocols and interconnects, NAS is now faster than SAN for cluster storage with dramatically superior price/performance.
SAN interconnects are oriented toward serving a smaller number of larger servers over Fibre Channel fabrics. Newer SAN transports include iSCSI over Ethernet. Multiple Fibre Channel connections can sustain multiple GB/s of bandwidth to individual SMPs. (NAS does not yet support multiple GB/s connections to individual SMPs.)
SAN scalability tends to be limited to 256 compute servers or less. The price of SAN interconnects is a practical limit, given SAN costs rise as the scalability increases. Many SAN storage devices limit the number of hosts to which they will speak. These limits are typically in the range of 20 to 256 hosts, with more expensive SAN equipment often required for the larger host counts.
SAN filesystems tend to provide coherent, POSIX compliant, APIs, much like the parallel I/O behavior on and SMP. Some SAN filesystems (such as ADIC StorNext) can deliver guaranteed bandwidth for video streaming and other time-critical functions.
OS interfaces: NAS interfaces, such as NFS and CIFS tend to be ubiquitous standards that are not usually sensitive to operating system upgrades. On the other hand SAN filesystems tend to use complex OS interfaces that may change during OS upgrades. The Lustre protocol (supported by HP SFS) currently lies somewhere between these extremes. Lustre is currently supported only on major Linux distributions (Red Hat EL 3, EL 4, and Fedora and SUSE SLES9). It requires a Linux kernel modification. These Lustre patches are expected to be included in future distributions from kernel.org.
Comparing Bandwidth/Capacity with High Availability
Solutions that deliver higher availability tend to deliver lower performance per dollar. These differences can by large---factors, not just fractional differences.
For example HP SFS delivers over five times as much large-block sequential bandwidth per dollar compared to the Clustered Gateway solution. On the other hand Clustered Gateway maintains continuously available service for Enterprise class storage.
Similarly the ADIC StorNext solution is geared for high bandwidth while the Veritas Storage Foundation solution concentrates on high availability and small-random transaction performance. In addition ADIC offers Managed Storage (transparent migration of data between hierarchical storage such as disk and tape).
Summary
HP SFS:
Highest bandwidth (10s of GB/s), highest capacity (512 TB),
1000s of Linux clients, limited number of NFS clients,
POSIX coherent I/O, resiliency geared for HPC
Clustered Gateway:
High bandwidth (>2 GB/s), high capacity (16 TB),
high transaction rates,
many Unix/Linux/Windows clients (NFS),
NFS read/write locking efficiency, high availability (HA)
ADIC StorNext with Managed Storage
High bandwidth (10s of GB/s at SAN prices), high capacity (100s of TB), maximum 256 clients (also limited by SAN pricing), multi-OS support (HP-UX, Linux, Windows, other UNIX),
POSIX coherent I/O, guaranteed bandwidth, Managed Storage (HSM)
Veritas Storage Foundation Clustered File System
High transaction rates, not geared for high bandwidth, maximum 16 clients, multi-OS support (HP-UX, Linux, Windows, other UNIX),
POSIX coherent I/O, high availability (HA)

## Slide 5: InfiniBand Storage SAN (iSER) and NAS (objects)
Block (SAN)
File (NAS)
S2A9500 InfiniBand RAID
Engenio 6498 InfiniBand storage
HP SFS
TP9700 InfiniBand Storage
GPFS
Isilon IQ
Better scalability than FC-SAN or iSER-SAN
Enables lower-cost storage options
Better price/performance than FC-SAN
Enables lower-cost storage options

## Slide 6: InfiniBand SAN and Object Based NAS
SAN: Traditional Block-level-SAN storage (iSER)
  Individual hosts access per LUN (no shared storage)
  Distributed database access (e.g. Oracle)
  SAN shared filesystems (limited client scalability)
      Often 16 or fewer clients
      Usually less than 100 clients
      Sometimes up to 256 clients
NAS: File-level (object based) storage
  Highly scalable shared file systems
  Scalable to server orders of magnitude more clients
    10s, 100s, 1,000s, or 10,000s of client servers
  Lustre is a leading open-source object-based storage protocol

## Slide 7: HP Unified Cluster Portfolio Data Management Options
Fabric
StorNext filesystem & Managed Storage
HP Tape Silos
Fabric
HP SFS
Lustre & NFS
Higher Bandwidth
& Capacity
Guaranteed BW
Greater HA
& Transactions
“Enterprise class”
Clustered Gateway
Higher Bandwidth
& Capacity
“HPC class”
Greater HA
& Transactions
“Enterprise class”
NFS & CIFS
Storage Foundation SAN Filesystem
Matrix
GFS
NAS Cluster Scalability
SAN SMP & FC scalability
Notes: Comparing NAS and SAN:
NAS storage works well to connect a handful to thousands of small servers, workstations, and PCs to a shared filesystem within a machine room or among continents. NAS is well suited to interconnect high-speed shared storage with multiple gigabytes-per-second (GB/s) using the new scalable storage servers such as HP SFS and Clustered Gateway.
NFS and CIFS are ubiquitous NAS protocols for Unix/Linux and Windows clients (respectively). New protocols, such as the Lustre™ protocol supported by HP SFS can deliver POSIX compliant coherent interfaces with parallel read/write locking behavior similar to that found on SMPs and shared SAN filesystems. This eliminates the locking and performance issues inherent in the more ubiquitous NFS protocol.
HP SFS supports the object-based Lustre protocol over GbE interconnects and over gigabyte-per-second (GB/s) interconnects such as InfiniBand, Myrinet, and Quadrics. Thus NAS can now deliver hundreds of MB/s of bandwidth to individual compute servers with aggregate cluster storage bandwidths of tens of GB/s. With these new advanced protocols and interconnects, NAS is now faster than SAN for cluster storage with dramatically superior price/performance.
SAN interconnects are oriented toward serving a smaller number of larger servers over Fibre Channel fabrics. Newer SAN transports include iSCSI over Ethernet. Multiple Fibre Channel connections can sustain multiple GB/s of bandwidth to individual SMPs. (NAS does not yet support multiple GB/s connections to individual SMPs.)
SAN scalability tends to be limited to 256 compute servers or less. The price of SAN interconnects is a practical limit, given SAN costs rise as the scalability increases. Many SAN storage devices limit the number of hosts to which they will speak. These limits are typically in the range of 20 to 256 hosts, with more expensive SAN equipment often required for the larger host counts.
SAN filesystems tend to provide coherent, POSIX compliant, APIs, much like the parallel I/O behavior on and SMP. Some SAN filesystems (such as ADIC StorNext) can deliver guaranteed bandwidth for video streaming and other time-critical functions.
OS interfaces: NAS interfaces, such as NFS and CIFS tend to be ubiquitous standards that are not usually sensitive to operating system upgrades. On the other hand SAN filesystems tend to use complex OS interfaces that may change during OS upgrades. The Lustre protocol (supported by HP SFS) currently lies somewhere between these extremes. Lustre is currently supported only on major Linux distributions (Red Hat EL 3, EL 4, and Fedora and SUSE SLES9). It requires a Linux kernel modification. These Lustre patches are expected to be included in future distributions from kernel.org.
Comparing Bandwidth/Capacity with High Availability
Solutions that deliver higher availability tend to deliver lower performance per dollar. These differences can by large---factors, not just fractional differences.
For example HP SFS delivers over five times as much large-block sequential bandwidth per dollar compared to the Clustered Gateway solution. On the other hand Clustered Gateway maintains continuously available service for Enterprise class storage.
Similarly the ADIC StorNext solution is geared for high bandwidth while the Veritas Storage Foundation solution concentrates on high availability and small-random transaction performance. In addition ADIC offers Managed Storage (transparent migration of data between hierarchical storage such as disk and tape).
Summary
HP SFS:
Highest bandwidth (10s of GB/s), highest capacity (512 TB),
1000s of Linux clients, limited number of NFS clients,
POSIX coherent I/O, resiliency geared for HPC
Clustered Gateway:
High bandwidth (>2 GB/s), high capacity (16 TB),
high transaction rates,
many Unix/Linux/Windows clients (NFS),
NFS read/write locking efficiency, high availability (HA)
ADIC StorNext with Managed Storage
High bandwidth (10s of GB/s at SAN prices), high capacity (100s of TB), maximum 256 clients (also limited by SAN pricing), multi-OS support (HP-UX, Linux, Windows, other UNIX),
POSIX coherent I/O, guaranteed bandwidth, Managed Storage (HSM)
Veritas Storage Foundation Clustered File System
High transaction rates, not geared for high bandwidth, maximum 16 clients, multi-OS support (HP-UX, Linux, Windows, other UNIX),
POSIX coherent I/O, high availability (HA)

## Slide 8: Typical SAN Filesystems
ADIC StorNext
  Many OSes, high bandwidth, rich media, guaranteed bandwidth, managed storage (HSM to tape), up to 256 clients
Red Hat GFS
  Linux, targeted at commercial HA, up to 256 clients
PolyServe Matrix SAN FS
  HA, Linux or Windows, 2 to16 clients
Symantec (Veritas) Storage Foundation Cluster Filesystem
  HA, HP-UX and Linux, 2 to 16 clients, integrated with ServiceGuard
SAN
Fabric
GFS

## Slide 9: Object Based Storage (Scalable NAS)
Scalable, coherent, high performance, high capacity, shared filesystems
Efficient scaling for coherent-shared storage
  10s to 1000s of clients
Most are POSIX compliant with distributed locking & coherency
  Solves the NFS coherency issues
Virtualizes storage at the Linux-object-server level
  Less expensive than virtualizing storage at the array level
Most targeted at Linux clustering
All support Ethernet
  Some support other interconnects such as InfiniBand

## Slide 10: Leading object-based open-source storage protocol
Open Source code from Cluster File Systems, Inc. (CFS)
HP and CFS work together on Lustre technology
  Hendrix ASCI DoE government project
Lustre support available from CFS and HPC vendors
  HP StorageWorks Scalable File Share (HP SFS)
    HP SFS is HP’s Lustre appliance
Compatible with most Linux releases
  Included in SUSE SLES9
  Ports for Lustre clients on other OSes in progress
“Portals” layer is transport independent
  InfiniBand, Ethernet (TCP/IP), Myrinet, Quadrics, …
  Soon on

## Slide 11: HP StorageWorks Scalable File Share Scalable High-Bandwidth Storage Appliance for Linux Clusters
Scalable bandwidth
  200 MB/s to 35 GB/s (more by request)
  Excellent price/performance
Scalable capacity
  2 TB to 512 TB (more by request)
Scalable connectivity
  Tens to thousands of compute clients
Scalable resiliency
  No single points of failure
  Flexible resiliency choices
Scalable simplicity
  Easy-to-use standard, simple-to-use shared file system
Scalable Bandwidth
Linux Cluster
A Cluster of
Data Servers
Forming a
Single Virtual Scalable File Server
Higher Cluster Throughput: Solves the I/O Bottleneck for Linux Clusters
Notes: [Enter any extra notes here; leave the item ID line at the bottom]
Avitage! Item ID: {{726638BE-B5BF-44CD-9819-0E8172FCEDC5}}

## Slide 12: HP SFS Attributes
Maximize
  Parallel bandwidth
  Capacity
  Resiliency/reliability/redundancy
  Ease of use with one big, fast and easy filesystem connected to 10s, 100s, or 1000s of client servers
Minimize Price &TCO
  By clustering low cost, standard, scalable components
X
$
$
$
$
$

## Slide 13: HP SFS Focus
Fast storage for scalable computing
  Clusters and server farms 10s, 100s, and 1000s of clients
Linux clusters & workstation farms
Lustre: Leading open-source, Linux, object-based filesystem standard
Simultaneous support for Ethernet and InfiniBand
  SANless HW (message passing)
Reliable and inexpensive SFS20 storage, virtualized and managed using Lustre & HP technology
Compute Farm
HP SFS

## Slide 14: HP SFS20 storage on InfiniBand Inexpensive HW virtualized with Lustre
Per OSS pair:
- 16 TB usable capacity
- 8 active SFS20s
2 TB per active SFS20
1180 MB/s read bandwidth per OSS pair
800 MB/s write bandwidth per OSS pair
Low cost:
No expensive SAN components
Resilient-redundant fail-over via inexpensive SCSI cables
Plugs into existing IB switches
OSS Pair
SFS20
SFS20
DL380
SmartArray
6404 x2
SFS20
SFS20
SFS20
SFS20
SFS20
SFS20
DL380
SmartArray
6404 x2
SCSI cables (two per SFS20)
IB
IB
GbE
GbE

## Slide 15: HP SFS: 2x to 4x superior price/ bandwidth compared to SAN FS on leading IB-block-SAN storage
Scalable Price/Performance on InfiniBand
GB/s
- SAN arrays
InfiniBand
RH GFS
- 32 to 128
GFS clients
Each SAN array:
- 32 TB
- 2 GB/s
- Quad IB-4x
0
2
4
6
8
10
- HP SFS:
Excellent price, performance, scalability, reliability - Each inexpensive
OSS: - 8 TB - 600 MB/s - Single IB-4X
IB-SAN suggested retail pricing for leading IB-connected SAN storage arrays
Price 
Expecting similar price/performance improvements on lower-cost IB-iSER enabled storage
Bandwidth 
3x
Traditional SAN-Array Technology
Object-based technology

## Slide 16
Notes: [Enter any extra notes here; leave the item ID line at the bottom]
Avitage! Item ID: {{2CA9AB1C-81F0-423A-AA65-BDB06BECC2B9}}