## Slide 1: Sockets Direct Protocol (SDP) for Windows - Motivation and Plans
Gilad Shainer
Mellanox Technologies Inc.
shainer@mellanox.com

## Slide 2: Agenda
SDP Protocol Overview
SDP vs. WSD
SDP Stack Components
Current Status

## Slide 3: Key Message
With SDP, any traditional TCP sockets-based applications can benefit from InfiniBand without any change
Notes: SDP enables existing socket based application to transparently utilize the InfiniBand capabilities and achieve superior performance

## Slide 4: Motivation
SDP sockets provide much better bandwidth and lower latency than traditional TCP sockets
SDP sockets provide lower CPU utilization and can benefit from RDMA
WSD sockets are not supported in all Windows operation systems
  XP, XP embedded and Vista do not have WSD support

## Slide 5: Sockets Direct Protocol (SDP) Overview
Transparent to the application
Maintains SOCK_STREAM Semantics
Leverages InfiniBand Capabilities
  Transport Offload – Reliable Connection
  Zero Copy – Using RDMA
Standardized wire protocol
Notes: Transparent: Socket switch selects TCP or SDP
  Administrable policy
Socket semantics: IPv4 addressing, Uses TCP port space, Connect/Accept model, Common socket options, Out of band data
Wire protocol: InfiniBand Specification 1.2 Annex A4

## Slide 6: SDP Stack Overview
Unmodified Application
winsock API
SDP
SDP WinSock
Provider
Socket Switch
WSD
SAN Provider
IB Access Layer
TCP/IP
IPoIB NDIS
Miniport
IB Access Layer
user
kernel
WinSock
Provider
Windows platform
OpenIB
Application

## Slide 7: Data Transfer Modes
Data
Source
Data
Sink
App
Buf
SDP
Buf
SDP
Buf
SDP
Buf
SDP
Buf
SDP
Buf
SDP
SDP Data Message
SDP
Buf
SDP
Buf
SDP
Buf
SDP
Buf
SDP
Buf
SDP
App
Buf
App
Buf
Data
Source
Data
Sink
App
Buf
SrcAvail Message
App
Buf
App
Buf
RdmaRdCompl Msg
BCopy
Read
ZCopy
RDMA Read
Read Response

## Slide 8: SDP vs. WSD
 | Sockets Direct Protocol (SDP) | Windows Sockets Direct (WSD)
API | Winsock 2.x, POSIX/BSD like API | 
WHQL | None | SAN / Winsock Direct
Wire Protocol Specification | IB spec 1.2 | Microsoft Proprietary
OS Support | Win XP, WS 2K3 | WS 2K3
Interoperability | Windows, Linux and any OS that conforms to IB specification | Windows Server only
Code | Open-source | Protocol - Windows proprietary SAN Provider - open-source
IHV Module | Socket Provider Library SDP kernel module | SAN Provider Library
Implementation Domain | Mostly kernel (similar to Linux) | Mostly user
Notes: WSD is supported on W2K, but IB is not supported on W2K Server
IHV module: IB access layer is required anyway

## Slide 9: ULP Comparison
 | IB Verbs | SDP/WSD | IPoIB
API | Low level | Socket (TCP only) | Socket
Latency | lowest | lower | low
Bandwidth | highest | high | medium
CPU Utilization | lowest (if not polling) | BCopy high ZCopy low | highest
Kernel bypass |  | SDP  WSD  | 
Stack Overhead | Light | Medium | High
Memory Registration | Explicitly by application/ middleware | Heuristics by SDP | None
Application Adaptation | Porting/ Development Required | Supports Unmodified Application | 
Notes: ULPs that we chose for this comparison: verbs, sdp and ipoib
IPoIB we got up to 400MB/s with some binding to CPU tricks
ZCopy CPU% - in gen1 implementation, with sync calls, we got much lower CPU utilization 40% compared with 370%, especially when more than one process is running in parallel
For example, MPI chose IB Verbs to get best latency, although its more complicated to implement
We recommend a 2 phase approach, where 1st deployment is SDP and then you write directly to verbs.
2 phase approach: 1) with SDP transparently do the installation, etc 2) implement over verbs

## Slide 10: SDP Socket Provider
User-mode library
Implements Socket Provider Interface (SPI)
  Supports TCP protocol
  WSPxxx function for each socket call
Socket switch implemented in the library
  Policy based selection of SDP vs TCP
  SDP calls are redirected to SDP module
Notes: Policy: Port, Address, Application Name
Socket switch: TCP calls are directed to original provider (next in provider chain)
SDP Module: Calls are sent using ioctl system call
Callback and events
  Synchronous operation (application thread blocks in kernel)
  For asynchronous operations
    Helper threads sleeping in kernel
    Object signaling from kernel
    Thread pool with kernel to user shared buffer (overlapped)

## Slide 11: SDP Module
Kernel module
  Implemented as a high level driver
Connection establishment
  Routing
  ARP through IPoIB
  Path Record
  CM
Data transfer mechanism
  Buffer Copy for first release
  Using physical memory region for local SDP buffers
Notes: Connection state and locking
  Enables locking at passive level and updates at DPC/IRQ level

## Slide 12: Kernel Implementation
Each user socket is implemented as a struct in the kernel, composed from 3 parts:
  For sending the data
  For receiving data
  For accepting new connections
    If this is a listening socket
Currently all the parts are being protected by one lock
  We will consider changing that in the future
In kernel all operations are being implemented as Asynchronous
  If operation is blocking, we block at the user level.
The Heaviest operations are data copy
  We might consider moving it from the lock.

## Slide 13: Buffer Copy Implementation
16KB buffers for send and receive.
The data is first copied into the buffers, and only then being sent
For each process, a second thread is created for user context operations
If the data copy should be done in interrupt context
  This thread will be waked up – for send and receive operations

## Slide 14: Current Status
Maintainer
  Tzachi Dar (Mellanox); tzchid@mellanox.co.il
Buffer Copy released Oct/05
  Support: Socket, Connect, Bind, Listen, Accept, Close, Send/Recv
  Only kernel code posted to openib.org repository
Zero Copy and API enhancements schedule TBD
  Will support overlapped (asynchronous) operation
  Will support Zero copy
Notes: VERY PRELIM: Win to/from Linux
  553MB/s over a single socket at 120KB message size
  CPU utilization 120% (out of 200%)
Platform:
Pentium 4 3.6GHz, single CPU, HT enabled, 1MB cache, 0.5GB RAM
Windows XP SP2

## Slide 15: Current Performance
2 sockets (2 processes) bandwidth benchmark
Message size (B)
Bandwidth (MB)
1
0.06
2
0.16
4
0.25
8
0.65
16
1.04
32
2.55
64
4.16
128
10
256
15.2
512
37.5
1024
61.8
2048
138
4096
233
8192
493
16384
573
32768
971
65536
980
131072
1241
262144
1205

## Slide 16: Resources
OpenIB WiKi
  https://openib.org/tiki/tiki-index.php?page=OpenIB+Windows
Openib-windows mailing list
  http://openib.org/mailman/listinfo/openib-windows
Sign up to contribute
  http://windows.openib.org/openib/contribute.aspx

## Slide 17: Q & A