## Slide 1: Next Steps for iWARP
Caitlin Bestler
Uri Elzur

## Slide 2: Impact of supporting iWARP
For InfiniBand specific Providers
  Some new methods to be stubbed.
    no additional functionality needed.
  Some new attributes to report
    all derivable from existing fields.
For IB specific OpenSTAC components:
  none
For Shared OpenSTAC components
  some new methods
  some new fields
  expanded semantics.
For OpenSTAC users
  No loss of transport specific capabilities.
  “Safe Harbor” transport neutral practices will be highlighted.
    Must understand broader semantics.
    If you have to add apples and oranges try counting fruit.

## Slide 3: Enabling RDMA over Multiple Reliable Transports
RDMA Services over reliable connections are mostly the same
  Same objects: PD, QP, CQ, SRQ, MR …
  The same primary messages: RDMA Write, RDMA Send, RDMA Read
But Differences Exist
  Completion Semantics, LKey/RKey/STag, Atomics, MTU values, Send with Invalidate …
How to deal with that?
  We do not want to simply Abstract them away:
    Not suitable for verb layer interface. Already done by DAT and IT-API.
  Just enumerating the differences is not enough
    ULP developers do not want a thick book of rules on how to do things differently for each transport.
  We must highlight “Safe Harbor” techniques that can be followed
    Practices which enable applications to not care which underlying transport.
    Example: Using RDMA Send to sequence RDMA Writes *always* works.

## Slide 4: Agenda
What will be covered for each feature:
  What is constant
  What varies
  How to not care
What features are covered:
  Completion Semantics
  Connection Establishment
  RDMA Read target buffer specification
  OpenSTAC Enhancements needed for both iWARP and InfiniBand 1.2
Lastly:
  ULP Strategy for using Transport Specific Capabilities

## Slide 5: The Biggest Difference: Completion Semantics
Many implications frequently listed as distinct differences:
  RDMA Write Ordering:
    iWARP does not guarantee placement ordering between RDMA Writes, however completion ordering is ALWAYS guaranteed
  Flow Control
    iWARP requires the ULP to flow control Send/Recv exchanges
    iWARP can truly have multiple in flight RDMA Reads
  Remote Access Errors
    An iWARP Work Request with invalid remote destination may complete successfully, with the error being reported in an RDMAP Terminate.
But they all symptoms of a single difference
  The only guaranteed meaning of a SendQ Work Completion is that the source buffers are no longer required.
  It does not mean that the peer has it, or even the peer host.

## Slide 6: iWARP/LLP Separation means SendQ Completions are Different
iWARP does not have its own flow control
  Reliability and Congestion management is provided by the Lower Layer Protocol (LLP)
  Receive buffer management is provided by the ULP.
  This is what enables iWARP to be transparent to the network.
A Send/RDMA Write can be completed as soon as source buffers are no longer needed.
  The content could have been “received” at several stops before the true destination:
    A: Transmit RNIC LLP Buffers
    B: Middlebox Buffering
    C: Receive RNIC LLP Buffers
      Even if only one: receive RNIC may ack before RDMA Processing has completed.
    D: Processed by RDMA, but completion is not noted by peer.
      Which means it may be on the RDMA Device’s cache, not in host memory.
      Also true for IB.

## Slide 7: Implication: ULP Flow Control
Data Sink ULP must pace Data Source ULP to avoid buffer overrun:
  not necessary for tagged data (Writes)
  but necessary for untagged data (Sends)
This is natural for typical usage:
  ULPs establish credit limit when connection is established.
    part of CM for IB.
    part of Private Data for iWARP (or constant/out-of-band)
  Sending a request decrements.
  Receiving a reply restores.
    With optional special adjustments.
When sender complies with the limit:
  transports behave identically
When sender does not
  iWARP may break connection.
  IB may fill SendQ.

## Slide 8: Implications: ULP Flow Control
What is constant:
  ULP need to manage flow control at the ULP layer.
  ULP cares about number it can post without overwhelming its peer, which covers complete span.
What varies:
  The penalty for not complying with the flow control policy.
How to not care:
  Use end-to-end ULP flow control.
    Pipeline can be kept full anyway.
  Don’t violate it.
    If you need N, say you need N, don’t allocate N-2 and count on the transport to fudge the difference.
  Per-connection ULP behavior shouldn’t be changed by the CQ size anyway.
Where is the impact:
  ULPs, not the core.

## Slide 9: Implication: Completions Required at the Data Sink
What is Constant:
  Using only RDMA Writes there is no way to guarantee when the remote peer will detect your message. It is inherently model specific.
What varies:
  InfiniBand provides more guarantees about how memory (as read back from an RDMA Read) will be updated in sequence.
How to not care:
  Ensure that there is a completion at the Data Sink when you want to be guaranteed that the data will be seen.
Where the impact is:
    ULPs.

## Slide 10: Implication: Remote Error Detection Varies
LLP Ack can be sent before the RDMA Headers are examined
Therefore the sender’s work request can complete “successfully”.
What remains constant:
  The error will be caught.
  The connection will be torn down.
  There will be no unauthorized access to memory.
What varies:
  How the error is reported.
How not to care (for core OpenSTAC code):
  Define additional asynch event for connection failure from remote access violation.
  Impact confined to shared code and iWARP specific, since IB will not generate it.
How not to care (for ULPs):
  Don’t send invalid work request
  Be prepared for error completions or asynch event errors if you do.
  Be prepared for seeing flushed completions before seeing the asynch event that tore down the connection.

## Slide 11: Connection Management
Immediate strategy:
  DAPL style connection management already defined in cma:
    works for both IB and iWARP
    Passive side listens, receives connection requests with Private Data, accepts/rejects.
    Active side requests connection to remote address/port with Private Data, gets accept/reject.
  Leave IB-only modes available through IB-specific connection manager.
  Deal with TCP-specific connection establishment in later releases.
Long term issues:
  How to support pre-MPA streaming mode negotiations
    for iSCSI/iSER
    for other new protocols
  How to avoid inconsistencies with host stack:
    ARP, Neighbor, MTU: already proposed.
    PMTU Maintenance (ICMP Unreachable because of fragmentation).

## Slide 12: IP Addressing
What is constant
  Support of IPv4 and IPv6 addresses.
What varies
  How the IP Address is translated onto the wire
  iWARP lacks visibility below IP Address
How to not care
  Maintain semantics of IP Address
  Only fetch L2 information through L2 interfaces
  Configure each fabric on its own terms
    only attempt to use a configured fabric in transport neutral ways.

## Slide 13: RDMA Read Target
What is constant:
  RDMA Reads specify registered memory as the Data Sink in an RDMA Read Work Request.
What varies:
  InfiniBand specifies the target of an RDMA Read as an LKey.
  iWARP verbs define the target of an RDMA Read as equivalent of an RKey.
    although the wire protocol is compatible with an LKey equivalent.
How NOT to not care in the long run
  Just post the Memory Region STag as the RDMA Read Data Sink STag
    Very snoopable value that should not be exposed on an untrusted network.
How to not care (OpenSTAC):
  Define a method for RDMA Read to RKey (IB Providers do not have to implement).
  Define an attribute to indicate support for RKey targeting (IB Providers do not have to set).
  Define an attribute to indicate when targeted LKey is exposed to the wire (Never true for IB).
How to not care (ULPs)
  Don’t rely on having RDMA Read SGL lengths greater than one.
  Use safe choices when possible:
    RDMA Read to LKey if LKey is not exposed to wire.
    RDMA Read to RKey if available
  Use RDMA Read to LKey if safe anyway
    snooping is not a concern (network is secure).
    the Memory Region will be promptly invalidated anyway.
  Simulate RDMA Read with ULP Requests if all else fails.

## Slide 14: Support for iWARP and IB 1.2 : Narrow Memory Windows
Narrow Memory Windows: only valid only QP used to bind it, rather than entire PD.
  Simpler caching logic when RKey is only used on a single QP.
  Limits scope of exposure to most natural default
Current proposal (iWARP branch): provider you either all wide or all narrow windows, dependent on the transport.
  Not terribly friendly to ULPs.
  Does not allow Provider to support both:
    Specifically allowed under IB 1.2 and RNIC-PI.
How to not Care (OpenSTAC):
  Define Device Attributes indicating support of each type, require that devices support at least one.
  Add mw constructor(s) that control the type.
How to not care (ULP)
  Use the default constructor when there is only one QP per PD anyway.
  Use narrow windows when supported.
  Use QP-specific Protection Domains and Shared Memory Regions otherwise.

## Slide 15: Support for iWARP and IB 1.2: Fast Memory Register Work Request
Privileged Work Request that updates a Memory Region
  Much like a window bind, but new contents supplied rather than referenced.
What is constant:
  Resulting FMR is the same whether bound by work request or verb.
What varies:
  Work Request pipelining enables fewer FMRs, but requires more SQ/CQ slots.
    Capability must be reported to allow ULP to adjust accordingly.
How to not care (for OpenSTAC)
  Define an optional FMR Work Request.
How to not care (for ULPs)
  The fmr pool can simulate pipelining.
  When using FMR work requests, account for extra requests/completions
    remember that even suppressed completions require slots in the CQ after an error.
  Extra FMRs or Extra WQEs.

## Slide 16: Support for iWARP and IB 1.2 : Bind/FMR Work Requests
What is constant:
  After bind/fast register the RKey (RTag) can be exported to the remote peer
    and it will be usable by the time the remote peer receives it.
  Memory Window binds can be pipelined.
What varies:
  How key portion of RKey/RTag is varied.
    iWARP and IB 1.2 specify a user controllable “key portion”
      Relevant for FMR Work Requests, and for all iWARP Binds.
How to not care (OpenSTAC):
  Define a device attribute indicating when user control of “Key portion” will be honored (FMR Work Requests only, FMR and Narrow Windows, always).
  Indicate on MR creation when FMR support will be required.
How not to care (ULPs):
  Don’t try to control the key portion. Just inc if ownership is assigned to ULP.
    Do so as low in the stack as possible (middleware, not application logic).
  Treat MRs as static or dynamic, don’t try to mix usage of any single MR.

## Slide 17: Transport Specific Enhancements
What varies
  InfiniBand Only
    Atomics
    Write/Send with immediate
  iWARP Only
    Send with Invalidate
    RDMA Read with Invalidate
How to not care (OpenSTAC):
  Define all capabilities. Do not require any of them to be implemented.
How to not care (ULP):
  Have an alternate strategy to achieve application specific goal when the transport specific solution is not available.
    Example: ULP uses a local invalidate if the remote peer did not invalidate.
    Example: use RDMA Atomics to lock if available, or ULP message/response when not available.

## Slide 18: Summary
Most methods / fields will be common.
Providers are not expected to emulate methods/features that are not part of their transport.
Transport-specific capabilities are clearly labeled as such
  but not hidden or blocked.
Connection Management has a common API
  but splits to transport specific implementations.
Build from current iWARP branch
  Complete label cleanup.
  Document/Educate on wider semantics.
  Phase in Narrow Windows, FMRs, new attributes …
By concentrating on what is common ULPs can write code that will work on either transport
  without “if (dev->type == iWARP)” lines scattered all over their code.