## Slide 1: IB Management Experiences
Cisco’s view of Sandia T-Bird bringup
Ted Wilcox
tewilcox@cisco.com

## Slide 2: Bringup
Do the bringup in manageable pieces.
We introduced idea of “pods” and did bringup on individual 16-node clusters in parallel.
Started with main SM host, 1 leaf switch, and added cores.
Then added “pods” in groups of 2-8.

## Slide 3: Steps to verify “cleanness”
As new hardware was added, first checked SM to be sure no ports were stuck in INIT, bouncing, or at wrong link width.
Then, ran port counter tests.
Good for detecting bad links, not good at finding things like flakey HW or temperature dependencies.

## Slide 4: Important details
Must get from IB concepts (GUID / switch port #) to user names (rack X chassis Y, port Z) easily.
We spent the first few days automating the gathering of information, and looking it up quickly.
All tools need to agree (SM, standalone tools)
Inconsistency in log output shows up quickly in a big installation. (“:” separated formats, endianness issues, hex vs. decimal, etc.)
Persistent, but updatable information is very important. (Think DB transactions, instead of either static data or current view.)

## Slide 5: SM Performance
Scaling issues weren’t where we expected.
  Was: # outstanding transactions / chip, depth of routing search
  Wasn’t: # of threads available for discovery or routing, receive queue depths
A fast CPU and HCA solve a lot of problems.

## Slide 6: Prosaic items to remember
Network bringup is not the center of the universe; many things are going on at once.
Environmental issues will come up.
  Cosmic ray induced DRAM flips
  Cooling problems or inconsistencies. (Temperature delta between HPL run and idle can be huge.)
  Power issues will come up.
  Data corruption can happen inside CPUs.
Enough off the shelf hardware can be like herding cats. MTBF can be lower than the time a large run takes. This is especially true early on.

## Slide 7: Relationship and Process
It takes more than a standard customer/vendor relationship. We needed help from everyone: our suppliers, our OEM, and the end user.
Enough smart people can solve most problems, but the long-term ones also take a methodical, patient process. We are certainly not done yet.

## Slide 8: Major things to fix:
“tail –f syslog” is bad. We need to be better at generating useful messages, and giving guidance on what events require maintenance.
Checking port counters is central to debugging, but we shouldn’t require customers to open the IB spec to do a large installation.