## Slide 1: SoftIB: A Virtual IB Device for Xen
Jianxin Xiong

## Slide 2: Overview
  SoftIB is:
    A software based IB device for virtualized environment (Xen)
    Built on top of Virtual Machine RDMA Interface (VMRI)
    Implemented as a driver in the OpenFabrics framework
  SoftIB tries to provide:
    An alternative inter-VM comm. mechanism with very good performance
    An environment for testing OFED based applications without the RDMA hardware

## Slide 3: OpenFabrics Software Stack
libibverbs
User-level HCA driver
IB Core (verbs, etc)
HCA Driver
HCA
IPoIB, SDP, SRP
kernel
User-level Access
Kernel
Bypass
uDAPL

## Slide 4: SoftIB Architecture
VMRI
libibverbs
libvmri
IB Core (verbs, etc)
ib_vmri
IPoIB, SDP, SRP
kernel
User-level Access
uDAPL

## Slide 5: Virtualization with Xen
OS
proc1
proc2
VM0
OS
proc3
proc4
VM2
hypervisor
Devices
VM1
OS
Memory, CPU, etc

## Slide 6
Virtual Network Device in Xen
Front end:
  standard interface
  packetizing
Device channel:
  shared ring buffer  requests
  event channel  interrupt
Back end:
  Process request
  copying / buffer flipping
High overhead
VM0
VM1
VM2
NetFE
NetFE
NetBE
src
dst
hypervisor
device channels

## Slide 7: Virtual Machine RDMA Interface
  A RDMA-style inter-VM communication mechanism
  Implemented as a service in the hypervisor
    Hypervisor has access to all the memory pages
    Memory registration required
    Accessible to all the VMs
  VMRI is fast because:
    0-buffering data copy
    Low overhead queue based RDMA protocol
VM1
VM2
hypervisor
VMRI
buf1
buf2
SQ
RQ
A Simplified View of VMRI

## Slide 8: VMRI Components
QPC
MRC
CQC
SQ buffer
RQ buffer
CQ buffer
SQ
RQ
EQC
PDC
EQ buffer
CQ
VM
device
mcast
group
request
processing
hypervisor
data buffer
guest code
hypercall
VIRQ
Notes: MRC (memory region context): list of machine physical pages, size, vaddr, access rights
QPC (queue pair context): send queue, recv queue & corresponding completion queues
CQC (completion queue context)
EQC (event queue context)
PDC (protection domain context)

## Slide 9: Data Moving: Send/Recv
sendbuf
recvbuf
wqe
SQ
cqe
CQ
wqe
RQ
cqe
CQ
mr1
dev1
dev2
mr2
hypervisor
qp1
qp2
direct copy
eqe
EQ
eqe
EQ
optional
optional
VM1
VM2
irq
irq
1
1
2
3
3
4
5
5
6
6

## Slide 10: Data Moving: RDMA Write
localbuf
remote
buffer
wqe
SQ
cqe
CQ
mr1
dev1
dev2
mr2
hypervisor
qp1
qp2
direct copy
eqe
EQ
optional
VM1
VM2
irq
1
2
3
3
4
5
6
Notes: send req contains info about remote buffer.

## Slide 11: Data Moving: RDMA Read
localbuf
remote
buffer
wqe
SQ
cqe
CQ
mr1
dev1
dev2
mr2
hypervisor
qp1
qp2
direct copy
eqe
EQ
optional
VM1
VM2
irq
2
1
3
3
4
5
6

## Slide 12: Data Moving: UD Send/Recv
VM1
sendbuf
recvbuf
wqe
SQ
cqe
CQ
wqe
RQ
cqe
CQ
mr1
dev1
dev2
mr2
hypervisor
qp1
qp2
direct copy
eqe
EQ
eqe
EQ
optional
optional
VM2
irq
irq
1
1
2
3
3
4
5
5
6
6

## Slide 13: Data Moving: UD Multicast
sendbuf
recvbuf
wqe
SQ
cqe
CQ
wqe
RQ
cqe
CQ
mr1
dev1
dev2
mr2
hypervisor
qp1
qp2
direct copy
eqe
EQ
eqe
EQ
optional
optional
VM1
VM2
irq
irq
1
1
3
3
4
5
5
6
6
multicast
group
2

## Slide 14: VMRI API
Through Xen “hypercall” interface:
Group of commands:
DEV (create/destroy/query) PD (create/destroy)
CQ (create/destroy/arm/disarm) EQ (create/destroy/bind)
QP (create/destroy/modify/query) MR (reg/dereg)
MCG (create/destroy/attach/detach) Misc (schedule/debug/status)
HYPERVISOR_vmri_op(
int cmd,
int dev_id,
void * args );

## Slide 15: SoftIB Kernel Driver
function pointers
ib_vmri
ib_core
VMRI
internal
functions
QP table
CQ table
EQ table
PD table
MR table
ib_dev
guest
kernel
VMM

## Slide 16: SoftIB User Mode Driver
function pointers
libvmri
libibverbs
ib user-level access
internal functions
ib core
ibv_cmd_xxx
read
write
ioctl
kernel
bypass
kernel
user
ibv_xxx

## Slide 17: SoftIB Status
  Based on Xen-unstable and OFED-1.2-rc2
  Supported:
    RC and UD transport
    Unicast and multicast
    Basic SA functionalities
    IPoIB, SDP, uDAPL
  Not supported:
    Shared receive queue
    Advanced SA functionalities
    Subnet management
  On going work:
    Testing applications such as NFS/RDMA
    Testing more ULPs such as SRP, iSER

## Slide 18: Performance Evaluation
Hardware:
  Xeon 5160 DP
  4GB Memory (only 2GB is used)
  Motherboard: S5000PAL
Software:
  RedHat EL4U4, CentOS 4.4
  Xen-unstable, cs14774
  NetPIPE, Intel MPI 3.0
Tested Devices:
  SoftIB (rdma, ipoib, sdp), Ethernet (vnif, ioemu), loopback, shm

## Slide 19: Performance Summary
Substantial performance improvement has been observed over the standard virtual Ethernet device:
 | Bandwidth Improvement | Latency Improvment
Para-Virtualized VM | up to 3.5x | 4.7x
Fully-Virtualized VM (IOEMU) | up to 237x | 56x
Fully-Virtualized VM (PV Driver) | up to 4.4x | 8.2x

## Slide 20: Performance Result (1)

## Slide 21: Performance Result (2)

## Slide 22: Performance Result (3)

## Slide 23: Performance Result (4)

## Slide 24
Thank You!