## Slide 1: Experience using Infiniband for computational chemistry
Mark Moraes
D. E. Shaw Research, LLC

## Slide 2: Molecular Dynamics (MD) Simulation
Single, millisecond-scale MD simulations
The goal of D. E. Shaw Research:
That’s the time scale at which biologically interesting things start to happen
Why?

## Slide 3: A major challenge in Molecular Biochemistry
Decoded the genome
Don’t know most protein structures
Don’t know what most proteins do
  Which ones interact with which other ones
  What is the “wiring diagram” of
    Gene expression networks
    Signal transduction networks
    Metabolic networks
Don’t know how everything fits together into a working system

## Slide 4: Molecular Dynamics Simulation
Iterate
Compute the trajectories of all atoms in a chemical system
25,000+ atoms
For 1 ms (10-3 seconds)
Requires 1 fs (10-15 seconds) timesteps
Years on the fastest current supercomputers & clusters
Iterate
1012 timesteps
with 108 operations per timestep
=> 1020 operations per simulation

## Slide 5: Our Strategy
– Designing a specialized supercomputer (Anton, ISCA2007, Shaw et al)
– Enormously parallel architecture
– Based on special-purpose ASICs
– Dramatically faster for MD, but less flexible
– Projected completion: 2008
– Applicable to
• Conventional clusters (Desmond, SC2006, Bowers et al)
• Our own machine
– Scale to very large # of processing elements
Parallel Architectures
Parallel Algorithms

## Slide 6: Why RDMA?
Today: Low-latency, high-bandwidth interconnect for parallel simulation
    Infiniband
Tomorrow:
  High bandwidth interconnect for storage
  Low-latency, high-bandwidth interconnect for parallel analysis
    Infiniband
    Ethernet

## Slide 7: Basic MD simulation step
Each process in parallel:
Compute forces (if own the midpoint of the pair)
Export forces
Sum forces for particles in homebox
Compute new positions for homebox particles
Import updated positions for particles in import region

## Slide 8: Parallel MD simulation using RDMA
For iterative exchange patterns, two sets of send and receive buffers are enough to guarantee that send and receive buffers are always available
Send and receive buffers are fixed and registered beforehand
The sender knows all the receiver’s receive buffers and use them alternately
Implemented with the Verbs interface. RDMA writes are used (faster than RDMA reads).

## Slide 9
Refs: Kumar, Almasi, Huang et al. 2006; Fitch, Rayshubskiy, Eleftheriou et al. 2006

## Slide 10
ApoA1 Production Parameters

## Slide 11
ApoA1 Production Parameters

## Slide 14: Management & Diagnostics: A view from the field
Design & Planning
Deployment
Daily Operations
Detection of Problems
Diagnosis of Problems

## Slide 15: Design
HCAs, Cables and Switches: OK, that’s kinda like Ethernet.
Subnet Manager. Hmm, it’s not Ethernet.
IPoIB: Ah, it’s IP.
SDP: Nope, not really IP.
SRP: Wait, that’s not FC.
iSER: Oh, that’s going to talk iSCSI.
uDAPL: Uh-oh...
Awww, doesn’t connect to anything else I have!
But it’s got great bandwidth and latency...
I’ll need new kernels everywhere.
And I should *converge* my entire network with this?!

## Slide 16: Design
Reality-based performance modeling.
  The myth of N usec latency.
  The myth of NNN MiB/sec bandwidth.
Inter-switch connections.
Reliability and availability.
A cost equation:
  Capital
  Install (cables and bringup)
  Failures (app crashes, HCAs, cables, switch ports, subnet manager)
  Changes and growth
  What’s the lifetime?

## Slide 17: Deployment
De-coupling for install and upgrade:
  Drivers [Understandable cost, grumble, mumble]
  Kernel protocol modules [Ouch!]
  User-level protocols [Ok]
How do I measure progress and quality of an installation?
  Software
  Cables
  Switches

## Slide 18: Gratuitous sidebar: Consider a world in which...
The only network that matters to Enterprise IT is TCP and UDP over IP.
Each new non-IP acronym causes a louder, albeit silent scream of pain from Enterprise IT.
Enterprise IT hates having anyone open a machine and add a card to it.
Enterprise IT really, absolutely, positively hates updating kernels.
Enterprise IT never wants to recompile any application (if they even have, or could find the source code)

## Slide 19: Daily Operation
Silence is golden....
  If it’s working well.
Capacity utilization.
  Collection of stats
    SNMP
    RRDtool, MRTG and friends (ganglia, drraw, cricket, ...)
  Spot checks for errors. Is it really working well?

## Slide 20: Detection of problems
Reach out and touch someone...
SNMP Traps.
Email.
Syslog.
A GUID is not a meaningful error message.
Hostnames, card numbers, port numbers, please!
Error counters: Non-zero BAD, Zero GOOD.
Corollary: It must be impossible to have a network error where all error counters are zero.

## Slide 21: Diagnosis of problems
What path caused the error?
Where are netstat, ping, ttcp/iperf and traceroute equivalents?
What should I replace?
  Remember the sidebar
  Software? HCA? Cable? Switch port? Switch card?
Will I get better (any?) support if I’m running
  the vendor stack(s)?
  or the latest OFED?

## Slide 22: A closing comment.
Our research group uses our Infiniband cluster heavily.
Continuously.
For two years and counting.
Our Infiniband interconnect has had fewer total failures than our expensive, enterprise-grade GigE switches.

## Slide 23: Questions?
moraes@deshaw.com

## Slide 24: Leaf switches and core switches and cables, oh my!
Core switch
Core switch
... 86 more
... 10 more
Leaf switch
12 servers
Leaf switch
12 servers