## Slide 1: Management Tools Development related to DoE
Hal Rosenstock
Notes: Hal Rosenstock <halr@voltaire.com>

## Slide 2: Performance Management
Architecture in management git tree
Tightly coupled to OpenSM rather than separate daemon
  Easy to find its location
  Leverage OpenSM infrastructure
  Can disable SM ? so run perf mgr only

## Slide 3: Performance Management
Obtain current topology from SM and monitor changes in topology as basis for tracking performance
  Perhaps configure node types of interest
    All, switches only, CAs only,
Poll counters periodically to determine rate of change

## Slide 4: Performance Management
Gather performance data (for subsequent report production)
  Format TBD
Flag events in log
  Configurable thresholds to determine events
    Events can be disabled by configuring their thresholds to max
  Used to determine
    “Problem” links
    Hot spots

## Slide 5: Performance Management
Also, counters can be reset
  Automatic policy (when counters close to sticky max value)
  On demand ?
  With reset logged
  Reset time per node (and possibly port as well) available

## Slide 6: Diagnostics
Pelaton cluster install experience
  Aside from performance manager
Enhancements to diag tools and scripts
  OFED 1.2 and beyond
Additional Perl scripts and installation improvements
  Work done by Ira Weiny & Albert Chu

## Slide 7: OFED 1.2 Diagnostics
Ibportstate
  Port reset, enable, disable
  Speed SDR
Additional saquery options
  CA by NodeDescription (name)
  Unique LID for name
  PathRecord by src/dest name
  Get SA ClassPortInfo

## Slide 8: OFED 1.2 Diagnostics
perfquery support for PortCountersExtended
vendstat
  IS3 general information
  IS3 port transmit wait counters
IB router support
  ibnetdiscover
  ibtracert
Switch map support
dump_mfts.sh

## Slide 9: OFED 1.2 Diagnostics
New Scripts
  ibfindnodesusing
    find a list of nodes which are routed through switch:port
      Attempt to find the nodes which might be affected by errors seen on that link/port
  ibprintca, ibprintswitch
    print only the ca/switch specified from the ibnetdiscover output
      Make "grepping" ibnetdiscover output easier
  ibswportwatch
    Attempt to diagnose a problem on a port
      Look for rates of change of error counters
      Will be deprecated by the performance manager

## Slide 10: OFED 1.2 Diagnostics
New scripts (cont’d)
  iblinkinfo
    Report link speed and connection for each port of each switch that is active
      Nice "sysadmin readable" output for all the information of all the links
      Combines output of the "lower level" diags into a "per link" output
      Also supports one line per link which is parseable by other tools

## Slide 11: OFED 1.2 Diagnostics
New scripts (cont’d)
  ibfinderrors
    Report counters on all switches in subnet
      Example output for -r (report port info) option: Errors for 0x0008f10400411b18 ""wopr switch" base" 1: [RcvSwRelayErrors == 10] Link info: 2 1[ ] ==( 4X 5.0 Gbps)==> 0x0002c90200219e64 1[ ] "wopri" Helps to determine what the other end of the link is. In this case, the link is connected to the node "wopri”

## Slide 12: OFED 1.2 Diagnostics
See man pages for more description and options available
Thanks to Ira Weiny and Al Chu for their many contributions

## Slide 13: Additional Diagnostics
Add LID/GUID to the error output in diag scripts for easier parsing
Enhance diag check script(s) to identify
  DDR capable peer ports not operating at DDR
  12x capable peer ports not operating at 12x
New diag capabilities to detect additional inconsistencies
  Duplicate port or node GUIDs
  Duplicate LIDs
  Zero value LIDs

## Slide 14
Thank You