## Slide 1: OFED 1.2 Management Update
Hal Rosenstock
Notes: Hal Rosenstock <halr@voltaire.com>

## Slide 2: OpenSM for OFED 1.2
Release Info
  git://git.openfabrics.org/~ofed_1_2/management.git
  openib-3.0.11 (OFED 1.2 rc3)
Currently used as basis for Pelaton cluster
New Functionality
Bug Fixes

## Slide 3: New Functionality
Routing improvements
SA optional record support “virtually” complete
IB router enablement
SA database dump/restore

## Slide 4: Routing Improvements
Performance improvements of over an order of magnitude
  Min hop
  Up/down
New routing (pathing) algorithms
  Fat Tree (Mellanox contribution)
  LASH (Simula contribution)

## Slide 5: Fat Tree Routing
Optimizes routing for congestion free “Shift” communication pattern
Deals with Fat Trees of various types
  Symmetrical
  Not just K-Ary-N-Trees
    Non constant K
    Not fully staffed
  Any CBB ratio
Automatically detects whether the topology is a Fat Tree
Provides
  LFT tables assignment
  MPI “rank” file of hosts
    Can be used for creating topology-aware communication patterns

## Slide 6: LASH – LAyered SHortest path
All dependency cycles found over the physical links are broken by separating the involved routes using “virtual layers”.
Within each layer, the routing function is deadlock free, but incomplete.
By restricting packets to one virtual layer, the complete routing function across all layers remains deadlock free.
Layers are not just a QoS issue! LASH can also be implemented with QoS
Deterministic, all packets follow shortest paths (can be extended to also support multipath routing).
Origin:
  2002, Simula Research Laboratory, Oslo, Norway.
  Tor Skeie (tskeie@simula.no), Olav Lysne (olavly@simula.no)

## Slide 7: LASH – the method (roughly)
Calculate shortest paths between all source / destinations
For each path, for all <source, destination> pairs
  find a virtual layer i that the current path can be assigned to without closing a dependency cycle in the (current) routing function for layer i.
  if such a layer cannot be found, create a new layer.
Once complete, lower numbered layers tend to be over represented with paths so a balancing stage is carried out to distribute an equal number of paths between each layer
The resulting algorithm is a deadlock free minimal path routing algorithm.

## Slide 8: LASH – Status in OpenFabrics
Added to OFED 1.2 branch as experimental in January ’07. Now transitioned from experimental.
One upcoming commercial offering using OpenFabrics will employ LASH
Further improvements requried to bring number of layers down. Mesh (any size) requires on 1 layer. Torus 10x10 requires 4 layers for independent paths and 8 layers for double paths (return path in the same layer). This can be improved and will scale. man page has details on layer requirements
The need for virtual layers is independent of the number of end nodes (HCAs); HCA does not need to support more than 1 VL
LASH resource web page under development at Simula
Notes: I think it’s important to state that the version of LASH in OpenFabrics can be improved upon. We have looked at reducing the number of layers for torus and it can come down to 2, we believe for torus of any size. It will be be up to industry to decide if this is something that should be done.
Simula will develop a resource page and a wikipedia entry that describes LASH.

## Slide 9: Performance LASH versus Up/Down
LASH avoids the congestion problem associated with the root node that is prevalent in Up*/Down* and supports minimal routing
LASH requires the use of Virtual Layers
Up*/Down* does not
Throughput plot comparing the performance of LASH an Up*/Down*. 128 switches were interconnected as a mesh for the experiments
Notes: The graph on the righthand side shows a typical throughput plot comparing LASH and Up/Down. The reason LASH outperforms Up/Down is that it avoids sending traffic through the root. A consequence of this is that LASH also ensure minimal path routing, while Up/Down can not.
So it 1. avoids a root and 2. ensure minimal path routing.
But to achieve this you need layers so LASH can replace Up/Down in technologies with Layers

## Slide 10: SA Optional Record Support
InformInfo improvements
InformInfoRecord, MulticastForwardingTableRecord, and SwitchInfoRecord added
SMInfoRecord now supports all SMs
  Not just local SM
Missing ServiceAssociationRecord
  Also, TraceRecord

## Slide 11: IB Router Enablement
Experimental
  ROUTER_EXP not enabled in build by default
  Much of IBA missing for routers
Fix handling of router ports
Support for off subnet GIDs in SA PathRecord
Support for non link-local scope in MGID in SA MCMemberRecord

## Slide 12: SA Database Dump/Restore
SA registrations can be dumped/restored
  Multicast
  Services
  Events
opensm-sa.dump in /var/log by default
-S option with dump file restores SA database
  If restoration successful, no client reregister

## Slide 13: Additional New Functionality
Socket support for console
Log rotation while running
Scope support in partition configuration for IPoIB multicast groups
Option to force SDR link speed

## Slide 14: Bug Fixes (since OFED 1.1)
See OFED 1.2 OpenSM release notes for details
Also, for non compliances

## Slide 15: Upcoming (beyond OFED 1.2)
More routing performance improvements
  Even more speedups
Better packaging/installation
“Native” daemon mode
Performance management
Quality of Service manager
  Based on IBTA annex soon to be released

## Slide 16: Needed
Better IPv6 solicited node multicast (SNM) handling
  Multiple groups share same MLID
NodeDescription changed trap handling
“Selected” IBA 1.2.1 enhancements
Handle local events ?

## Slide 17: Futures
Many things
  More improvements
    Core
    Routing algorithms
  Continued improvements in Stability and Scalability
    More tests and testing
    Larger cluster experience
What do you think is needed ?
What would you like to see added ?

## Slide 18: Diagnostics
Many improvements since OFED 1.1
  Covered in DoE tools talk
ibdiagui
  GUI for ibdiagnet
    Used at SC06
  Mellanox contribution
  Part of ibutils package
    git://git.openfabrics.org/ofed_1_2/ibutils.git

## Slide 19: ibdiagui

## Slide 20: Related
ibsim
  OpenSM and OpenIB diags work unmodified on this
    uses ibnetdiscover format for topology
  Voltaire contribution
  Not part of OFED 1.2
  git://git.openfabrics.org/~sashak/ibsim.git

## Slide 21
Thank You

## Slide 22
Backup

## Slide 23: Other technology from Simula
MRoots
  Use multiple Up*/Down* trees each with their own root in different layer. Reduces root congestion problem
LASH-TOR
  Transition Orientated LASH, an extension to reduce the number of virtual channels required for LASH by using transitions between virtual layers
FRoots
  Fault tolerant routing using layers to ensure fabric stays connected in the face of a fault. This works and could be implemented for InfiniBand
Please contact Tor Skeie (tskeie@simula.no) or Olav Lysne (olavly@simula.no) for further details
Simula Research Laboratory is a state funded research lab that conducts basic research in the fields of communication technology, scientific computing and software engineering. Simula focuses on fundamental scientific problems with a large potential for important applications in society. http://www.simula.no/