## Slide 1: OFED Usage in VMware Virtual Infrastructure
Anne Marie Merritt, VMware
Tziporet Koren, Mellanox
May 1, 2007 Sonoma Workshop Presentation

## Slide 2: Agenda
OFED in VMware Community Source
OFED Components Used
Integration Challenges
Enhancements in ESX kernel and drivers
How the components fit in VMware ESX
I/O consolidation value propositions
Virtual Center management transparency

## Slide 3: OFED in VMware Community Source Development
InfiniBand with OFED – one of the first projects in VMware community source program
Active development by several InfiniBand vendors
Leverage community-wide development and vendor interoperability
Virtual Infrastructure (ESX) based product in the future

## Slide 4: OFED Components Used

## Slide 5: IB Enablement in ESX
OFED Linux based drivers used as basis
Device driver, IPoIB and SRP (SCSI RDMA Protocol)
Storage and Networking functionality
Looks like regular NIC or HBA
VMotion is supported
Subnet Management agent functionality
Sourced from OpenFabrics Alliance (www.openfabrics.org)
Uses 2.6.19 kernel API

## Slide 6: The Challenges
ESX Linux API is based on a 2.4 Linux Kernel
  Not all the 2.4 APIs are implemented
  Some 2.4 APIs are slightly different in ESX
  Different memory management
  New build environment
Proprietary management for networking and storage

## Slide 7: Enhancements or Optimizations
ESX kernel changes
  Common spinlock implementation for network and storage drivers
  Enhancement to VMkernel loader to export Linux-like symbol mechanism
  New API for network driver to access internal VSwitch data
  SCSI command with multiple scatter list of 512-byte aligned buffer
  Various other optimizations
InfiniBand driver changes
  Abstraction layer to map Linux 2.6 APIs to Linux 2.4 APIs
  Module heap mechanism to support shared memory between InfiniBand modules
  Use of new API by network driver for seamless VMotion support
  IPoIB working with multiple QPs for different VMs and VLANs
  IPoIB was modified to support the ESX NIC model
  Limit one SCSI host and net device per PCI function

## Slide 8: InfiniBand with Virtual Infrastructure 3
Transparent to VMs and Virtual Center

## Slide 9: VM Transparent Server I/O Scaling & Consolidation
VM
VM
VM
VM
Virtualization Layer
VM
GE
FC
GE
GE
GE
FC
VM
VM
VM
VM
Virtualization Layer
VM
IB
Typical Deployment Configuration
IB
With Mellanox InfiniBand Adapter
~3X networking, ~10X SAN performance
Per adapter performance. Based on comparisons with GigE and 2 Gb/s Fibre Channel

## Slide 10: SRP SAN Performance from VMs
Same as four dedicated 4Gb/s FC HBAs
128KB Read benchmarks from four VMs

## Slide 11: Using Virtual Center Seamlessly
Storage configuration
vmhba2

## Slide 12: VMware Contact
For further information please contact your VMware account team
Notes: <number>

## Slide 13: Thank You