## Slide 1: Customer Experiences
Requirements from Financial and Database Enterprise Customer
Notes: This is an OFED presentation, not just IB.

## Slide 2: Application Requirements
Financial Services
  How to handle 300,000+ Messages/Second?
  How to guarantee bounded latency?
  How to assure up time?
Database
  How to feed modern multi-socket multi-core CPUs?
  How to configure for bounded transaction times?
  How to assure up time?
Notes: OS Bypass is the key to controlling latency and supporting high transaction rates
- RDP, User space multicast, SDP/WSD.
- MPI is nice for HPC, but not used by many commercial customers
- Consider polling; with multi-socket multi-core CPUs you can afford to burn one…
Bounded latency
- Must bound jitter, even under heavy load.
- What the jitter bounds are, is less important than knowing them.
IB attached storage
- Easily supports 1200 MB/sec per-HCA (dual port)
- 2 HCAs provide 2400 MB/sec; 3 HCAs start to hit other limits
- DDR is good for HA; one port can handle full data rate
- Cheap 2U-3U SRP (and iSER) targets support 300 MB/sec random IO with RAID-5
- Current Multicast performance is 1,500,000 1500 byte frames/second.

## Slide 3: Environment
High Availability
  No single point of failure as a starting point
    Hardware and drivers
  2x hardware
    Even when a “unit” is internally HA (IT group requirement)
  Deterministic performance
    Must provide a scaling model
  All errors must be detected, reported, and handled.
Security
  OFED must not introduce any new security issues
Manageability
  IB management must be transparent
  Need casual tracing / sniffing for SDR, DDR, QDR
Notes: You need to target the IT guys. They own the environment you will be installing into. They are responsible for HA, security, and managing the environment. They know Ethernet and maybe FC. They do not know IB.
10 GigE + iWARP + RNICs along with the appropriate switching fabric is a much easier sell into many commercial accounts. Having IB available for top end performance and lowest cost is a good story, but OFED is the key to selling to the IT guys.
Expect to be tested. Cables will be pulled. Nodes, switches, bridges (FC and Ethernet), and storage will be unplugged. Your HA must be HA.

## Slide 4: Spotlight OFED
IB is not a selling point
  Nobody wants another fabric
  OFED supports IB and 10GigE
Customers love
  Performance
  Determinism
  Scalability
Customers hate
  Complexity
  New management or monitoring software
  New wires
Notes: Commercial customers will not get locked into one vendor long term.
If a vendor requires the customer to use their IB stack:
- Stack must not depend on vendor SM
- Stack must interoperate with other vendor stacks
- Stack must interoperate with OFED
Think of IB stacks like IP stacks. If you must create, test, support, and ship your own stack for some reason, you must assume (and test) that your stack interoperates with other subnet managers and stacks. At a minimum this means OFED.
UNH and certification is important here

## Slide 5: What OFED IB Provides
An IO fabric
  OFED provides access to IO
    Ethernet
    Storage (Direct attach and through FC)
  IPoIB is nice (reduces wires), but GigE and 10 GigE is more comfortable.
Performance
  1, 2, and 4 GB/sec with 1.2 uS ping times
Notes: As an industry, we need to focus on seamless integration of IB and existing infrastructures. High port count DDR IB switches are useful and required, but commercial customers do want to see them, manage them, or even know they exist.
Commercial customers care about cheap, high performance, low and bounded latency access to their existing data and infrastructure. They want to perform more of the same tasks tomorrow that they do today but faster, cheaper, and with higher reliability. They do NOT want to manage a new fabric. They will not sacrifice security.
Performance needs to be measured using industry (and customer…) specific benchmarks

## Slide 6: OFED Enhancements
High Availability
  More testing of HA IPoIB and SRP
  Better path ordering or limiting by SA
  Leverage alternate path support
OS Bypass
  Add user space multicast
  Detect and make use of multiple cores (polling!)
New features
  IPoIB offload exploitation
  Virtualization (Xen, VMWare, etc.)
  10 GigE and FCoIB support on new Silicon
  Full boot support (PXE, Int13, Linux, Windows, etc.)
Notes: Test plans and regression buckets are as important as code.
Boot includes BIOS extensions and stack support. Windows is important.

## Slide 7: OFED Management
Model is APIs to integrate fabric management into existing frameworks.
  Example standalone management code for unit test
IB SM/SA management enhancements
  External APIs to feed policy and policy exits
    Partition membership, 3rd party policy exit IPC, etc.
  Policy “exits” or “plug-ins”
    Partition membership, path ordering, SDR/DDR/QDR management, node/port setup profiles, etc.
Automatic fabric diagnostics and alert management
  Verify topology, rates, link widths, etc.
  Monitor counters to detect path errors and flaky hardware.
  Integrate reporting with existing frameworks
    SNMP, CIM, etc.
Standard device management APIs
  Reference devices (next page), management APIs, and example code.

## Slide 8: OFED Devices
Routers
  Required for distance and administrative control separation
Software network monitoring tool
  “Ethereal for IB”
IB to Ethernet Bridges
  Required for datacenter integration
  VLANs/Partitions, LACP, IGMP snooping, etc.
Storage Bridges
  Local storage, iSCSI, and FC bridging
  IB Partition support, LUN masking, etc.
Notes: Devices must provide HA, management APIs, etc.
Reference devices (Linux appliances?) would be a good way to provide, an interoperability target, and establish management APIs. Vendors are then free to create value add devices that are differentiated on price, performance, features/functions, HA, etc.