## Slide 1: IB Cross-Subnet Communication
OpenFabrics Alliance Workshop
May 1st, 2007

## Slide 2: Why IB Routing?
Scalability
Local address space reuse
Containment of failures and topology changes
Confinement of fabric management scope to subnets
H1
H2
HM
…
Subnet M
SM/SAM
H1
H2
HN
…
Subnet N
SM/SAN
H1
H2
HQ
…
Subnet Q
SM/SAQ
Router-3
Router-1
Router-2
H1
H2
HN
…
Subnet P
SM/SAP

## Slide 3: Introduction and Agenda
IBTA Working on IB Cross-Subnet Communication Spec
  Past Work
Agenda
  Scope
  Guidelines
  Problem Partitioning
  Advanced Topics

## Slide 4: Scope and Phased Approach
Limiting Scope via..
  Topology Restrictions
  Intermediate Solution Simplifications
    e.g. Static Routing Tables
Market Guidance
  OFA Feedback Requested
H1
H2
HM
…
Subnet M
SM/SAM
H1
H2
HN
…
Subnet N
SM/SAN
H1
H2
HQ
…
Subnet Q
SM/SAQ
Router-3
Router-1
Router-2
H1
H2
HN
…
Subnet P
SM/SAP
Router-1

## Slide 5: IB Routing Guidelines
<number>
Layered Architecture
Leverage from the IP world whenever possible
SM is a Subnet Local Entity
Preserve Existing IB Management Infrastructure
Interoperability
H1
H2
HM
…
SM/SAM
H1
H2
HN
…
SM/SAN
Router
Switch
Switch
Switch
Switch

## Slide 6: A Day in the Life of Cross-Subnet IB Traffic
Assume Network is Setup and Configured
Connection Setup
  Endnode Needs
    GID for destination (DGID)
    Local Subnet GID (next hop for DGID)
    Local Subnet Path Parameters for next hop GID (DLID, SL)
    Global Path Parameters (P_Key, MTU, Static Rate, Q_Key)
    End to End CM
  Router
    No special involvement. Cross-subnet CM packets are treated just like regular packets

## Slide 7: A Day in the Life… (cont’d)
Mainstream Operation
  Endnode: No changes from intra-subnet case
    Address Vector is agnostic to whether parameters are local or global
  Router:
    Receive Packet
    Strip LRH
    Compute next hop GID (from packet DGID)
    Obtain Local Subnet Path Parameters for next hop GID
    Append new LRH
    Transmit Packet

## Slide 8: Problem Partitioning
Global Network Setup and Management
  Global Parameters Management
  Establishing Routes
  Monitoring, Statistics, Debugging
Connection Setup
  Global Name Resolution
  Global Path Parameters Discovery
  Cross Subnet CM
Mainstream Data Transfer
  Routing Decision
  L2 Address Resolution
  Cross Subnet IB Transport Protocol

## Slide 9: Global Network Setup and Management
Global Parameters Management
  MTU, P_Key, Q_Key, Static Rate
Establishing Routes
  Deadlock Avoidance
  Routing Protocol
    Including Inter-router messaging format and protocol
    …or Static Routing
Monitoring, Statistics, Debugging

## Slide 10: Global Name Resolution
Goal: Map Service Name to GID
Impacts
  Routers
    None
  Endnode
    IB DNS Query
  Management Infrastructure
    Name Resolution Service

## Slide 11: Global Path Parameters Discovery
Goal: Obtain Global Path Parameters for Inter-Subnet Traffic
  Path MTU, Static Rate, P_Key, Q_Key
Some Possible Approaches
  Global Manager Query
    Requires GM Sync with Routing Protocol
  Probed Discovery
    Limits Runtime Global Policing
    Orthogonal to whether global or distributed
Impacts
  Router
    GMQ: N/A
    PD: participates in the protocol
  Endnode
    GMQ: Query GM
    PD: initiates pre-CM probe
  Management Infrastructure
    GMQ: Responds to Queries
    PD: Setup only

## Slide 12: Routing Decision
Goal: Given a DGID obtain next hop GID
  Amazingly similar to IPv6 routing function
Impacts
  Router
    Routing Table Lookup
  Endnode
    Routing Table Lookup or Query External Agent
  Management Infrastructure
    None

## Slide 13: L2 Address Resolution
Goal: Map Subnet Local GID to IB L2 Address
Impacts
  Router
    PathQuery to the SA
    Caching
  Endnode
    PathQuery to the SA
  Management Infrastructure
    None

## Slide 14: Advanced Topics
Multicast
  Setup and Management
    Group Membership Protocol
  Mainstream Operation
    Packet Replication
Global QoS
Load Balancing
High Availability
Congestion Control
Fault Containment

## Slide 15: Call to Action
IBTA LWG Charter (joint work with MgtWG)
Plan
  Step 0: Scoping
  Step 1: Near Time Solution
  Step 2: Full Blown Solution
Join the IBTA to Participate in the Definition
  www.infinibandta.org