## Slide 1: InfiniBand Routing in OFA
Jason Gunthorpe – Obsidian
Sean Hefty – Intel
Hal Rosenstock – Voltaire
Notes: Hal Rosenstock <halr@voltaire.com>
Jason Gunthorpe <jgunthorpe@obsidianresearch.com>
Sean Hefty <sean.hefty@intel.com>

## Slide 2: What Works
Prototype wire-speed 2 port Obsidian router:
  SC|06 XNET demo with Qlogic and Mellanox
  Non-CM RDMA flows
AFCEA|07 Obsidian demo with Rackable:
  Unicast IPoIB traffic between two subnets
Longbow XR
Longbow XR
Optical Fiber
Host
Subnet B
Host
Subnet A
Two Port Router
Notes: SC|06 = Supercomputing 2006, Tampa.
AFCEA|07 = Armed Forces Communications and Electronics Association 2007, West

## Slide 3: Problem Areas
QP Lid Matching
IB CM
Multipath / APM
IPoIB
Multicast Scalability
RDMA CM Addressing
Router / SA Communication
Link Flow Control

## Slide 4: QP LID Matching
C9-57 requires QP to verify LRH:SLID/DLID
Mixes OSI layers 2 (LID), 3 (GID) & 4 (QPN)
Major problem for LMC > 0 or multiple routers
Eliminate matching?
  May break existing HW/FW
Most Pressing Issue
Notes: Routers must vary the LRH on a QP by QP basis and match the expectation established by CM when it configured the QP.

## Slide 5: QP LID Matching
Router
LMC=1
CA
DLID=2
DLID=3
QP3 Forward
DLID=3,SLID=1
DGID=B
QP2 Forward
DLID=2,SLID=1
DGID=B
Router
LID=3
Router
LID=4
CA
A
CA
B
Return path with mismatched
router SLID
Return path requires
SLID=3 for QP3 and
SLID=2 for QP2
QP4 Forward
DLID=3,SLID=1
DGID=B
QP4 Return
DLID=1,SLID=4
DGID=A
Notes: When used with a > 0 LMC the CA can select multiple DLIDs for the router
Due to C9-57 the router must choose the DLID selected by the CA for the LRH.SLID in packets on the return path for that QP.
When used with multiple routers (independent or otherwise) the forward path router input port must match the return path router exit port to meet the LID requirement. In the case of independent routers this can become dependent on choices made on the remote subnet.

## Slide 6: IB CM
Spec requires active side select paths
  Must learn passive side path
  Specify active & passive side LIDs
  4 paths in total
Passive side path carried in REQ
Requires inter-subnet coordination
May require protocol changes to avoid
How does the passive side obtain LIDs?
Notes: If C9-57 remains the active side must select all the LIDs
Otherwise passive side LID selection causes a problem for APM and requires more intelligent targets

## Slide 7: Multipath / APM
Routers required to produce different LRHs to same port
  Must be predictable and based on GRH
  Use DGID, FL, TC fields to select LRH
CM / SA must know GRH to LRH mappings
APM must select paths that are independent
  Harder if APM failover is between routers
Needs Specification
Notes: Having the router randomly select LRHs based on some internal policy is good for load balancing but not for failover. Failover works best if the forward and reverse paths use the same physical links while the primary and alternate paths use maximally independent links.

## Slide 8: Multipath / APM
Router
Router
CA
CA
Good Primary/Secondary
Bad Primary
Router
CA
Bad Path uses all switches/routers
Fails completely if any link fails
Notes: With QP LID matching APM becomes somewhat simpler since the routers have to follow the selection made by the CA which can choose forward and reverse paths that are good for failover.
If the router selects paths completely independently from the subnet then APM for failover becomes difficult.

## Slide 9: IPoIB
Currently uses link local scope for multicast groups
  Prevents crossing routers
Need this configurable per interface
Inter-subnet multicast groups need to agree on parameters
Scalability issues
  IPv6 solicited node multicast
  IPv4 ARP broadcast
IB routers likely to provide IP routing for scalability
Notes: - IPoIB
+ Current implementations use a link local scope for multicast
groups - prevents crossing routers
+ Need more software support to make this per-interface configurable
+ Inter subnet multicast groups need to agree on parameters
+ IPv6 solicited node multicast is a huge scalability problem.
One multicast group per IPv6 address shared across the entire routed
IB network = potentially tens of thousands of multicast groups in the
routers.
+ IPv4 on the other hand broadcast ARPs to potentially tens of thousands
of hosts.
+ Many SMs today do not handle IPv6 solicited node multicast
groups very well. Runs out of MLIDs.
** IB routers probably also have to do IP routing to provide scalability.

## Slide 10: Multicast Scalability
Which MC groups must an SA know about?
RFC 4391 (sec 10) solution for IPoIB scalability
  Interaction with native IB apps?
All routers MC group not native IB concept
How can this be optimized?
Uncertainty on SA, router & IPoIB MC interaction
Notes: - Multicast Scalability
+ Does every SA need to know every multicast group in the entire routed
network?
+ RFC4391 section 10 perscribes a solution to the scalability for IPoIB,
but how does this interact with native IB apps? All routers multicast group
is not an IB native concept.
+ How can this be optimized?
** Uncertainty on how multicast works together between SA, router and ipoib

## Slide 11: RDMA CM Addressing
Unscalable to span IPoIB across routers
RDMA CM uses ARP to learn remote GID
  Limited to single IPoIB subnet
Expand RDMA CM beyond IPoIB subnet
Use GID addressing with IPv6 DNS/etc?
Discover GIDs without using ARP?
Notes: Small environment can use a single IPoIB subnet and make use of RDMA CM. We predict larger networks will have the scaling issues identified in the prior two slides

## Slide 12: Router / SA Communication
Unicast and multicast routing protocols
Router to host or SA prefix advertisement
Inter-subnet coordination
  PKey, TClass (QoS), SA services
Multicast memberships
Least Pressing Issues
Needs Specification
Notes: Existing routing protocol solutions from IPv6 should work acceptably.
The extent that the SA and router should be coupled is unclear.
Supporting APM for fail over complicates this issue

## Slide 13: Link Flow Control
Implementing in routers can lead to dead lock
  Depends on per-subnet routing, not routers
No flow control leads to packet loss
  Even small loss affects IB RC performance
Need Solution
Router
Traffic to router and
traffic from router
on same VL/Link
Form half a network
Cycle.
Notes: Very simple network configurations (ie 1 switch, 1 router port) are safe, but more complex arrangements cause problems

## Slide 14: Final Thoughts
IB intra-subnet traffic has centralized control within the SM
IB inter-subnet needs to be decentralized to scale well
Retaining the unique features of IB will require different approaches from Ethernet/IP

## Slide 15: Go Forward
Work-arounds to allow more testing
Software router for experimentation?
  Linux, commodity HCAs
Device Implementers: Follow Specs
More IBTA Specifications Needed
GMPs can have GRHs
Path records can return global paths