## Slide 1: iSER Storage Target
Yaron Haviv, CTO, Voltaire
yaronh@voltaire.com

## Slide 2: Agenda
iSER storage target – definition
  Product functions
  Status
Compatibility
  OFED 1.1
  Current limitations
Case study

## Slide 3: What is it? FalconStor IPStor with IB Target
Intelligent router
  iSER to FC routing
  Management
  Storage virtualization
  Data protection – mirroring, replication
Internal storage target
  Enable commodity disk attach
  Present native iSER target
  Advanced services available but not required

## Slide 4: FalconStor IPStor InfiniBand added to host connection
InfiniBand / RDMA
iSER Target Connectivity

## Slide 5: IPStor Management
Extensive GUI, SNMP, and CLI support
iSER clients managed just like iSCSI clients
  IpStor supports both iSER and iSCSI/IPoIB seamlessly

## Slide 6: System Requirements / Compatibility
Host | 
O/S | RH5 SLES10
Initiator | OFED 1.1
HCA’s | Mellanox, Voltaire
Server – both gateway and target appliance | 
O/S | RH4u2 (RH5 end April)
IPStor | V 5.1 build 5182 or higher
Voltaire | iSER target driver
HCA’s | Mellanox, Voltaire

## Slide 7: Case Study – Production Customer
Low-latency network providing market data to variety of end users
Required low latency storage, with minimal budget
Decide on commodity storage appliance enabled by software from Voltaire, FalconStor.
Cross mirroring to protect from hardware failures
Initial hardware:
  2 x RedHat Enterprise Servers (Targets)
  Quad 8000 series AMD procs, Tyan motherboard
  48 x 750 GB SATA II drives
  3 x 24 port Areca PCI Express cards
  1 x Voltaire DDR Infiniband dual port card

## Slide 8: Available today – box level failover
InfiniBand
FibreChannel
IB-FC Gateway
X

## Slide 9: Available early May
InfiniBand
FibreChannel
IB-FC Gateway
X
Fully redundant path
Transparent failover

## Slide 10: Infiniband Performance rates:
3 SDR Clients, one DDR Target:
  1400MB/s (close to PCIe Limitation)
  Use 4 FC 4Gb Ports and Enterprise FC RAIDs as the backend
1 SDR Client, 2 Targets
  850MB/s (close to SDR Limitation)
 | Throughput | I/O Response time
Sequential Reads 100% | 635 MB/s | 0.033 msec
Sequential Reads 50% and Writes 50% | 438 MB/s | 0.067 msec
Sequential Writes 100% | 742 MB/s | 0.033 msec
1 SDR Client, 1 SDR Target, Native Storage