## Slide 1: Novell® Infiniband and Virtualization VM-IB project
  Patrick Mullaney

## Slide 2: Infiniband, and Virtualization
Background
  Virtualization technologies attempt to abstract access to I/0 in order to share access to devices and generalize guest OS driver support
    Device emulation
    Paravirtualized drivers
  Infiniband technologies allow low overhead by bypassing the OS stack(OS bypass) and providing direct but abstracted access to ib devices
  Combining these ideas is the goal of this project

## Slide 3: Xensource: XEN-IB history
XEN-IB tree at xensource is a proof-of-concept implementation of VMM-bypass
In VMM-bypass, the guest performs control path operations in a paravirtualized manner but then performs data-path operations directly on the HCA
Original work done by IBM Research and Ohio State

## Slide 4: VM-IB
Implementation
  Paravirtualized driver approach for control operations
    CQ, QP creation, memory registration, etc.
    event handling
  Direct access for data path operations (VMM-bypass)
    QP access
    CQ polling

## Slide 5: VM-IB: block diagram

## Slide 6: VM-IB Status
Project status
  Code integrated as a set of 3 patches to OFED 1.1build
  Reorganized XEN-IB guest HCA driver to separate common code from hardware dependent parts ( 1 patch to mthca)
  IPoIB working
  Guest user level access to ib verbs layer working
  Support for VM migration
  x86_64 is now supported
  Download from openfabrics soon

## Slide 7: Standard Benchmarks
IB Performance Tests
  Guest throughput and latency results show little difference to native OS
Netperf
  Guest performance shows little difference when compared to native OS
  Guest tcp round robin performance nearly doubles over netfront/netback driver

## Slide 8: VM-IB Status
Problems and limitations
  Guest access to IB management (SA, CM) not fully supported
    Completion of MAD proxy will enable and development is rapidly progressing
  Locking holding problem on HCA resource destroy
  Portions of the code VMM aware(e.g. XEN)
  Paravirtualized driver messaging layer is currently limited to homogeneous environments. Can't mix x86_64, i386, windows
  Security problems
    physical pages when registered from guest
    guest access to UARs via ioremap
  bugs

## Slide 9: Next Steps

## Slide 10: Guest IB Management and Migration
IB management
  Full access to IB Management for guests
ISER support
VM Migration
  IPoIB working across a migration
    Teardown and re-establishment of HCA resources
    currently unstable (bug in base xenbus code causes a crash)
  User-level IB applications will require that suspend/resume notification be extended to user space
    applications will need to respond to notification with a notification complete before migration can proceed

## Slide 11: IVMC: Slow-Path Communication (“IPC”)
Inter-VM communication (IVMC) API will allow reliable, in-order, connectionless datagrams to be exchanged between VMs (Guest to Host, Guest to Guest, etc).
  Common API allows VM-IB layers to remain VMM agnostic
  API will map to underlying VMM technology where applicable
Basic primitives of send() and recv() offer various modes of IO completion:
  asynchronous – non-blocking with completion-notification
  synchronous – blocking at the VMM layer
  sleepable-synchronous: blocking in guest stack to allow inter-task parallelism where applicable.

## Slide 12: IVMC (Cont)
Data Marshaling to manage VM-IB message structure
  based on a standardized data-representation format TBD (e.g. XDR)
  creates platform neutrality (32 bit guest on 64 bit host, etc)

## Slide 13: Security
Memory Management
  Host validates ownership of memory registrations from guest
    Guests must register memory regions via control path (IVMC)
    usage of reserved Lkey disabled for guests
  Guest access to “User access regions”
    allocated by a guest via host OS
    Host backend driver reserves region for guest during allocation
    only the guest that performed the allocation will be allowed to map the region into its address space (ioremap)

## Slide 15
Unpublished Work of Novell, Inc. All Rights Reserved.
This work is an unpublished work and contains confidential, proprietary, and trade secret information of Novell, Inc. Access to this work is restricted to Novell employees who have a need to know to perform tasks within the scope of their assignments. No part of this work may be practiced, performed, copied, distributed, revised, modified, translated, abridged, condensed, expanded, collected, or adapted without the prior written consent of Novell, Inc. Any use or exploitation of this work without authorization could subject the perpetrator to criminal and civil liability.
General Disclaimer
This document is not to be construed as a promise by any participating company to develop, deliver, or market a product. Novell, Inc., makes no representations or warranties with respect to the contents of this document, and specifically disclaims any express or implied warranties of merchantability or fitness for any particular purpose. Further, Novell, Inc., reserves the right to revise this document and to make changes to its content, at any time, without obligation to notify any person or entity of such revisions or changes. All Novell marks referenced in this presentation are trademarks or registered trademarks of Novell, Inc. in the United States and other countries. All third-party trademarks are the property of their respective owners.