## Slide 1: InfiniBand Routing Solution Approach
Yaron Haviv, CTO, Voltaire
yaronh@voltaire.com

## Slide 2: Getting To The Other Subnet
Subnet A
Subnet B
SM
SM
DGID -> Router DLID ?
Send to Router
Send to Next Hop
DGID -> DLID ?
Send to Destination
And Back …

## Slide 3: Step 1: Getting to the router
Maintain host side routing table
  Contain E2E path attributes per remote IB Subnet
  Filled manually or part of a future routing protocol
  Multiple paths may be indicated for HA or aggregation
resolve requests to remote GIDs like IP
  If GID Prefix <> local find router DGID from table
  Map router DGID to IB path (LID etc.) via SM or Cache
  Override E2E path attributes such as MTU ?
Dst GID | Tclass | IB Router | QoS | MTU
5.6.*.* | * | G 1.2.3.98 | 1 | …
5.7.*.* | * | G 1.2.3.99 | 1 | …
Sample Host Routing Table

## Slide 4: Step 2: Router next hop
Router maintains a routing table (similar to the host table), maps incoming packets to relevant egress paths

## Slide 5: Step 3: Router to Destination
Similar to step 2, except routing table resolved dynamically
  In case of a DGID lookup failure issue a local SA request and store the packet
  Or maintain a sync copy of the SA path table

## Slide 6: Step 4: Getting back
Respond to client by conducting a reverse lookup (based on SGID)
  Typically CM Rep messages or ARP responses
  Require changes in the spec and the current CM implementation

## Slide 7: HA & Multipath
Upon a router failure path need to be updated with the new router info
  Require scalable notification mechanism to hosts
  The VRRP way doesn’t work in IB since there is no MAC faking (a node cannot just take someone else's GID/MAC), need an equivalent IB mechanism
Multiple routers may be placed between subnets
  Can have VRRP like Active-Active configuration (each host “sees” a different primary router)
  Or hosts see all paths and can load-balance across (similar to the LMC approach)

## Slide 8: Partitioning & QKey
What does an IB Partition represents ?
Partition key is an L4 value representing a group of services that communicate with each other
Services can be in the same “IP” subnet or not
Someone needs to know & approve connectivity between different services (by specifying the same PKey/QKey)
IPoIB Subnet = F ( Pkey & IB Subnet)
  IB router may or may not perform IP routing as well
  IPoIB subnets may be local (use link local Mcast)

## Slide 9: Exception Handling
Exception typically communicated/detected between router and source
  MTU problems, Unreachable, router failure, ..
A mechanism need to be implemented for reporting errors to hosts
  QP1 seems to be the only option (global & unique)
  Special MADs would need to be formed
  Need to consider “multicast” or unacked MADs, can also address the router take-over issues